## Slide 1: SA/DA hiding
Date: 2021-09
Authors:

## Slide 2: Abstract
Problems: SA/DA are transmitted in the clear OTA in frame headers
  Reveals MAC addresses of wired devices in the DS, including OUI
    Doesn’t provide user tracking but does reveal information that might be considered private.
  STA-to-STA communication reveals longer-lived MAC addresses used in DS
    When combined with frame sizes, can be used to track users around the DS – even if OTA MAC addresses are changing frequently.
  Solutions need to consider legacy devices which would not include new features
    Note: A-MSDU could be used to hide SA/DA

## Slide 3: For Reference: Address fields
TA = MAC address of the AP/STA transmitting the frame
RA = MAC address of the AP/STA receiving the frame
SA = MAC address of the source device (wired or wireless) of the frame
  Can be the same as TA
DA = MAC address of the destination device (wired or wireless) receiving the frame
  Can be the same as RA

## Slide 4: Introduction
SA and/or DA does not need to be in the clear OTA
  Sending this in the clear is a historical artefact
  So far, no-one has worried because there is “lower-hang fruit” which is easier to exploit
  Once we start patching up the privacy holes with random MAC, then this might become the low hanging fruit!

## Slide 5: Concerns with MAC Addresses of Wired devices in DS
SA/DA sent in the clear OTA reveals MAC addresses of wired devices in the DS, including OUI
  OUI can reveal presence of expensive wired devices (e.g. high-end TV)
    Thieves can do a “drive-by scan” of frames and check OUI to target houses to break into.
  More detailed profiling can be applied using traffic analysis
  Doesn’t provide user tracking but does reveal information that is considered private.

## Slide 6: Recap of 11-21/1328 “Changing STA MAC addresses per association”
802.11-21/1328 includes proposing the following privacy mitigations (MLO model)
Affiliated STA MAC addresses
  Sent in the clear OTA
  Changes per association to prevent tracking OTA STA MAC Addresses between associations
Non-AP MLD MAC address
  Sent securely OTA between STA and AP
    Never transmitted in the clear
    Only STA and its AP should know mapping from random OTA and Non-AP MLD MAC addresses
  Used for addressing the STA in the DS
  May persist over a single association or multiple sequential associations.
    A multi-sequential-association Non-AP MLD MAC address would suit scenarios when two STAs are communicating, so that higher later protocols between STA A and STA B are not impacted by associations as the STAs move between APs.

## Slide 7: SA/DA and STA-to-STA communication
Assume we randomize the OTA MAC addresses of the STAs in a large enterprise network to provide privacy
If two such STAs are communicating, then from the two transmissions of a single frame, adversary infers the mapping between random OTA & non-AP MLD MAC addresses for both STA
Sending SA/DA in the clear will compromise/nullify other privacy mitigations!
DS
STA A
AP X
AP Y
STA B
STA A MAC Addresses OTA: random ab..cd
Non-AP MLD: 12..34 (hidden)
STA B MAC Addresses OTA: random ef..gh
Non-AP MLD: 56..78 (hidden)
Frame header includes TA: ab..cd
DA: 56..78
Frame header includes RA: ef..gh
SA: 12..34
Adversary observes & correlates frames using size.
Infers random OTA addr ab…cd corresponds to Non-AP MLD addr 12..34.
Infers random OTA addr ef…gh corresponds to Non-AP MLD addr 56..78.

## Slide 8: Example Solutions
SA and/or DA (when present) are sent encrypted OTA
  Example 1: use A-MSDUs
  Example 2:
    SA and/or DA are extracted from frame header inserted into the frame body prior to applying encryption and integrity protection.
      Fields containing SA and/or DA may be either removed from frame header, or set to some value (e.g., all zeroes or random values).
    After applying integrity verification and decryption, SA and/or DA are extracted from the frame body and used in further processing of the frame.
Note: SA/DA in frames used by legacy STAs will still reveal the per-association persistent MAC address (non-AP MAC Address) of source/destination STAs that use changing OTA MAC addresses (this slide). Note this is not an issue for a DS which prohibits STA-to-STA communications.

## Slide 9: Slides to add to 11-21-0641-r2 “Proposed Issues” (Use cases)

## Slide 10: Y) Tracking SA and DA OTA
Problem/Issue
SA and DA are currently sent in the clear OTA.
This reveals MAC addresses of other Devices used in the DS, which allows
  Identifying OUI of Wired Devices, and further profiling using traffic analysis
  Tracking STAs performing STA-to-STA communication, even if other tracking mitigations are applied
Status
  [Text indicating when use case was presented and any agreements on the use case.]
Reference
(This contribution)

## Slide 11: SP2
Do you agree to include this “Tracking SA and DA OTA ” issue in document “21/641 Proposed Issues”?