## Slide 1: TWT for WLAN Sensing Measurement
Date: 2021-09-15
Authors:

## Slide 2: Motivation
A broad range of wireless local area network (WLAN) sensing applications require long-term, periodic sensing measurement and reporting of measurement results.
In these applications, low power consumption is a key requirement for battery-powered WLAN sensing devices.
This contribution attempts to address the issues of periodic sensing measurement and power saving.

## Slide 3: A Brief Overview of TWT
“Target wake time (TWT) allows an AP to manage activity in the BSS in order to minimize contention between STAs and to reduce the required amount of time that a STA utilizing a power management mode needs to be awake. This is achieved by allocating STAs to operate at nonoverlapping times and/or frequencies, and concentrate the frame exchanges in predefined service periods.” (Clause 26.8 of 802.11ax-2021)
With the TWT mechanism, a STA can agree with an AP on a wake schedule, allowing it to wake up only when required.

## Slide 4: Types of TWT
Implicit TWT (TWT negotiation decides the start time of TWT and TWT wake interval) vs. explicit TWT (not supported in 11ax/be)
  Implicit TWT enables a periodic wake schedule.
Individual TWT vs. broadcast TWT
  Mandatory support by HE/EHT AP for individual TWT
  Optional support by HE/EHT non-AP STA for individual TWT
  Optional support by HE/EHT AP/non-AP STA for broadcast TWT
  Since a sensing session is pairwise (Motion 23), individual TWT fits naturally.
Trigger-enabled TWT (The AP transmits at least one trigger in each TWT service period (SP) to schedule STA’s transmissions) vs. non-trigger-enabled TWT (No trigger is transmitted in any TWT SP)
Announced TWT (The TWT requesting STA may be at the doze state at the beginning of TWT SP and the AP transmits frames to the STA after receiving a PS-Poll/APSD trigger from the STA) vs. unannounced TWT (TWT requesting STA wakes up at the beginning of TWT SP)

## Slide 5: TWT Negotiation
To initiate the negotiation, the TWT-requesting STA communicates its waking schedule information to the AP via a TWT request message.
The AP devises a schedule and delivers TWT parameter values in a response message to the STA.
  TWT: the next time at which the STA should wake up for the TWT session
  TWT wake interval: the time interval between subsequent TWT sessions for the STA
It may require more than one pair of request-response messages to conclude the agreement negotiation phase.
Once the TWT parameters are agreed, the STA can go to sleep until the next TWT SP starts.
The STA wakes up and participates in sensing measurement periodically according to the schedule.
TWT Setup/Teardown/Information frames are used to set up, tear down, and update a TWT agreement, respectively.
TWT negotiation should be included in the sensing setup phase for a sensing initiator and a sensing responder to exchange and agree on the TWT parameters associated with a sensing session.

## Slide 6: Example 1 – Non-Trigger-Enabled Individual TWT
TWT-responding/scheduling AP: sensing initiator/receiver
TWT-requesting/scheduled STA: sensing responder/transmitter
After the STA agrees with the AP on a wake schedule for a non-trigger-enabled TWT, it transitions to the doze state.
At the beginning of the first TWT SP, the STA wakes up and transmits an NDP frame to the AP.
The AP receives the NDP frame and performs sensing measurement.
The STA goes to sleep until the start of the next TWT SP.
The AP and the STA repeat the above process during each TWT SP.
doze
TWT
Request
TWT
Response
TWT wake interval
NDP
NDP
AP
STA
doze
TWT SP
TWT SP

## Slide 7: Example 2 – Trigger-Enabled Individual TWT
TWT-responding/scheduling AP: sensing initiator/receiver
TWT-requesting/scheduled STA: sensing responder/transmitter
After the STA agrees with the AP on a wake schedule for a trigger-enabled TWT, it transitions to the doze state.
At the beginning of the first TWT SP, the AP transmits a trigger frame (TF) to solicitate NDP transmissions.
The station wakes up, receives the TF, and transmits an NDP frame to the AP.
The AP receives the NDP frame and performs sensing measurement.
The STA goes to sleep until the start of the next TWT SP.
The AP and the STA repeat the above process during each TWT SP.
TWT
Request
TWT
Response
TWT wake interval
NDP
AP
STA
doze
TWT SP
TWT SP
TF
TF
NDP
doze

## Slide 8: Example 3 – TWT for NDPA Sounding
TWT-responding/scheduling AP: sensing initiator/transmitter
TWT-requesting/scheduled STA: sensing responder/receiver
After the STA agrees with the AP on a wake schedule for an individual TWT, it transitions to the doze state.
At the beginning of the first TWT SP, the AP transmits an NDPA frame followed by an NDP frame to the STA.
The STA wakes up, receives the NDPA and NDP frames, performs measurement, and feedbacks measurement result.
The STA goes to sleep until the start of the next TWT SP.
The AP and the STA repeat the above process during each TWT SP.
TWT
Request
TWT
Response
TWT wake interval
NDP
measurement feedback
AP
STA
doze
TWT SP
TWT SP
NDPA
NDPA
NDP
measurement feedback
doze

## Slide 9: Summary
A high-level introduction to TWT-based WLAN sensing measurement has been presented.
Using TWT, each sensing STA negotiates awake periods with the sensing AP to transmit and receive packets for sensing measurement and reporting, saving energy the rest of the time as the STA remains in the doze state.
  Enables scheduling of periodic wake time for sensing measurement
  Leads to low energy consumption for the participating sensing STAs
  Provides flexibility in how the transmission period can be used for exchange of sensing information, as it allows both uplink and downlink sensing traffic and does not limit transmissions only to those poll-based
Since the HE/EHT TWT mechanism is defined primarily for communications, in-depth details need to be addressed in the sensing context.

## Slide 10: SP
Do you agree with the following?
  11bf shall define a sensing measurement procedure based on the Target Wake Time (TWT) mechanism specified in 11ax/be.