## Slide 1: Some Observations on Optimizing 802.11be Release 1 with respect to Enterprise AP Use Cases
Date: 2021-09-20
Authors:

## Slide 2: Abstract / Executive Summary
Situation
IEEE 802.11be has an unapproved draft and is partway through pre-LB comment collection
Problem
The R1 features as currently defined can be better optimized for enterprise use cases
Comment resolvers may not be fully aware of how enterprise Wi-Fi operates, and then are not accounting for these important use cases
Next steps
Provide broader education on how enterprise Wi-Fi operates (here)
Raise the visibility of these issues with the wider WG community and invite them to share their expertise in TGbe
Overarching goal is to show how to optimize 802.11be for enterprise use cases

## Slide 3: Example Enterprise Use Cases
A call center with many densely-packed workers each with a wireless headset
A sporting/cultural event where audience members use their smartphone cameras to share the live experience with remote friends and family and/or take photos which are sync-ed to the cloud, and there might be multiple venue-provided streams of video or audio (instant replays, multilingual translations, etc) and/or a connected referee or announcers; ticket scanners & point-of-sale
A lecture theater with hundreds of laptops using various educational webtools and performing auxiliary Internet tasks (web research, email syncing, app downloading, etc) including information from the lecturer’s laptop
A hospital with a large number of 802.11-connected medical devices supporting vital patient care and also provides guest access so patients can chat / email / call / video call their friends and family
Dense office deployment with a mix of offices, cubes, meeting rooms and open space for informal meetings. Employees and their guests are transferring large files, conducting high-quality video teleconferences

## Slide 4: Technical Requirements for Enterprise Use Cases
Devices operate across 2.4, 5 and/or 6 GHz
Devices will be a mix of legacy and 802.11be
The offered load varies over time
There are many types of devices, but the same (converged) 802.11be network infrastructure provides connectivity for them all
Some critical devices and flows must be afforded strict priority, while otherwise attempting to maximize the wireless experience of all devices even when the environment is highly congested
Network coverage most often designed for dense deployment and capacity

## Slide 5: Current Techniques to Meet Technical Requirements of Enterprise Use Cases
Techniques to achieve these goals that are field-proven to be necessary and effective are:
  Proactively load balancing client devices to lightly loaded links
  Link management where one “safehaven” link is available to critical traffic and relatively protected from other traffic
  Dense deployments require higher frequency reuse (where 320 MHz is less useful, 20/40 MHz used in 2.4/5 GHz, 80 MHz also planned in 6 GHz)

## Slide 6: Link management
Link management might use separate SSIDs for critical devices and for guests that operate on a different links so that greater determinism is available to the critical devices. However, this static link separation is not optimized, e.g.:
  certain devices may not support the link that their SSID is operating on, and
  spectral efficiency is unnecessarily low (e.g., if the guest SSID is limited to a 2.4 GHz link, then guests cannot take advantage of a 5 GHz link even when the load on that link is low, which can result in an inferior wireless experience for the guests)
Therefore, some existing deployments might overlap the SSIDs in some or all links (or even use a common SSID for all devices, with VLAN separation)
To ensure the critical devices are still prioritized, such deployments use load balancing algorithms to maintain a sufficiently low load on the safehaven link for the critical devices by restricting the number of guest devices operating there
  This may complement other QoS features for prioritization between traffic that shares the same channel/band

## Slide 7: Load Balancing
The load balancing algorithms:
steer the devices between links preferably using the 802.11v BTM mechanisms for better QoE, or else
use the more disruptive legacy steering mechanisms
  e.g., deauthentication, association rejection, probe suppression
That said, load balancing algorithms are out of scope of the 802.11 standard

## Slide 8: Multi Link Operation – Current Situation
By default, client is connected on all links
  Negotiation is allowed but reverts to this if negotiation fails
Client can also go into power save on N-1 links and pick its preferred link
The AP, with full visibility and a desire to optimize all clients’ experience, is not yet equipped with the most efficient tools to robustly optimize the wireless experience
  AP can still use more disruptive legacy mechanisms (e.g. disassoc), unequal allocation of SSIDs to link, and/or create a safehaven link for critical traffic, etc.
By default, all TIDs are mapped to all links
  Negotiation is allowed but reverts to this if negotiation fails
  Individual negotiations consume medium time and thus are not well optimized for high density deployments
  Diminishes the AP’s current ability to manage the QoE
AP link add/delete is not yet present (although the feature discussions are underway, they have not been motioned yet)
  Current AP Link Add does not actually let clients use the link without a reassociation!
  Temporary link disablement (for CAC) is not yet present

## Slide 9: MLO - Goals
Network infrastructure can use MLO and still perform load balancing, and even in a more seamless way
Network infrastructure can enhance the throughput and latency of critical devices’ traffic by enabling more links than just the safehaven link when and while these extra links are not over-burdened
Network infrastructure can enhance the throughput and latency of many guests’ QoS flows by enabling the QoS TIDs of guests on the safehaven link when and while that safehaven link is lightly loaded
True AP Link Add – AP advertises a new link in its MLD and clients can add the link to their MLD without a reassociation
Complete the Temporary link disablement feature to enable AP functions like off-channel scanning (e.g., for CAC for DFS spectrum)
No load balancing
Unnecessary congestion in some bands
Load balancing via probe suppr, assoc rej, deauth
Reduced congestion, when stable
Load balancing via 11v BTM
Reduced congestion with roaming-like experience
Load balancing via optimized MLO
Reduced congestion even in dynamic congestion with seamless connectivity

## Slide 10: Restricted TWT
The Restricted TWT feature enables normal contention-based access for much of the time while also reserving time for flows with high QoS requirements
Such a feature is most useful if all STAs in a BSS, even STAs that do not have flows with high QoS requirements, respect such Restricted TWT periods
If Restricted TWT periods are not respected by all STAs on a link, then the ability of this feature to meet enterprise KPIs is markedly lower
Accordingly, we recommend that respect of Restricted TWT periods should be mandatory, for all 11be STAs in the BSS
For many enterprise use cases, it is sufficient for the respect of Restricted TWT periods to be per-BSS since OBSS can be sufficiently managed within an ESS

## Slide 11: Concluding Remarks
We encourage members to consider the range of enterprise use cases and how to better optimize 802.11be for them
  E.g. involvement in TGbe comment resolution, and upcoming WG LB
Enterprise includes where we all work, eat, and play:
  Healthcare
  Education
  Stadia / entertainment venues
  Manufacturing
  Hospitality (hotels, etc)
  Travel & hubs (airports, train stations, planes, trains, buses, etc)
  Retail
  Carpeted enterprise
  And many more

## Slide 12: Backup

## Slide 13: MCS12 and MCS13 (4KQAM)
The dynamic range of MCS12/13 is very small
  In 802.11be D1.0, the required sensitivity of MCS13 at [80 160 320] MHz is [-40 -37 -34] dBm but the maximum input level at 6 GHz is -30 dBm, which provides only [10 7 4] dB of guaranteed dynamic range
In comparison, 802.11ax requires a minimum of 13 dB dynamic range for MCS11 at 160 MHz
As historical context, a maximum input level of -30 dBm for OFDM in 5 GHz was introduced by the 802.11a-1999 amendment. In 802.11g-2003, the maximum input level was defined as -20 dBm for OFDM in 2.4 GHz. These levels have carried forward unchanged in the 802.11n/ac/ax amendments and in the 802.11be draft for a period of 18-22 years
At a minimum, we propose to match the maximum input level in 5/6 GHz to that of 2.4 GHz, for a 10 dB increase in dynamic range
The utility of 4KQAM would be markedly better for all verticals by increasing its specified dynamic range