## Slide 1: Opportunistic Sensing Measurements
Date: 2021-10-12
Authors:

## Slide 2: Abstract
Opportunistic sensing is the use of any frame from a Sensing Transmitter to a Sensing Receiver to make a sensing measurement. The frames do not need to be triggered and need not be NDPs.
This Contribution explores the use of opportunistic sensing measurements.
It discusses how measurement flow can potentially provide a basis for a non-Trigger-based procedure.

## Slide 3: Background
Non NDP based measurement leverages the LTF in a PPDU’s preamble from any transmission
Potential benefit to leverage existing transmissions for sensing allows for reduced overhead
Pure Opportunistic Sensing can occur today using existing 802.11 standards, however no coordination or signalling exists
Discussion around can TGbf amendment improve operation?

## Slide 4: STA as UL Sensing Transmitter
Sensing Receiver
Sensing Transmitters
AP
STA1
How to signal measurement is intended for sensing?
A participating STA may transmit a PPDU containing a “Sensing Frame” payload.
  New Frame or Existing Frame?
  Provides relevant information to fit into WLAN SENS Procedure [3].
  Contents: TBD
Sensing transmissions from STA to AP do not require solicitation. The STA may simply produce a PPDU transmission.
Assumed AP is always awake and listening
The Sensing Receiver then performs a sensing measurement on LTF.
  Any STA can participate by transmitting.
STA2

## Slide 5: STA as UL Sensing Transmitter
The periodic sensing transmissions may be configured by the Sensing Initiator (in this example, the AP) but no elicitation is required.
  Once configured, periodic sensing transmissions may be managed by the STA.
Timing of Sensing Frames are managed by the STA (either within or outside of the MAC).

## Slide 6: STA as DL Sensing Receiver
Ongoing transmissions from AP to STA can also be used for opportunistic sensing.
STA receiving the WLAN PPDUs (non-NDP) may perform sensing based on PHY preamble.
  Any STA receiving the PPDU can perform WLAN sensing.
PPDU can be, for example, Beacons, Data frames, etc.
Sensing Receivers
STA1
STA2
AP
Sensing Transmitter
AP
STA1
STA2
Measurement
Measurement

## Slide 7: Standard Support
For the UL Transmitter case, management of periodic transmissions can be managed without additional Standard Support
However, can better fit into WLAN Sensing (SENS) Procedure by having ability for Sensing Transmitter to signal which transmissions are intended for Sensing
  Standard support can define signalling which can be used to indicate the PPDUs intended use for Sensing (e.g., Measurement Setup ID, Measurement Instance ID, etc).
Ability to fit into reporting flow for ensuring Sensing Initiator receives measurements

## Slide 8: Summary
Sensing measurements can be performed using non-NDP transmissions
Allows any PPDU transmission to be used for Sensing
A STA can act as a UL Transmitter, or DL Receiver
Potential items which TGbf can address to better utilize opportunistic sensing as a Measurement Instance have been presented.

## Slide 9: References
[1] 11-21-1047-01-00bf-legacy-support-in-11bf
[2] 11-21-0753-01-00bf-sub-7-phy-long-training-field-selection
[3] 11-21-0504-03-00bf-specification-framework-for-tgbf

## Slide 10: SP1
Do you agree that:
Opportunistic Sensing can be used as a measurement instance in the WLAN Sensing (SENS) Procedure?
Y/N/A