## Slide 1: Discussion on one-to-one sensing measurement instance
Date: 2021-09-29
Authors:
Chaoming Luo (OPPO)
Name | Affiliation | Address | Phone | Email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Pei Zhou |  |  |  | 
Lei Huang |  |  |  | 

## Slide 2: Introduction
The group has discussed to support an NDPA/NDP-based measurement procedure. [1]
A non-TB sensing measurement procedure for non-AP STA Initiator was introduced. [2]
This contribution discusses more about the procedure of one-to-one sensing scenario (only two sensing participant STAs), especially clarifies for AP Initiator case.

## Slide 3: Background: Unidirectional Sounding
Only consider (AP, non-AP STA) case, do not consider P2P case.
Unidirectional: in a single measurement instance, there are only two participants (AP and non-AP STA) , and one is Transmiter, the other is Receiver.
Case U1: if non-AP STA is Initiator & Transmitter, then non-AP STA obtains TXOP, we assume to use non-TB procedure. (scenario 2 of 21/1433r0)
Case U2: if non-AP STA is Initiator & Receiver, then non-AP STA obtains TXOP, we assume to use non-TB procedure. (scenario 3 of 21/1433r0)
U1 (non-TB)
U2 (non-TB)
TBD, we may have this “dummy” NDP
TBD, we may have this “dummy” NDP

## Slide 4: Background: Unidirectional Sounding
Only consider (AP, non-AP STA) case, do not consider P2P case.
Unidirectional: in a single measurement instance, there are only two participants (AP and non-AP STA) , and one is Transmiter, the other is Receiver.
Case U3: if AP is Initiator & Transmitter, then AP obtains TXOP, we assume to use TB procedure.
Case U4: if AP is Initiator & Receiver, then AP obtains TXOP, we assume to use TB procedure.
U3 (TB)
U4 (TB)

## Slide 5: Background: Bidirectional Sounding
Only consider (AP, non-AP STA) case, do not consider P2P case.
Bidirectional: in a single measurement instance, there are only two participants (AP and non-AP STA) and are both Transmiter and Receiver.
Case B1: if AP is Initiator, then AP obtains TXOP, we assume to use TB procedure.
Case B2: if non-AP STA is Initiator, then non-AP STA obtains TXOP, we assume to use non-TB procedure. . (scenario 1 of 21/1433r0)
B1 (TB)
B2 (non-TB)

## Slide 6: Discussion: TB or non-TB
Why non-TB procedure is not good if the Initiator is an AP?
  The non-AP Responder may “not available” to participate in a sensing measurement instance, where “not available” could indicate any of the following cases:
    The Responder (e.g, a AR/VR glass) may have pretty much low latency UL data buffered.
    The Responder (e.g., a laptop) may be in low battery state.
  It’s true that there are cases a non-AP Responder may always “available” (e.g., a freezer which is cable-powered and has little DL/UL data transmission), but there may not be so beneficial to have two different procedures for the same AP Initiator.
Considering a simple and unified procedure, it’s better that AP does not initiate non-TB measurement instance.

## Slide 7: SP 1
Do you agree to add the following into 11bf SFD ?
  The measurement instance shall be initiated by an AP as a TB measurement instance if the AP is the Initiator.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 8: Reference
[1] 11-21-1015-02-00bf-non-tb-and-tb-measurement-procedure-for-wlan-sensing
[2] 11-21-1433-00-00bf-non-tb-sensing-measurement
[3] 11-21-1445-01-00bf-requirements-for-sensing-transmitters
Chaoming Luo (OPPO)