## Slide 1: Privacy Protection Issues
Date: 2021-10-04
Authors:
Name | Affiliations | Address | Phone | Email
Thomas Derham | Broadcom |  |  | thomas.derham@broadcom.com
Nehru Bhandaru |  |  |  | 
Jarkko Kneckt | Apple |  |  | jkneckt@apple.com
Daniel Borges |  |  |  | 
Sid Thakur |  |  |  | 
Tianyu Wu |  |  |  | 
Charles Dominguez |  |  |  | 
Elliot Briggs |  |  |  | 
SK Yong |  |  |  | 
Yong Liu |  |  |  | 
Debashis Dash |  |  |  | 

## Slide 2: x+1) Protecting authentication identifiers and key identifiers
Issue
Frames sent prior to PTK establishment contain unprotected long-term key identifiers (e.g. PMKID) and/or user authentication identifiers (e.g. in EAP exchanges), which can enable tracking and/or identification of a user
Status of issue
  Discussed in TGbi 9/15/2021
Document references
  11-21-1396r1
Note: It is assumed that protection of SAE Password Identifiers, and of other device identifiers such as MAC addresses, is covered by other issues already incorporated in 0641r3

## Slide 3: x+2) Soft/mobile AP privacy
Issue
Soft/mobile APs are commonly implemented on mobile devices
Soft/mobile APs transmit persistent identifiers that can be used to track the user
  APs send unprotected broadcast frames, e.g. Beacon, Probe Response
    SSID field contains explicit PII (or, at least, a static identifier over the BSS’s lifetime)
    Elements in these frames can be used for fingerprinting
  BSSID (in MAC headers) and BSS Color (in PHY preambles) of all frames are long-term static in the Soft AP’s BSS
Status of issue
  Discussed in TGbi 9/15/2021
Document references
  11-21-1396r1

## Slide 4: x+3) Client MAC addresses during ESS association
Issue
Mobile clients remain connected to an ESS for long durations
Current standard requires the STA MAC to remain constant while associated with the ESS, which can be used for device tracking
  Standard also requires the same STA MAC to be reused if a cached PMK is used, even when reconnecting after previously disconnecting from the ESS
  Note – continuity of sequence numbers and scrambler seed can also be used to track device while the STA MAC remains constant
Requiring the STA to disconnect+reconnect just to rotate its MAC is deleterious to user experience (connectivity outage), creates unnecessary network overhead (e.g. accounting) and over-the-air overhead (e.g. need to repeat FT initial assoc)
Status of issue
  Discussed in TGbi 9/15/2021
Document references
  11-21-1396r1
Note: This issue relates to various use cases, including the “Smart Home Environment” use case in 0641r3

## Slide 5: x+4) Protecting behavioral fingerprinting while associated
Issue
Different client device implementations have identifiable characteristics during association, e.g. how often and under what conditions they:
  enter power save
  change operational mode (e.g. bw, nss)
  use recovery / resync mechanisms (e.g. BAR)
These characteristics are externally visible in unprotected signaling, and hence can be used to fingerprint and track the device, e.g.
  non-robust action frames (OMN, OPS, Quiet Time Period, ...)
  control frames (e.g. BAR)
  MAC headers (e.g. PM bit in frame control field)
Status of issue
  Discussed in TGbi 9/15/2021
Document references
  11-21-1396r1

## Slide 6: x+5) PHY/RF related privacy
Issue
CSI is signaled in unprotected action frames (Beamforming reports) and might be used to facilitate inference of user behavior
  e.g. when CSI is high quality, channel perturbations caused by keystrokes might be detected
Some PHY/RF characteristics of a transmitting device can be identifiable and used to track a device
  e.g. CFO, spectral characteristics
  in general these PHY/RF characteristics may not need to be addressed in the standard
Status of issue
  Discussed in TGbi 9/15/2021
Document references
  11-21-1396r1

## Slide 7: 2bis) [edits] Avoid Element Fingerprint
Issue
Elements carried in an unprotected management frame are sent in clear to provide capabilities, operation parameters, or vendor specific indication, etc.
  Additional elements containing information with high specificity, e.g. for link enablement, will also be sent per draft amendments under development, e.g. 11be
A large number of elements carried in an unprotected management frame may provide sufficient entropy as a fingerprint of a device/user
Need to provide privacy and avoid element fingerprint
  Note in some case the frame length can imply the contents, even when encrypted/masked
Status of issue
Issue presented at IEEE 802.11bi session on 05/14/2021
Document references
Why MAC Address Randomization is not Enough: An Analysis of Wi-Fi Network Discovery Mechanisms
11-21-0839r0, 11-19-0489r0, 11-20-940r0, 11-20-746r1, 11-21-1396r1

## Slide 8: Straw polls
SP1) Do you agree adding “x+1) Protecting authentication identifiers and key identifiers” issue into TGbi proposed issues document (DCN 21-641)?
Y: N: A:
SP2) Do you agree adding “x+2) Soft/mobile AP privacy” issue into TGbi proposed issues document (DCN 21-641)?
Y: N: A:
SP3) Do you agree adding “x+3) Client MAC addresses during ESS association” issue into TGbi proposed issues document (DCN 21-641)?
Y: N: A:
SP4) Do you agree adding “x+4) Protecting behavioral fingerprinting while associated” issue into TGbi proposed issues document (DCN 21-641)?
Y: N: A:
SP5) Do you agree adding “x+5) PHY/RF related privacy” issue into TGbi proposed issues document (DCN 21-641)?
Y: N: A:
SP6) Do you agree updating the “Avoid Element Fingerprint” issue in TGbi proposed issues document (DCN 21-641) per “2bis”?
Y: N: A: