## Slide 1: Primary and Secondary User in R-TWT
Date: 2021-10-08
Authors:
Name | Affiliations | Address | Phone | email
Thomas Handte | Sony Group Corporation |  |  | Thomas.Handte (at) sony.com
Dana Ciochina |  |  |  | Dana.Ciochina (at) sony.com
Daniel Verenzuela |  |  |  | Daniel.Verenzuela (at) sony.com
Yusuke Tanaka |  |  |  | Yusuke.YT.Tanaka (at) sony.com

## Slide 2: Introduction
Low latency service is an important application scenario for 11be
  TGbe introduced R-TWT as a protected period for STAs to deliver low-latency data [1, 2]
  Within a R-TWT service period (SP)
    the AP may select the STAs that are eligible to transmit
    the start time is often guaranteed
    Interference of legacy STAs may be reduced by use of overlapping quiet element
While R-TWT framework is good for low latency traffic, the impact to non-low latency traffic should be considered too
  Even with R-TWT in place, by the nature of operation in unlicensed bands, there is some variance of end-to-end transmission delay caused by
    Channel access delay
    Transmit time (e.g. by MCS change)
    Retransmission time (e.g. retransmission of PPDUs or fraction of it)
  Therefore, a R-TWT would often be designed with a margin to cover exceptional cases
    The margin covers delays that exceed the “typical“ transmission delay
However, R-TWT SPs designed with a margin are harmful to BSS throughput, because the margin may often be non-used

## Slide 3: Related submissions and CIDs
Some related submissions [3, 4, 5] address similar aspect
  Transmit latency sensitive data first among any other traffic
  Indication sent by STAs that they are ready for SP termination
  Terminate R-TWT SP when there is no more LL-traffic [4, 5]
  Automatically terminate an SP when channel is idle [5]
  AP to perform prioritization by trigger frame in trigger enabled TWT SP [3]
CIDs 5875, 6866, and 7471 [6] address the issue of under utilization of R-TWT SP

## Slide 4: Issue
R-TWT SP duration is designed with some margin
  Target: Successful data delivery is achieved in most cases within R-TWT SP duration
    Nominal TXOP and contention duration is baseline
      E.g. based on avg. MCS, MSDU size, contention delay, …
    A reasonable margin is added to the baseline duration depending on statistics
      E.g. based on 90%-ile of contention delay, retransmission probability, max. TXTIME, …
The margin may be often unused
  The higher the margin, the more R-TWT SP duration is mostly unused

## Slide 5: Proposal – Concept
In R-TWT setup
  A primary and secondary user set are defined
    Classification into the two sets may be TID specific
  Any other STA should not access the R-TWT SP
A primary user
  can contend for channel access right after the R-TWT SP begins
  shall indicate to secondary users that it finished data transfer
    e.g. empty queue for specified TID
  shall not transmit once it issued the indication to secondary users
    Unless it is a secondary user too
A secondary user
  can contend for channel access after having received a release indication

## Slide 6: Proposal – Details
Design of the R-TWT SP release indication
  A 2-step approach is preferable in which the AP releases the R-TWT SP
  Primary user STA1 indicates to AP that it finished its data transfer
    The indication (indA) may reside in a subfield (TBD)
      E.g. queue size = 0 in QoS Control subfield or a reserved bit in CAS Control subfield
  AP collects STAs’ indication and transmits a release indication (indB) once all primary user STAs successfully finished their data transfer
    The indication may be conditional to BAck/Ack response status
      i.e. indB is only included if BAck indicates success
    The release indication (indB) may reside in BAck frame (e.g. BA Control field) or in a separate frame (TBD)

## Slide 7: Example
R-TWT setup
  Primary user: STA1 (TID 6), STA2 (TID 4)
    Both STAs may transfer low-latency data under these TIDs
  Secondary user: STA3 (any TID)
    A secondary user STA may rarely obtain a TXOP
      Therefore, the traffic of a secondary user should not be of type low-latency but rather best effort
Operation
  Each STA indicates with “queue size=0” of QoS data frame for the respective TID that no more data is pending for transmission
    If BAck is success, the AP considers the R-TWT SP as released from the particular STA
    If BAck indicates an error, the AP considers the R-TWT SP as not released from the particular STA
  Once all primary user STAs indicated that their queue size is zero, the AP releases to SP to secondary users
    The BAck comprising the SP release may be a multi-STA BAck

## Slide 8: Special Role of AP
The AP is neither a primary nor secondary user
  It shall collect indications by primary user STAs and release the R-TWT SP
  It may use EDCA at any time under the following guidelines
    Any PPDU should only be transmitted to STAs that are either primary or secondary user
    Downlink BUs for secondary user STAs should only be transmitted once the R-TWT SP is released
    Trigger frames that trigger secondary user STAs should only be transmitted when the R-TWT SP has been released
  We believe that guidelines are more appropriate than strict rules, because the AP has all knowledge that it needs for not harming any uplink traffic from a primary user of its BSS
    The AP should have the flexibility to allocate unused resources to secondary user STAs although the R-TWT SP has not been released

## Slide 9: Benefits
The proposed mechanism allows R-TWT to be flexibly and fairly used
  1st priority is successful transmission of high priority (low latency) traffic
  2nd priority is to utilize remaining duration of R-TWT SP
The secondary user set identifies which STAs are eligible to transmit after a release indication and provides the following benefits over SP termination
  Enhanced contention control
    After a release indication, the set of STAs that can access the channel is limited to the secondary users
      In contrast to SP termination, the number of STAs contending for channel access after the release indication can be controlled
  Enhanced protection of upcoming R-TWT SPs
    After a SP termination, a non-R-TWT-compliant STAs (e.g. HE STA) may obtain TXOPs
      Those TXOPs may extend beyond start of next R-TWT SP
  Enhanced power save
    STAs that don’t belong to primary or secondary user group may be in doze state during the SP
      No need to listen for TWT SP termination

## Slide 10: Application to time sensitive networking (TSN)
Frame Preemption as defined in 802.3br and 802.1Qbu [7]
  “Express frames suspend the transmission of preemptable frames”
    Source or destination of express frames define primary user STAs of a R-TWT SP
    Source or destination of preemptable frame define secondary user STAs of a R-TWT SP
Example: BSS with 3 STAs
    STA1 and STA2 schedule periodically express frames (e.g. low latency traffic) to be delivered to AP
    AP, STA1, STA2, STA 3 have preemptable frames (e.g. best effort traffic) queued, too
    Two persistent R-TWT SPs (#1 and #2)

## Slide 11: Conclusion
R-TWT SP may be often underused
  A significant margin needs to be added to the nominal duration due to the nature of unlicensed bands
Proposal
  R-TWT SP setup defines primary and secondary users
    Primary users may transmit first
      Once a primary user finished data transfer, it transmits an indication to AP
    AP collects all indications and transmits a release indication to all secondary users
    A secondary user may transmit after having received a release indication by the AP
Benefits
  The R-TWT SP is flexibly and fairly used
  The secondary user group clearly defines STAs which can expect to receive a release indication
    Beneficial for contention control, R-TWT protection, and power safe

## Slide 12: SP #1
Do you agree that:
  TGbe defines a mechanism which allows the remaining time of an R-TWT SP to be used by other STAs once all intended STAs finished their frame exchanges
    An intended STA is a non-AP STA that may use the R-TWT SP starting from its beginning

## Slide 13: SP #2
Do you agree that:
  In setup of an R-TWT SP differentiates two user groups
    A primary user may use the R-TWT SP starting from its beginning
    A secondary user may use the R-TWT SP once it received a release indication

## Slide 14: SP #3
Do you agree that:
  Within an R-TWT SP that differentiates primary and secondary user groups
    A primary user STA shall indicate to an AP that it finished its data transfer
    An AP shall collect all indications from primary users and transmit a release indication to secondary users once all indications have been received

## Slide 15: References
[1] 11-20/1046r12 Protected TWT Enhancement for Latency Sensitive Traffic
[2] Draft P802.11be D1.2
[3] 11-21/1020r0 Handling Fairness Issue in Restricted TWT
[4] 11-21/1115r0 CC36-CR-35.6 Traffic Prioritization During Restricted TWT SPs
[5] 11-21/1358r0 Restricted TWT Termination
[6] 11-21/1018r14 IEEE 802.11be CC36 comments
[7] 11-18/2027r0 Overview of IEEE 802.1 TSN and IETF DetNet