## Slide 1
Error Recovery in Triggered TXOP Sharing
Date: 2021-10-29
Authors:

## Slide 2: Introduction
Triggered TXOP sharing procedure is defined in the Draft 1.2 [1].
  The Triggered TXOP sharing procedure allows an AP to allocate a portion of the time within an obtained TXOP to only an associated non-AP EHT STA for transmitting one or more non-TB PPDUs.
AP’s procedure during or after TXOP sharing is defined but a STA’s procedure using a shared TXOP is not fully defined.
In this contribution, STA’s error recovery is discussed.

## Slide 3: Recap: Triggered TXOP sharing
The AP (the TXOP holder) can early terminate the shared P2P TXOP if the CS mechanism indicates that the medium is idle at the TxPIFS slot boundary.
It is not fully discussed in the Draft 1.2 that how STA2 should utilize the shared TXOP.
  Which is the TXOP holder during the shared TXOP duration ?

## Slide 4: Transmission error handling in the shared TXOP
When there is a transmission error during the shared TXOP, error recovery procedure shall be defined.
  Since the AP is the TXOP holder, STA2 is not able to retransmit the DATA.

## Slide 5: Error recovery during the shared TXOP (1)
If STA2 is able to successfully transmit DATA to STA3, STA2 can be the TXOP holder of the shared TXOP.
STA2 can perform PIFS recovery after a successful initial PPDU transmission during the shared TXOP.

## Slide 6: Error recovery during the shared TXOP (2)
Since the portion of TXOP is shared with STA2, the shared TXOP is assumed to be already established and STA2 is assumed to be the TXOP holder of the shared TXOP.
STA2 can perform PIFS recovery during the shared TXOP.

## Slide 7: Error recovery during the shared TXOP (3)
If the TXOP holder of the shared TXOP is still AP, AP can assist STA2 for error recovery.

## Slide 8: Conclusion
How to recover an error during the shared TXOP is not defined for triggered TXOP sharing in the Draft 1.2.
Which is the TXOP holder of the shared TXOP should be decided.
  STA can be the TXOP holder of the shared TXOP
    After a successful initial transmission in the shared TXOP
    After the allocation of the shared TXOP
  AP is the TXOP holder of the shared TXOP
In this presentation, possible error recovery procedures during the shared TXOP are discussed.
  STA controlled error recovery
  AP assisted error recovery

## Slide 9: Reference
[1] Draft P802.11be D1.2