## Slide 1
TID-to-Link mapping in eMLSR
Date: 2021-11-20
Authors:

## Slide 2: Introduction
eMLSR STA MLD can communicate with AP MLD using the links negotiated with EML OMN
Depending on the TID-to-Link mapping, there might be a case where AP MLD can not transmit DATA with a certain TID using the negotiated link
  Since TID-to-Link mapping is a separate procedure, TID can be mapped to a link which is not negotiated with EML OMN
TID-to-Link mapping considering EML OMN and eMLSR link management are discussed

## Slide 3: Recap: eMLSR EML OMN
Links to use for eMLSR can be negotiated with EML OMN
Since TID-to-Link mapping is a separate procedure, a certain TID can be mapped to a link not used for eMLSR

## Slide 4: eMLSR TID-to-Link mapping
Option 1) EML OMN may include TID-to-Link mapping element
  During EML OMN negotiation, TID-to-Link remapping can be negotiated.
Option 2) TID-to-Link mapping for eMLSR can be default mapping
  In order to avoid eMLSR link to TID mismatch, TID-to-Link mapping can be automatically switched to default mapping (all TID to all link mapping) after EML OMN negotiation
Option 3) Depending on the TID of DATA, AP may initiate OMN procedure (AP initiated OMN)

## Slide 5: eMLSR TID-to-Link mapping (Option 1)
EML OMN may include TID-to-Link mapping element

## Slide 6: eMLSR TID-to-Link mapping (Option 2)
TID-to-Link mapping for eMLSR can be default mapping

## Slide 7: eMLSR TID-to-Link mapping (Option 3)
Depending on the TID of DATA, AP may initiate OMN procedure (AP initiated OMN)

## Slide 8: Conclusion
eMLSR links can be negotiated with EML OMN.
Since TID-to-Link mapping is a separate procedure, mismatch on eMLSR link with TID-to-Link mapping can happen.
During EML OMN negotiation, TID-to-Link remapping can be performed.
  Default TID-to-Link mapping
  TID-to-Link mapping element in EML OMN
Depending on the TID of the BU and TID-to-Link mapping, AP may initiate EML OMN procedure.
In this presentation, considerations on TID-to-Link mapping in eMLSR were discussed.

## Slide 9: Reference
[1] Draft P802.11be D1.2