## Slide 1: Consideration for NDPA in 11BF
Date: 2021-11-15
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Sang Kim |  |  |  | sanggook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Nov. 2021

## Slide 2: Introduction
As in following motion 26c, we have agreed that NDPA sounding is used for sensing measurement.
  The NDPA sounding procedure defined in 11bf consists of:
    A transmission of an NDP Announcement frame
    A transmission of an NDP SIFS after transmitting the NDP Announcement frame
    Note: The detailed definition of the NDP Announcement frame is TBD.
    Note : This may be applied to pre-HE STAs (i.e. not limited to HE and/or EHT STAs)
However, regarding the NDPA frame, there has been no decision on how to design this frame for WLAN sensing.
In this contribution, we consider the design of the NDPA frame for WLAN sensing.

## Slide 3: NDPA frame variants(1/3)
In 802.11, four NDPA frame variants have been defined:
  VHT NDPA
  HE NDPA
  Ranging NDPA
  EHT NDPA
The frame format of Ranging NDPA and EHT NDPA is same as a HE NDPA frame .
  The STA info field included in those NDPA variant consists of 4 Byte bits.

## Slide 4: NDPA frame variants(2/3)
These four variants are distinguished by setting of the NDP Announcement Variant in the Sounding Dialog Token field.
All values for indicating the NDPA variants are already exhausted.

## Slide 5: NDPA frame variants(3/3)
In each NDPA variants, STA info subfield is configured as following.
  To avoid the wrong detection of AID by VHT STA, the Disambiguation field is included in HE/Ranging/EHT NDPA commonly.
VHT
Ranging
HE
EHT

## Slide 6: Considerations
As shown in the previous slides, the independent NDPA frame was defined according to the 802.11 protocols.
  Currently, four NDPA frame variant were defined in 11spec.
Since the use of the NDPA frame is very self-explanatory, it is necessary to consider how to define the NDPA frame used only for sensing for the efficient sensing measurement.
With respect to NDPA for sensing, we can consider the following two approaches for NDPA frame design.
  Approach 1: Reuse the defined NDPA frame variant
  Approach 2: Define the sensing NDPA frame variant

## Slide 7: Approach 1: Reuse the defined NDPA frame variant
It is a straightforward method and all defined NDPA frames can be used in sensing.
  The use of which variant for NDPA frame can be determined according to the capability of STA which participates in sensing.
    The variant of the NDPA frame can be limited by participating STA’s capability.
    For example,
      If the STAs that participate in the sensing are HE STAs, the HE NDPA frame is used for sensing.
  To support the sensing protocol defined newly, a part of the content in the NDPA frame can be newly configured.
    So, even though the existing NDPA variant is used for sensing, it is needed to be an indication that this NDPA is used for sensing.

## Slide 8: Approach 2: Define the sensing NDPA frame variant
For supporting the sounding efficiently according to 802.11 protocols, an independent NDPA frame variant was defined separately.
So, we can consider the defining of the sensing NDPA frame variant for specific sensing measurement.
  We can freely configure the NDPA frame for sensing to support the new features or apply the new parameters.
The sensing NDPA frame variant can be designed with a new format or reusing of existing frame formats.
  The identification of the sensing NDPA frame variant should be considered to distinguish it from the existing variant of the NDPA frame.

## Slide 9: The sensing NDPA indication
In both approaches, we can recognize that the indication of the NDPA for sensing is needed to support the new features and/or the specific measurement in 11bf.
  As shown in slide 4, there is no room anymore to indicate additional variants in the NDP Announcement variant subfield.
So, for the indication of the NDPA for sensing, we can consider the following options.
  Option 1: use of the one bit of sounding dialog token number field
  Option 2: use of the Subtype subfield in the frame control field.
  Option 3: use of Special STA info field

## Slide 10: The sensing NDPA indication - Opt.1
One bit in the sounding dialog token number field can be allocated additionally for indication of the sensing NDPA.
  It is simple and similar to the conventional indication of signaling of NDPA variants.
  One of bit in the sounding dialog token field can be used, e.g. B7
    In the sensing NDPA, the setting of B7 is always 1. and otherwise, it is used to indicate the sounding dialog token number.
The configuration of the sounding dialog token field for indication of the sensing NDPA
 | B0 B1 | B2 B6 | B7
 | NDP Announcement variant | Sounding Dialog Token Number | Sensing
Bits: | 2 | 5 | 1

## Slide 11: The sensing NDPA indication - Opt.1
As the sensing NDPA is indicated with one bit(e.g., B7) of sounding dialog token field, we can consider the following setting of NDP Announcement variant field.
  Case 1: fixed setting as a specific value.
    For example,
      The NDP Announcement variant field is set to 01 (i.e. Ranging NDPA variant)
      The sensing field (i.e., B7) is set to 1.
  Case 2 : set as with the existing way.
    NDP Announcement variant field is set to a value according to the NDPA frame format.(i.e., VHT/HE/Ranging/EHT)
    It is possible to reuse the defined NDPA frame according to 802.11 protocol.

## Slide 12: The sensing NDPA indication - Opt.2
There are some reserved values for subtype field in frame control subfield. And, by using one of these reserved values, we can simply indicate the sensing NDP Announcement frame.
  This indication is a straightforward method that does not need additional signaling.
  Three subtype values, for example, 0000, 0001, and 1111 can be considered.


## Slide 13: The sensing NDPA indication - Opt.2
Since the sensing NDPA frame is indicated by using the subtype field in the frame control field, the Sounding Dialog Token field of the sensing NDPA variant can be newly designed.
  We can consider the various bit configurations for Sounding Dialog token field, for example,
    A part of bits(i.e., B0-Bx) in this field can be used to identify the specific measurement in the sensing session.
      It can be used as a measurement setup ID
    Other remain bits(i.e., By-B7) can be used to indicate the sounding dialog token number.
      It can be used to identify the each measurement instance.
    The configuration of sounding dialog token field in sensing NDPA variant
 | B0 Bx | By B7
 | Measurement setup ID | Sounding Dialog Token Number
Bits: | TBD | TBD
Notes: Sounding dialog token 재구성 가능 함
Bit 구성은 좀더 크게 고려 – 자유롭게 구성 가능함

## Slide 14: The sensing NDPA indication - Opt.3
There are many reserved AIDs that are not used in STA info field of four NDPA variants.
  For example, the following AIDs are reserved in 11be.
Thus, to indicate the sensing NDPA, we can consider the use of a specific AID reserved in current NDPA variants.
In addition, we can consider defining a Special STA info field that includes a specific AID.
  A Special STA info field is located at the first in STA info fields and has an equal size with other STA info fields.

## Slide 15: The sensing NDPA indication - Opt.3
Sensing NDPA frame considering the Special STA info field can be configured as follows, for example.
  The frame format of Sensing NDPA frame can be the same as an HE NDPA frame.
  The content of STA info field can be redesigned.
As the Special STA info field is located at first than other STA info fields, it is possible to check early whether the received NDPA is a sensing variant or not.
The Special STA info field can contain the parameters related to sensing measurement.
  Details for Special STA info field is TBD.
 | MAC header |  |  |  |  |  |  |  |  | 
 | Frame Control | Duration | RA | TA | Sounding Dialog Token | Special STA Info | STA Info 1 | … | STA Info n | FCS
Octets: | 2 | 2 | 6 | 6 | 1 | TBD | TBD |  | TBD | 4

## Slide 16: The sensing NDPA indication – comparison
We consider the following three options for the indication of the sensing NDPA.
  All options are possible to redesign the content of the sensing NDPA.
 | Pros. | Cons. or Consideration
Opt.1 | It is possible to incorporate the sensing NDPA with all defined NDPA variants. | False detection possibility for Sounding Dialog Token Number when B7 set to 1.
Opt.2 | It has no restriction for the design of the sensing NDPA | Use of subtype field for specific operation
Opt.3 | It is possible to incorporate the sensing NDPA with all defined NDPA variants. | Detection error of special info field for VHT, Default overhead for Special STA info field,

## Slide 17: STA info field (1/2)
As shown in slide 5, according to the NDPA variant, the STA info field has a different size.
  In the VHT NDPA variant, it consists of 2 bytes
  In other NDPA variants (HE/Ranging/EHT), it consists of 4 bytes.
Considering the signaling for new sensing features, it seems to be reasonable to use the STA info field configured with 4 bytes.
  As using the existing size of the STA info field, we can prevent the issues such as the complexity of the new design.
    As long as the existing size of the STA info field is maintained, we can also prevent the ambiguity with the STA info field of other variants.

## Slide 18: STA info field(2/2)
The STA info field in the sensing NDPA may contain the following information.
  AID
  Feedback type and Ng
    Indicate the feedback type such as CSI, threshold based, and so on and the granularity of channel measurement.
  Codebook size
    Configuration of feedback information, for example, bit size for amplitude or angle of carriers.
  Disambiguation
    To prevent the wrong detection of AID by VHT STA, it should be included.
    For this field, one bit is allocated.
  Partial BW info
    Indicate the disallow sub channel in PPDU BW
    We can reuse the Partial BW info defined in 11be
  Nss
    The number of spatial stream for NDP transmission.
  LTF information
    Type/GI, repetition
In addition to the above information, various information may be considered.

## Slide 19: Summary (1/2)
In this contribution, we took into account the various points for the design of the sensing NDPA.
  First,
    As an aspect of the design of the sensing NDPA frame, we considered two approaches as follows.
      Approach 1: reusing the existing NDPA frame variant
      Approach 2: define the new sensing NDPA frame variant
  Second,
    For the indication of the sensing NDPA, we introduced the following three options.
      Option 1: use of the one bit(e.g. B7) of sounding dialog token number field
      Option 2: use of the reserved value of the Subtype subfield in the frame control field.
      Option 3: use of Special STA info field

## Slide 20: Summary (2/2)
  Third,
    It seems to be reasonable to use the STA info field configured with 4 bytes to secure the sufficient bit for newly defined information for sensing.
    The sensing NDPA frame format is same as HE NDPA frame format.
      Example of the sensing NDPA frame format
  Fourth,
    The STA info field in the sensing NDPA contains the information related to sensing measurement.
    For example, the contents illustrated in slide 15 may be included.

## Slide 21: Straw Poll #1
Do you agree to add the following to 11bf SFD?
  The sensing NDPA frame includes the Special STA Info field.
  The special STA Info field includes the common information related to sensing measurement.
    The details are TBD.
  The Special STA Info field of sensing NDPA frame has the same size as the STA Info field.
  The Special STA Info field of sensing NDPA frame is placed in front of other STA Info fields.
  The Special STA Info field of sensing NDPA frame is identified by using a specific AID.
    The value of the specific AID is TBD.

## Slide 22: Straw Poll #2
Do you agree to add the following to 11bf SFD?
  The Special STA info field includes the Measurement setup ID.
    Other information is TBD.

## Slide 23: Straw Poll#3
Do you agree to add the following to 11bf SFD?
  The sensing NDPA frame shall include the Sounding Dialog Token field
    NDP Announcement Variant subfield (B0B1) is set to 10 (i.e. Ranging NDP Announcement frame)
    Sounding Dialog Token Number subfield (B2-B7) is used to indicate the measurement instance ID

## Slide 24: Reference
[1] IEEE P802.11-REVme D0.3
[2] IEEE P802.11ax-2021
[3] IEEE P802.11az D3.2