## Slide 1: EHT Sounding Enhancements
Date: November 2nd, 2021
Authors:
Name | Affiliation | Address | Phone | Email
Arik Klein | Huawei Technologies |  |  | Arik.Klein@huawei.com
Shimi Shilo |  |  |  | Shimi.Shilo@huawei.com
Ross Jian Yu |  |  |  | ross.yujian@huawei.com

## Slide 2: Introduction
  EHT Sounding is described in 802.11be D1.2.
  One of the new features in 802.11be is preamble puncturing
    Preamble puncturing has an impact on the EHT Sounding procedure
  In this contribution we want to raise several concerns / open issues that need to be addressed in the EHT Sounding procedure to fully support the required use cases with punctured PPDUs

## Slide 3: Sounding Overview
  The sounding procedure, defined in the 802.11 be spec, consists of multiple frames depicted in the following diagram:
  The sounding mechanism may be used for multiple purposes, such as:
    Beamforming – the beamformee feedbacks the beamforming weights that the beamformer may use for its transmission(s); the respective SNR is also fed-back
    Scheduling – in order to determine where (in frequency) is the best RU to allocate a specific STA in a MU transmission, and with what parameters (MCS, Nss etc.) to allocate, an AP may initiate a sounding mechanism; in response, the STA feedbacks a CQI for the requested RUs or the entire BW

## Slide 4: Puncturing in 11be
  The 802.11be D1.2 spec currently supports the following puncturing patterns:
    EHT MU (non-OFDMA) – a single ‘hole’ in the used bandwidth; there are 45 supported patterns defined by the 5-bit punctured channel indication in the U-SIG field
    EHT MU (OFDMA) – any one of 7 puncturing patterns is supported for each 80MHz subblock (‘0111’,’1011’,’1101’,’1110’,’0011’,’1001’,’1100’) by using 4 of 5 bits of the punctured channel indication in the U-SIG field
  An AP may use the Disabled Subchannel Bitmap to indicate to all STAs which subchannels should not be used for all PPDU exchanges on this operating channel in this EHT BSS
    The Disabled Subchannel Bitmap shall correspond to one of the non-OFDMA puncturing patterns
    In both MU and non-HT Duplicate PPDUs, a STA may puncture other subchannels in addition to those indicated in the Disabled Subchannel Bitmap
  The feedback resolution for 320MHz BW is 40MHz, as defined in both the NDP Announcement and the EHT MIMO Control field– irrespective of the puncturing resolution being used

## Slide 5: Sounding & Puncturing in 11be
  As a result of the puncturing rules defined in 11be, there are several severe inefficiencies that come up in the context of the sounding mechanism
  In particular, the following three problems:
    Excessive BW reduction for both OFDMA and non-OFDMA
    Limitation on sounding for scheduling
    Mismatch between actual feedback report size and size derived from the MIMO Control field for the 320MHz BW case
  In the next slides we give more details about these problems

## Slide 6: Problem #1 – Excessive BW Reduction
  As mentioned in the previous slide, the Disabled Subchannel Bitmap (as defined today) must correspond to a non-OFDMA puncturing pattern
  Let us consider an AP which wants to transmit on 160MHz and senses two 20MHz subchannels as busy (e.g. due to interference of incumbent users) - as shown in the figure below - and wants to mark these subchannels as disabled
  The AP wants to set a Disabled Subchannel Bitmap which ensures all STAs refrain from any frame exchange on these interfered subchannels
  The only non-OFDMA puncturing pattern that is suitable in this scenario is a single 20MHz ‘hole’ in the primary 80MHz BW - therefore, the actual BW in which the frame exchange is allowed has to be reduced from 160MHz to 80MHz (giving up the S80 channel for any frame exchange)

## Slide 7: Problem #2 – Sounding for Scheduling
  When sounding is used for scheduling purposes, the AP may request a STA to feedback information respective to the entire (or large portions of the) BW so that the AP can choose where to allocate the STA (e.g. what RU to use)
  Transmitting data in an EHT MU PPDU is very flexible in terms of puncturing (e.g. different puncturing in each 80MHz subblock)
    However, this flexibility is severely limited by the constrained puncturing support in the preceding non-OFDMA punctured frames (e.g. sounding NDP) and the defined feedback resolution/coverage
  The following figure depicts an example where OFDMA could be used with 320MHz in the DL with per-80MHz puncturing, but is limited to 80MHz because of the sounding NDP frame using non-OFDMA puncturing

## Slide 8: Problem #3 –Feedback & Puncturing Mismatch
  The beamformer (e.g. AP) instructs the beamformee (e.g. STA) for which subcarriers it should feedback information via the Partial BW Info subfield
    The beamformer includes this subfield in the NDP Announcement, and the beamformee responds with this subfield in the MIMO Control field
  The feedback resolution for BW up to 160MHz is 20MHz.
  In case of 320MHz BW, the Partial BW Info is in resolution of 40MHz, irrespective of the puncturing being actually used – which may be in resolution of 20MHz (even if previous problems are solved)
  This creates two different problems:
    The NDPA and NDP frames may be transmitted with a 20MHz puncturing granularity, but the MIMO Control field is limited to 40MHz granularity, which in these cases will create a mismatch between actual report size and the size reported in the header, and therefore an error in decoding – see figure in next slide
    The AP cannot instruct the non-AP STA to provide feedback on specific non-punctured 20MHz subchannels – only in coarse steps of 40MHz – which may lead to non-negligible overhead
  Therefore, the option of requesting (and reporting) a channel feedback in resolution of 20MHz subchannel for BW greater than 160MHz should be added.

## Slide 9: Problem #3 –Feedback & Puncturing Mismatch
  An example for 320 MHz BW with two 20 MHz punctured subchannels is given below

## Slide 10: Conclusions
  We described several scenarios where the puncturing rules existing in 11be severely restrict the employment of sounding
    This is true for both OFDMA and non-OFDMA transmissions, and for beamforming and scheduling purposes
  It is our view that 11be should address these issues

## Slide 11: SP1
  Do you support to modify the EHT Sounding procedure in 802.11be R1 to address the following problem:
    Support OFDMA puncturing patterns in Disabled Channels bitmap
  Yes / No / Abstain

## Slide 12: SP2
  Do you support to modify the EHT Sounding procedure in 802.11be R1 to address the following problem:
    Support OFDMA puncturing patterns in Sounding NDP
  Yes / No / Abstain

## Slide 13: SP3
  Do you support to modify the EHT Sounding procedure in 802.11be R1 to address the following problem:
    Support 20 MHz subchannel resolution for channel feedback when Sounding NDP BW is greater than 160MHz (both in NDPA and in BFR (in MIMO Control field)).
  Yes / No / Abstain

## Slide 14: References
  [1] IEEE P802.11be D1.2, September 2021 (amendment to IEEE 802.11-2020 standards)