## Slide 1: Imaging Radar data report
Date: 08-Nov-21
Author:
Name | Affiliation | Address | Phone | Email
Alecsander Eitan | Qualcomm |  |  | eitana@qti.qualcomm.com
Assaf Kasher | Qualcomm |  |  | akasher@qti.qualcomm.com
Solomon Trainin | Qualcomm |  |  | strainin@qti.qualcomm.com

## Slide 2: Agenda
This presentation introduces the Imaging Radar
We present the typical processing of an Imaging Radar
Discuss the report options and evaluate them

## Slide 3: Imaging Radar
Imaging Radar provides “image” of the scene The image is: 2D (Az, Range or Az, El or Range, Doppler) 3D (Az, El, Range or Az, Range, Doppler) 4D (Az, El, Range, Doppler)
Typical Imaging Radar processing block diagram
Notes:
2D is a two-dimensional data, 3D is a three-dimensional data and 4D is a four-dimensional data
Az and El are Azimuth and Elevation
CFAR is - “Constant False Alarm Rate”. CFAR detection refers to a common form of adaptive algorithm used in radar systems to detect target returns against a background of noise, clutter and interference)

## Slide 4: Imaging Radar Data

## Slide 5: Imaging Radar Data

## Slide 6: Imaging Radar Data
Snapshot from a nice video from NXP

## Slide 7: Imaging Radar Data
Time Domain (CSI): 24 bit per sample -> Huge size (12x2xTmeas)
2D/3D/4D: -> Huge size
2D/3D/4D Filtered: -> Large size
Targets: -> Compact

## Slide 8: Conclusions
Reporting Time-domain data is very ineffective for imaging Radar, and requires the recipient to perform processing, like AoA (which requires knowledge known only at the receiver)
Reporting Unfiltered 2D/3D/4D map is very ineffective for imaging Radar.
Reporting Filtered 2D/3D/4D map is practical
Reporting Targets is the most efficient method

## Slide 9: SP #1
Do you agree to add the following to 11bf SFD:
  The 11bf amendment shall define one or more report methods for 2D, 3D and 4D filtered maps.

## Slide 10: Motion #1
Move to add the following to the TGbf SFD:
  The 11bf amendment shall define at least one measurement result type for 2D, 3D and 4D filtered maps, for DMG/EDMG.
  This measurement result type is an optional feature.
  Supporting 2D, 3D and 4D are each optional feature
  The details of the report format is TBD
  2D is a two-dimensional map, where the two dimensions are any from: Range, Azimuth, Elevation & Doppler.
  3D is a three-dimensional map, where the three dimensions are any from: Range, Azimuth, Elevation & Doppler.
  4D is a four-dimensional map, where the four dimensions are: Range, Azimuth, Elevation & Doppler.

## Slide 11: SP #2
Do you agree to add the following to 11bf SFD:
  The 11bf amendment shall define one or more report methods for targets. (“Target” is a detected object. e.g. with a 3D size and specific doppler)

## Slide 12: Motion #2
Move to add the following to the TGbf SFD:
  The 11bf amendment shall define at least one measurement result type for targets, for DMG/EDMG. (“Target” is a detected object)
  This measurement result type is an optional feature.
  The details of the measurement result type is TBD