## Slide 1: Measurement setup frame formats
Date: 2021-11-09
Authors:
Chaoming Luo (OPPO)
Name | Affiliation | Address | Phone | Email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Lei Huang |  |  |  | 
Pei Zhou |  |  |  | 

## Slide 2: Introduction
The SFD states that an optional negotiation process in the sensing measurement setup is defined. [1]
This contribution discusses more about the detail of measurement setup frame formats.

## Slide 3: Recap: measurement setup
Measurement setup in SFD:
An optional negotiation process in the sensing measurement setup is defined that allows for a sensing initiator and a sensing responder to exchange and agree on operational attributes associated with a sensing measurement instance.
The operational attributes may include initiator’s and responder’s roles, measurement report types, and other operational parameters.
The type of measurement result reported in a WLAN sensing procedure shall be decided by its initiator.
Trigger-based (TB) sensing measurement setup – TBD.
Non-TB sensing measurement setup – TBD.
Note: according to “Figure 1: WLAN sensing procedure (example)” in SFD, we assume the negotiation is pairwised conversation.

## Slide 4: Discussion: procedure
What are the possible sensing measurement setup procedures?
  Option 1 (unified sequence): A sequence of a Request and a Response frame.
  Option 2 (mixed sequence): Either a sequence including a Request and a Response frame, or a sequence including a Request and a Response and a Confirmation frame.

## Slide 5: Discussion: option 1
It’s pretty straightforward that a sensing measurement setup procedure as following could handle the most common cases.
If the Responder rejects the proposed operational attributes, the Initiator may request again as shown in case 2 with modified operational attributes based on the rejection reason of the previous response.
case 1: Responder accepts the attributes at the first shot.
case 2: Responder rejects the attributes at the first shot but accepts at the second.

## Slide 6: Discussion: option 1 (cont.)
However, a Responder may provide more information for preferred operational attributes, to assist the Initiator to make a successful setup.
  Note: the setup is actually fails when using the Measurement Setup Response with Alternate attributes, which is similar as TWT setup exchange in 11ax.
    Alternate means preferred attributes but also willing to accept other attributes.
    Dictate means only willing to accept the proposed attributes and any other will be rejected.
  Need a second measurement setup exchange in order to succeed. – unified procedure with possible overhead.
case 3.1: Responder proposes different attributes at the first shot but accepts or rejects at the second.

## Slide 7: Discussion: option 2
So, should we go with the same way as TWT setup exchange in 11ax? A possible options 2 is:
  For case 1 and 2, it’s same as option 1.
  For case 3, a Measurement Setup Confirmation frame could be considered to reduce overhead. --a little bit more complex procedure reducing overhead of one frame.
case 3.2: Responder proposes different attributes and Initiator confirms to accept or reject Responder’s proposal.

## Slide 8: Proposal: Measurement Setup frames
Propose a new subtype of Public Action frame: Sensing Public Action frame. It may be a protected frame if RSNA is established.
  Consider that we may support sensing with unassociated-STAs, Public Action frame is the best choice. (Note: 11az also use Public Action frames)
Propose to define all possible sensing action frames using the same Public Action field value (e.g., 51), and have to a Sensing Subtype field to differentiate them.
  Reserve more Public Action field values for future amendment specs.
Detailed parameters are contained in frame dependent fields and elements.

## Slide 9: Proposal: Sensing Subtype field
Sensing Subtype field, e.g:
Sensing Subtype field value | Description
<ANA> | Sensing Measurement Setup Request
<ANA> | Sensing Measurement Setup Response
<ANA> | Sensing Measurement Setup Termination
<ANA> | Sensing Measurement Report
Sensing Measurement Setup Confirmation depends on whether we choose option 2
Other Sensing Subtypes are TBD

## Slide 10: Proposal: Measurement Setup Request/Response
Frame dependent fields and elements for Sensing Measurement Setup Request:
  Setup Command field (size TBD):
    Demand(0)/Suggest(1) for request
    Accept(2)/ Reject(3)/Alternate(4) for response
  Sensing Operational Parameters element: operational attributes for the Responder.

## Slide 11: Proposal: Measurement Setup Confirmation
Frame dependent fields and elements for Sensing Measurement Setup Confirmation:
  Setup Command field: Accept(2)/ Reject(3). (size TBD)
  Reason Code field: exists when Setup Command field indicates Reject. (size TBD)

## Slide 12: SP 1
Which option do you prefer to design the sensing measurement setup procedure?
  Option 1 (unified sequence): A sequence of a request and a response frame.
  Option 2 (mixed sequence): Either a sequence including a request and a response frame , or a sequence including a request and a response and a confirmation frame.
  Abs
  Y/N/A
Chaoming Luo (OPPO)

## Slide 13: SP 2a
Do you agree to add the following into 11bf SFD ?
  A sensing measurement setup procedure is defined in which:
    In a response to a received sensing measurement setup request, a Responder may reject the request and propose with alternate operational attributes.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 14: SP 2b
Do you agree to add the following into 11bf SFD ?
  A sensing measurement setup procedure is defined in which:
    In a response to a received sensing measurement setup request, a Responder may reject the request and propose with alternate operational attributes.
    The Initiator shall send a sensing measurement setup confirmation frame to accept or reject the alternate operational attributes proposed by the Responder.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 15: Reference
[1] 11-21-0504-03-00bf-specification-framework-for-tgbf
Chaoming Luo (OPPO)