## Slide 1: EBCS Data Transmission Timing
Date: 2021-11-09
Authors:

## Slide 2: Abstract
This presentation is a discussion material for EBCS Data transmission timing.
Addressing CID 2038 and 2222.

## Slide 3: Comments
CID 2222
  Why does EBCS DL have to be transmitted immediately after a Beacon. If its destination is any STA in range, the transmission should be more flexible.
  An EBCS DL stream should be able to be configured to transmit on a schedule that is independent of the BSS operation. There should be no requirement for the transmissions to occur immediately after a beacon, although for some cases, that could be the case. The commenter is willing to collaborate to create a submission to address this comment.
CID 2038
  I suppose the EBCS Data frame(s) are transmitted right after the Beacon frame that carried the EBCS TIM element indicating buffered EBCS traffic. Please clarify. In addition, please clarify the operation when it corresponds to the DTIM beacon for the BSS and the group address bit is set to 1 - i.e., both infra BSS MC/BC frames and EBCS broadcast follow the Beacon frame.

## Slide 4: Current Draft (D2.0)
EBCS Info frame is transmitted immediately after a Beacon frame. (11.55.2.2)
EBCS TIM element in a Beacon frame indicates whether the traffic is buffered or not. (11.55.2.2)
EBCS Data frame transmission timing is not described.
  Author’s intension in D2.0
    AP can transmit EBCS Data frames anytime in the beacon interval that is indicated the traffic is buffered.
    Receiver keep wake-up during the beacon interval that is indicated the traffic is buffered.
    Burst transmission should be avoided for HCFA that utilizes the frame transmission timing.

## Slide 5: Assumption
AP cannot know when the traffic comes.
2 categories of content
  Category 1: Live Streaming
    Content is generated continuously.
    AP should not buffer the traffic to avoid extra latency.
    Receivers need to keep wake-up.
  Category 2: Intermittent Content (e.g. timetable updated every 3 sec)
    Static content (e.g. a set of files)
    AP can buffer the traffic.
    Receivers can sleep.

## Slide 6: Proposed Resolution
Add 1 bit that indicates the content category of the traffic, to the Content Information Control subfield in the Content Information field in the EBCS Info frame.
  Value 0 indicates the traffic is not buffered. (unbuffered traffic)
  Value 1 indicates the traffic is buffered. (buffered traffic)

## Slide 7: Buffered Traffic
AP buffers received traffic.
AP indicates the buffered traffic in the EBCS TIM element.
AP transmits the buffered traffic immediately after the Beacon frame indicating the traffic is buffered.
When the buffered traffic is in multiple frames, More Data subfield in the Frame Control field in the EBCS Data frames except the last one is set to 1.
For HCFA, dot11HCFAKeyChangeInterval = n * dot11BeaconPeriod.
Beacon
Traffic
1
1
0
1
More Data
EBCS TIM
0
1
0
1
0
HCFA Key 1
(n = 1)
HCFA Key 2

## Slide 8: Unbuffered Traffic
AP always indicates the traffic is not buffered in the EBCS TIM element even if there are no buffered traffic.
AP transmits the traffic as soon as possible.
More Data subfield in the Frame Control field in the EBCS Data frames is always set to 1.
No restrictions for dot11HCFAKeyChangeInterval.
Beacon
Traffic
1
1
1
0
More Data
EBCS TIM
0
1
1
0
0