## Slide 1: Evolution Time for the IEEE 802 Architecture
Date: 2021-11-11
Authors:

## Slide 2: Abstract
The time has come to update the IEEE 802 architecture, as nominally represented in IEEE Std 802-2014.

## Slide 3: IEEE Std 802: Overview and Architecture
Maintained by 802.1 WG
Originally IEEE Std 802-1990
  Note: IEEE 802 was initiated ten years earlier.
Revision IEEE Std 802-2001
Revision IEEE Std 802-2014
Amendments
  IEEE Std 802d-2017: Allocation of Uniform Resource Name (URN) Values in IEEE 802 Standards
  IEEE Std 802c-2017: Local Medium Access Control (MAC) Address Usage
  P802f: Amendment: YANG Data Model for EtherTypes (WG ballot)

## Slide 4: Procedural issue require a revision
Reason:
  No new amendments beyond three
Bigger Reason:
  an IEEE standard may remain continuously active only if a revision process for that standard is completed and approved within 10 years from the date that the standard was approved or last revised
  If the revision project has not been completed and approved by Year 10, the approved standard will be transferred to inactive-reserved status.
Need to complete a revision within 3 years.
Do we need more than a maintenance roll-up?

## Slide 5: Current discussion status
IEEE 802 Restructuring ad hoc (Technical Coherence sub-ad hoc) discussed “a focused pre-PAR activity, conducted in, for example, a Study Group or an Industry Connections Activity such as Nendica” with “ambitious but documented goals”
Nendica (IEEE 802 “Network Enhancements for the Next Decade” Industry Connections Activity) was rechartered September 2021 for two years
  Hosted by IEEE 802.1 WG, but without membership
  Evolved Link Layer Architecture [ELLA]: Nendica Study Item since July 2021 <https://1.ieee802.org/nendica-ella/>
802.1 Chair announced Technical Plenary series starting Dec 2.
I anticipate that 802.1 WG will seek March 2022 PAR.

## Slide 6: What is the IEEE 802 Family?
IEEE Std 802 says:
  This standard serves as the foundation for the family of IEEE 802 standards published by IEEE for local area networks (LANs), metropolitan area networks (MANs), personal area networks (PANs), and regional area networks (RANs).
  several types of medium access technologies are currently specified in the family of IEEE 802 standards
What is a “Family of Standards”?
In what way are the standards “related”:
  The nature of the relationship is not explained or explored.
What do IEEE 802 standards have in common?
  They largely share addresses.
So, is this a family, or simply a group of “roommates” with shared addresses?

## Slide 7: What is the IEEE 802 Architecture?
What does IEEE Std 802 say about the IEEE 802 architecture?
  Very little
  The Scope says “The IEEE 802 architecture is defined”
  The word “architecture” appears sparsely.
  No content purports to specify the architecture.
  The closest to a specification of the architecture is in Clause 5 (“Reference models (RMs)”) says “Figure 3 shows the architectural view of IEEE 802 RM for end stations and its relation to the OSI/RM. A variation of the model applies within bridges, as described in 5.3.2.”
  Conclusion: The IEEE 802 architecture is neither defined nor specified.
Not in the 802 Architecture:
  LLC, bridging, VLANs, priorities, PDU size limits, …
  The Link Layer Service

## Slide 8: The “Common” LLC
In relation to the IEEE 802 RM figure (Fig. 3), IEEE Std 802 says:
  For the mandatory data services supported by all IEEE 802 networks, the DLL is structured as two sublayers, with the logical link control (LLC) sublayer, described in 5.2.2, operating over a MAC sublayer, described in 5.2.3.
So, the LLC is the commonality in the 802 architecture.
IEEE Std 802.2 is “Logical Link Control.” IEEE Std 802 says:
  IEEE Std 802.2-1989 (reaffirmed 2003) was administratively withdrawn as an IEEE standard on 11 January 2011 in deference to the stabilized standard ISO/IEC 8802-2:1998 where the same material continues to be available.
IEEE Std 802 does not detail a role for 8802-2 in the architecture.
IEEE Std 802 explains 8802-2 only in relation to protocol identification; however, it requires support for a different method of protocol identification, and the Introduction says:
  While the protocol identification mechanism specified by ISO/IEC 8802-2 (IEEE Std 802.2™, withdrawn) is still used, its use for new standards has been deprecated.
    See EPD and LPD
So, what exactly is the common LLC?

## Slide 9: Link Layer Service
Open Systems Interconnection (OSI) specifies seven layers.
ITU-T X.212 (OSI “Data Link Service [DLS] Definition”) describes the service provided by the DLS to the Network Layer, including:
  Provides for the transparent transfer of DLS user-data. It does not restrict the content, format or coding of the information, nor does it ever need to interpret its structure or meaning.
  The DLS relieves the DLS user from loss, insertion, corruption or, if requested, misordering of data which may occur. In some cases of unrecoverable errors in the Data Link Layer, duplication or loss of DLSDUs may occur.
  Data Link addresses have only local significance within a specific Data Link configuration over a single transmission medium (point-to-point or multi-point physical connection) or a group of parallel transmission media (multi-link or splitting function). Therefore it is not appropriate to define a global addressing structure.
  and more
Connectionless-mode and Connection-mode services are specified
Does 802 specify the 802 Link Layer Service provided to the network?
  No.

## Slide 10: Do we need an LLC?
Potential functions of an LLC
  Protocol multiplexing/demultiplexing
    With unified “EPD” and “LPD”
  VLAN multiplexing/demultiplexing
  Improved operation with the MAC service below
    Translates among different MACs
  Unified interface to the LLC Client above
    Instead of a custom interface to each IEEE 802 MAC
  Well-defined service at the LLC interface (LSAP)
    Primitives and parameters
    Clear expectation of the service requirements (e.g., ordering)
      Including, e.g., priority, etc.
      Pass QoS parameters; e.g. stream identification
    Expectations of allowed and disallowed frame formats
Backward compatibility
  Existing application interface to MSAP should still function

## Slide 11: Further Information
Potential Nendica Study Item: Evolving IEEE 802 Architecture Requirements
  https://mentor.ieee.org/802.1/dcn/21/1-21-0014-03-ICne.pdf
ELLA: What is the IEEE 802 Link Layer Service?
  https://mentor.ieee.org/802.1/dcn/21/1-21-0045-02-ICne.pdf
ELLA: Proposed Aspects of IEEE Std 802 Revision
  https://mentor.ieee.org/802.1/dcn/21/1-21-0060-04-ICne.pdf