## Slide 1: Redundant Transmission over ML for Low Latency Traffic
Date: 2021-11-12
Authors:

## Slide 2: Background
Restricted TWT is introduced to support RTA traffic in 11be.
  rTWT will work fine for periodic RTA traffic
Interval and data volume of RTA traffic burst changes
  From AP point of view, interval of DL RTA traffic burst to an APP in a STA is changing along with the situation of the network busy status between the AP and the peer point of the APP.
  The interval and data volume of some RTA UL traffic burst may be changing along with the RTA APP running.
The rTWT SP needs be set long enough to cover the interval change and data volume change of RTA traffic burst to meet the low latency requirements.
  This leads to impacts to the BSS.

## Slide 3: Background
3GPP New Radio (5G) introduces PDCP PDU duplication transmission over multiple cells for URLLC (Ultra Reliable Low Latency Communications).
  Copies of a PDCP PDU are being transmitted concurrently over multiple cells.
  The transmission is stopped as soon as one copy is transmitted successfully.
  The latency of the PDCP PDU is the latency of the copy first successfully transmitted.
Multi-link is introduced in 11be.

## Slide 4: Discussion
To have low latency, redundant transmission over multiple links between 2 MLDs can be utilized as a supplementary to rTWT.
  Redundant transmission over multiple links between 2 MLDs means copies of a MPDU are being transmitted concurrently over the multiple links.
MLO fits for redundant transmission over multiple links
  Acknowledgement across links
  Duplication detection
To keep the impacts of rTWT SP to the BSS small,
  rTWT SP can be set with a proper duration (which is no need to cover all RTA traffic data arrivals ) to afford most of the RTA traffic bursts.
  RTA data that are not transmitted during the rTWT SP because of late arrival or bigger data volume can be redundantly transmitted over multiple links to meet the latency requirements.

## Slide 5: Examples

## Slide 6: Considerations
Which data to apply redundant transmission over multiple links?
  Rules are needed to prevent abuse.
Over which links the redundant transmission is applied?
  TID mapped links, or subset of TID mapped links
Others?
  Maximum number of copies of the redundant transmission
  ……

## Slide 7: Conclusion
To keep the impacts to the BSS small, it is not good to set a long rTWT SP enough to cover the interval change and data volume change of RTA traffic burst.
3GPP’s PDCP duplication transmission provides a method to achieve low latency, which has been proved in practice.
MLO fits for redundant transmission over multiple links.
Rules are needed to prevent abuse of redundant transmission over multiple links.

## Slide 8: Proposal
Redundant transmission of MPDU over multiple links between 2 MLDs is introduced in 11be.
  Related rules are TBD.

## Slide 9: SP
Do you support to introduce redundant transmission of MPDU over multiple links between 2 MLDs in 11be with TBD rules?
  Option 1, Yes
  Option 2, No
  Option 3, Abstain