## Slide 1: NDPA for Sensing
Date: 2021-11-15
Authors:
Name | Affiliation | Address | Phone | Email
Junghoon Suh | Huawei |  |  | junghoon.suh@huawei.com
Yan Xin |  |  |  | 
Osama AboulMagd |  |  |  | 
Edward Au |  |  |  | 
Mengshi Hu |  |  |  | 
Ross Jian Yu |  |  |  | 

## Slide 2: Background
The NDPA control frame in the current 802.11 baseline is shown below
The first two bits in the Sounding Dialog Token field have been used to indicate the amendment version of the NDPA frame
  The first two bits are already consumed to indicate 4 amendments, VHT, Ranging, HE and EHT R1 (in case EHT R2 change the subfields of the STA Info field)
We need to come up with a new proposal to distinguish the NDPA frame for Sensing
NDPA
Frame
Control
Duration
RA
TA
Sounding
Dialog Token
STA Info
1
...
STA Info n
FCS
Octets
:
2 2 6 6 1 2 /4
/
/
2/4 4

## Slide 3: Option 1: Setting the Sounding Dialog Token Number to all 1’s
If we denote the bit index for the 6 bit Sounding Dialog Token Number as B2 to B7, we propose to set all the bits from B2 to B7 in Sounding Dialog Token Field to all 1’s, while B0 and B1 are set to zero.
  Sounding Dialog Token Number corresponds to the Measurement Instance ID for Sensing
  NDPA can be regarded as a VHT NDPA by the legacy devices, but through the examination of AIDs in the STA Info fields and the FCS, it is easily ignored by the legacy devices
  We leave all 1’s case in Sounding Dialog Token Number as a special indication for the presence of the additional 2 byte NDPA variant field, immediately following the Sounding Dialog Token field
Current 802.11 NDPA Sounding Dialog Token Field
Ranging (B0) | HE (B1) | Description
0 | 0 | VHT NDPA
0 | 1 | HE NDPA
1 | 0 | Ranging NDPA
1 | 1 | EHT NDPA (R1)
Ranging
Bits
:
1 1 6
HE
Sounding Dialog
Token Number
11
az
Reserved
Bits
:
2 6
Sounding Dialog
Token Number
VHT
Reserved
Bits
:
1 1 6
HE
Sounding Dialog
Token Number
HE
B0
Bits
:
1 1 6
B1
Sounding Dialog
Token Number
EHT
B2
B7

## Slide 4: New NDPA Frame Format
Among those 8 bits in Sounding Dialog Token field, the first two bits are zeros and the remaining 6 bits are ones
16 bits from B0 to B15 in NDPA Variant field can be used for the indication of NDPA Version ID, Measurement Instance ID and some possible common information in the future amendments except for B11
  B11 needs to be set to 1 as the Disambiguation subfield to avoid the wrong detection of AID
  Some bits among the remaining bits can indicate NDPA Frame Version ID for Sensing, future amendments like EHT R2, EHT+, etc.
  Some bits shall be set to Measurement Instance ID subfield
  All the unused bits in the NDPA Variant field are Reserved and can be used for future purposes such as common information (e.g. BW, Preamble Puncturing pattern indication) for all the recipient STAs
    One of the unused bits may be used to indicate the extension of the NDPA Variant
STA Info # 1
STA Info # n
FCS
NDPA
Version
ID
MAC
Header
Sounding
Dialog
Token
Octets
:
1 NDPA Variant (2) 4
4 4
Reserved
Disambi-
guation
B0
B11
B15
Reserved

## Slide 5: Option 1-A: Setting the B11 in the NDPA Variant Field to 1
The B11 in the NDPA Variant field is set to 1, and indicates the NDPA Variant field
The first two bits of Sounding Dialog Token field are set to zero, while the remaining 6 bits of the Sounding Dialog Token field continue to play a role of the Measurement Instance ID / Sounding Instance ID, depending on the SENS or main stream 802.11 sounding
All the unused bits in the NDPA Variant field are Reserved and can be used for future purposes such as common information (e.g. BW, Preamble Puncturing pattern indication) for all the recipient STAs
  One of the unused bits may be used to indicate the extension of the NDPA Variant
The size of NDPA Variant field can be extended to the larger size
The size of the STA Info field can be extended larger than 4 bytes as well
  In this case, the size of the STA Info field can be indicated in the NDPA Variant field
STA Info # 1
STA Info # n
FCS
NDPA
Version
ID
MAC
Header
Sounding
Dialog
Token
Octets
:
1 NDPA Variant (2) 4
4 4
Reserved
Disambi-
guation
B0
B11
B15
Reserved

## Slide 6: Option 2: Define a new control frame for the new sounding frame
The 4 bit Subtype subfield of the Frame Control field in the MAC header is running out of the control frame subtypes
However, 3 control frame subtypes 0000, 0001 and 1111 are still reserved. We can use one of these remaining 3 control frame subtypes to define a new control frame called “New NDPA” frame.
The example format of this new NDPA is as follow
Frame
Control
STA Info # 1
STA Info # n
FCS
Duration
TA
Sounding
Dialog
Token
RA
Octets
:
2 2 6 6 2 4
4 4
NDPA Variant
Measurement Instance ID /
Sounding Instance ID
Bits:
8
8

## Slide 7: Option 2-A: Define a new control frame with Control Frame Extension
One of the Control Frame subtypes was already defined for a generation of future control frames which is the Control Frame Extension
We propose to use this Control Frame Extension to create a new control frame for the NDPA of future variants and Sensing
The 4 bit Subtype subfield of the Frame Control Field in the MAC header is set to 0110, which indicates the Control Frame Extension frame. The following format is an example of a new NDPA frame using the Control Frame Extension
  One of the Extended subtypes in the Control Frame Extension subfield indicates the New NDPA frame type
Frame
Control
STA Info # 1
STA Info # n
FCS
Duration
TA
Sounding
Dialog
Token
RA
Octets
:
2 2 6 6 2 4
4 4
NDPA Variant
Bits:
8
8
Measurement Instance ID /
Sounding Instance ID
B0
B1
B2
B3
B4
B7
B8
B11
B12
B15
Protocol
Version
Type
Subtype
(0110)
Control
Frame
Extension
Power Management /
More Data /
Protected Frame / +HTC

## Slide 8: Summary
We proposed three different proposals to accommodate the new NDPA frame needs
  Option 1 use the existing NDPA Control frame
    Additional NDPA Variant field is proposed
  Options 2 and 2-A use the new Control frame subtypes
    Use one of the available Reserved subtype
    Use the Control Frame Extension subtype