## Slide 1: CR for PAR throughput verification
Authors:
Name | Affiliations | Address | Phone | Email
Yiqing Li | Huawei | Shenzhen, China |  | liyiqing3@Huawei.com
Yuchen Guo |  |  |  | 
Yunbo Li |  |  |  | 
Ming Gan |  |  |  | 
Jian Yu |  |  |  | 
Guogang Huang |  |  |  | 
Yuxin Lu |  |  |  | 
Yousi Lin |  |  |  | 
Michael Montemurro |  |  |  | 
Date: 2021-11-05

## Slide 2: CID 7619
CID | Commenter | Clause Number | Page. Line | Comment | Proposed Change | Resolution
7619 | Tomoko Adachi |  |  | Verification is needed to see how much throughput can be achieved by R1 features. By doing this, we can think of how to achieve 30 Gb/s throughput and what kind of features are required at the end in P802.11be. | As in the comment. | Rejected. Note to commenter. This comment is rejected since it does not result in a change to the draft. For the 30Gbps throughput verification, four R1 features as Multi-Link, 4KQAM, 1024 MPDU Aggregation per A-MPDU, 320MHz bandwidth guarantee 30Gbps for SU and MU cases and achieve the goal setout in the PAR for the project. Please refer to https://mentor.ieee.org/802.11/dcn/21/11-21-1900-02-00be-cr-for-par-throughput-verification.pptx for detailed simulation results.

## Slide 3: PAR
Doc: 11-18-1231-06-802.11 EHT Proposed PAR[1]
  Capable of supporting a maximum throughput of at least 30 Gbps, as measured at the MAC data service access point (SAP), with carrier frequency operation between 1 and 7.250 GHz while ensuring backward compatibility and coexistence with legacy IEEE Std. 802.11 compliant devices operating in the 2.4 GHz, 5 GHz, and 6 GHz bands
  at least one mode of operation capable of improved worst case latency and jitter.

## Slide 4: How much throughput can be achieved by R1 features
R1 features that are considered in the simulation.
  Multi-Link (with 2 links), 4KQAM, 1024 MPDU Aggregation per A-MPDU, 320MHz
Throughput is measured at MAC data SAP.
Simulation Setup Parameters | Default value
The number of AP MLD | 1
The number of non-AP MLD | 8
The size of area | 20m*20m
Traffic type | Full buffer UL/DL traffic
Packet size | 1500 Bytes per MPDU
TX power | 20dbm for AP MLD; 15dbm for non-AP MLD
NSS | 8
CWmax | 15
CWmin | 7
AIFS | 34us
The number of links | 2 (5GHz&6GHz)
TXOP | 4.096ms
RTS/CTS | on
AP 1
AP 2
STA 1
STA 2
AP MLD 1
Non-AP MLD 1
Link 1
Link 2
PPDU
PPDU
ACK
ACK
Simple scenario: 1 AP MLD and 1 non-AP MLD
Topology: 20m*20m

## Slide 5: 11ax vs Individual EHT Features
Simulation cases | Aggregation | Link # | Bandwidth (MHz) | QAM
Case 1-1 | 256 | 1 | 160 | 1K
Case 1-2 | 1024 | 1 | 160 | 1K
Case 1-3 | 256 | 1 | 160 | 4K
Case 1-4 | 256 | 1 | 320 | 1K
Case 1-5 | 256 | 2 (160MHz for link 1 + 160MHz for link 2) | 160 | 1K
Case 1-1 combines 11ax features, i.e., 256 aggregation for A-MPDU, one link with 160MHz bandwidth, 1KQAM.
For the MU case, each non-AP STA affiliated with non-AP MLD is 1 NSS with 8 non-AP MLDs in total.
No individual feature achieves the target throughput mentioned in the PAR, under these conditions.
Case 1-4 (320 MHz) and Case 1-5 (MLO with 2 links) have better performance.
  The gain increases in order as 4KQAM, 1024 aggregation, 320MHz, Multi-Link.
Chart: Throughput/Mbps
| Case 1-1 | Case 1-2 | Case 1-3 | Case 1-4 | Case 1-5
DL SU | 5522.1 | 7817.58 | 6165.336 | 7938.756 | 11062.26
UL SU | 5525.1 | 7785.276 | 6174.756 | 7830.18 | 11075.652
DL MU | 7667.1 | 8475.96 | 8873.124 | 12970.968 | 15331.08
UL MU | 8384.484 | 8891.136 | 9858.912 | 15133.884 | 16762.956
Gain versus Case 1-1 | Case 1-2 | Case 1-3 | Case 1-4 | Case 1-5
DL SU | 41.57% | 11.65% | 43.76% | 100.33%
UL SU | 40.91% | 11.76% | 41.72% | 100.46%
DL MU | 10.55% | 15.73% | 69.18% | 99.59%
UL MU | 6.04% | 17.86% | 80.50% | 99.93%

## Slide 6: Combinations of two EHT R1 features
Simulation cases | Aggregation | Link # | Bandwidth(MHz) | QAM
Case 2-1 | 1024 | 1 | 320 | 1K
Case 2-2 | 1024 | 2 (160MHz for link 1 + 160MHz for link 2) | 160 | 1K
Case 2-3 | 1024 | 1 | 160 | 4K
Case 2-4 | 256 | 2 (320MHz for link 1 + 160MHz for link 2) | 320 | 1K
Case 2-5 |  | 2 (320MHz for link 1 + 320MHz for link 2) |  | 
Case 2-6 | 256 | 2 (160MHz for link 1 + 160MHz for link 2) | 160 | 4K
Case 2-7 | 256 | 1 | 320 | 4K
There are two different cases when combining two links with 320MHz bandwidth labeled as case 2-4 and case 2-5.
Case 2-5 (MLO with 2 320 MHz links) for UL MU achieves 30Gbps – due to higher transmission efficiency.
Chart: Throughput/Mbps
| Case 2-1 | Case 2-2 | Case 2-3 | Case 2-4 | Case 2-5 | Case 2-6 | Case 2-7
DL SU | 13678.896 | 15517.092 | 9166.296 | 13474.524 | 15642.528 | 12239.64 | 8571.756
UL SU | 13668.12 | 15624.708 | 9167.904 | 13360.956 | 15639.996 | 12317.376 | 8506.296
DL MU | 16883.292 | 16952.844 | 10167.852 | 20618.196 | 25922.196 | 17747.652 | 14665.824
UL MU | 17680.14 | 17783.7 | 10667.952 | 23548.656 | 30283.68 | 19722.348 | 17492.292
Gain versus Case 1-1 | Case 2-1 | Case 2-2 | Case 2-3 | Case 2-4 | Case 2-5 | Case 2-6 | Case 2-7
DL SU | 147.71% | 180.99% | 65.99% | 144.01% | 183.27% | 121.65% | 55.22%
UL SU | 147.38% | 182.80% | 65.93% | 141.82% | 183.07% | 122.93% | 53.96%
DL MU | 120.20% | 121.11% | 32.61% | 168.91% | 238.09% | 131.48% | 91.28%
UL MU | 110.87% | 112.10% | 27.23% | 180.86% | 261.19% | 135.22% | 108.63%

## Slide 7: Combination of three or four EHT R1 features
Chart: Throughput/Mbps
| Case 3-1 | Case 3-2 | Case 3-3 | Case 3-4 | Case 3-5 | Case 3-6 | Case 4-1 | Case 4-2 | Case 5
DL SU | 15701.292 | 14734.092 | 17155.356 | 18322.452 | 21473.1 | 26710.884 | 24748.632 | 30416.124 | 33537.06
UL SU | 15537.12 | 14688.96 | 16954.932 | 18302.82 | 21435.108 | 27109.2 | 24881.124 | 31052.58 | 32823.036
DL MU | 19830.216 | 23495.076 | 29257.692 | 20341.98 | 25307.352 | 33764.376 | 30041.376 | 39717.168 | 38911.104
UL MU | 21012.6 | 27356.004 | 34998.552 | 21331.968 | 26659.908 | 35457.072 | 31669.896 | 42069.828 | 40570.56
With three combined R1 features, case 3-3 for UL MU, case 3-6 for MU cases achieves 30Gbps.
With four combined R1 features, case 4-2 for both MU and SU cases achieves 30Gbps.
Multiple links with 320MHz improve throughput
  Case 4-2 has 262.77%, 270.36%, 373.70%, 401.76% throughput gain in DL SU, UL SU, DL SU and UL MU respectively compared with case 1-1 with four R1 features combined.
In case 5, three links are applied by adding one link with 160MHz based on case 4-1 and it achieves 30Gbps for both MU and SU cases.
  Adding links improves the throughput compared with case 4-1.
Simulation cases | Aggregation | Link # | Bandwidth (MHz) | QAM
Case 3-1 | 1024 | 1 | 320 | 4K
Case 3-2 | 256 | 2(320MHz for link 1 + 160MHz for link 2) | 320 | 4K
Case 3-3 |  | 2(320MHz for link 1 + 320MHz for link 2) |  | 
Case 3-4 | 1024 | 2(160MHz for link 1 + 160MHz for link 2) | 160 | 4K
Case 3-5 | 1024 | 2(320MHz for link 1 + 160MHz for link 2) | 320 | 1K
Case 3-6 |  | 2(320MHz for link 1 + 320MHz for link 2) |  | 
Case 4-1 | 1024 | 2(320MHz for link 1 + 160MHz for link 2) | 320 | 4K
Case 4-2 |  | 2(320MHz for link 1 + 320MHz for link 2) |  | 
Case 5 | 1024 | 3(320MHz for link 1 + 160MHz for link 2 + 160MHz for link 3 ) | 320 | 4K

## Slide 8: Throughput performance with varying traffic rate
Adopt 1024 aggregation for A-MPDU, 2 links (320MHz for link 1 + 320MHz for link 2) and 4KQAM in UL MU MIMO case. Vary the traffic rate and the number of non-AP MLDs.
Traffic Rate (Gbps) | 0.1 | 3.5 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14 | 16 | 18 | 20 | 22
2 non-AP MLDs | 0.19974 | 6.98244 | 8.1027 | 15.0123 | 19.6703 | 22.9616 | 25.4602 | 27.4043 | 28.9793 | 31.3975 | 32.8893 | 34.2942 | 35.0681 | 35.1356 | 35.1077
4 non-AP MLDs | 0.39984 | 13.973 | 16.0045 | 23.5776 | 29.1083 | 32.4679 | 35.4538 | 37.4762 | 38.884 | 39.2018 | 39.416 | 39.3573 | 39.178 | 39.2449 | 39.3014
8 non-AP MLDs | 0.7992 | 27.8695 | 31.5976 | 39.9895 | 41.3457 | 41.5174 | 41.8953 | 41.3567 | 41.6605 | 41.9004 | 41.6343 | 41.7427 | 41.8355 | 41.4449 | 41.5577
Chart: Traffic rate/Gbps
| 0.1 | 3.5 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14 | 16 | 18 | 20 | 22
2 non-AP MLDs | 0.19974 | 6.9824 | 8.1027 | 15.0123 | 19.6703 | 22.9616 | 25.4602 | 27.4043 | 28.9793 | 31.3975 | 32.8893 | 34.2942 | 35.0681 | 35.1356 | 35.1077
4 non-AP MLDs | 0.39984 | 13.973 | 16.0045 | 23.5776 | 29.1083 | 32.4679 | 35.4538 | 37.4762 | 38.884 | 39.2018 | 39.416 | 39.3573 | 39.178 | 39.2449 | 39.3014
8 non-AP MLDs | 0.7992 | 27.8695 | 31.5976 | 39.9895 | 41.3457 | 41.5174 | 41.8953 | 41.3567 | 41.6605 | 41.9004 | 41.6343 | 41.7427 | 41.8355 | 41.4449 | 41.5577
Traffic rate is the packet generation ratio for all links at the transmitter.
In UL MU MIMO case, each affiliated non-AP STA is 4 NSS when the number of non-AP MLDs is 2. Similarly, 2 NSS for each affiliated non-AP STA when there are 4 non-AP MLDs and 1 NSS for each affiliated non-AP STA with total 8 non-AP MLDs.
Throughput increases with increasing traffic rate until it reaches the saturation due to the limited PHY data rate since the bandwidth, MCS and NSS are fixed.
Throughput increases with increasing number of non-AP MLD due to the transmission overhead in MU cases.
  Larger number of non-AP MLD reaches throughput saturation faster.

## Slide 9: Summary
The contribution provides simulation results to show how much throughput can be achieved by combining R1 features.
  Multi-Link, 4KQAM, 1024 Aggregation for A-MPDU, 320MHz bandwidth
Combining all four R1 features achieves 30Gbps for both SU and MU cases. Multi-Link with two links using 320MHz channels and 1024 aggregation for the UL MU case achieves 30Gbps throughput.
Generally, the impact on throughput for EHT features from lowest to highest is: 4KQAM, 1024 aggregation, 320MHz, Multi-Link. (i.e. Multi-Link achieves greater throughput gain when compared with 4KQAM).

## Slide 10: Reference
P802.11be (EHT) PAR - https://development.standards.ieee.org/myproject-web/public/view.html#pardetail/6886

## Slide 11: SP
Do you agree to resolve CID 7619 with the resolution shown on Slide 2?