## Slide 1: Threshold-based Local Reporting of Sensing Measurement
Date: 2021-11-xx
Authors:
–
Name | Affiliations | Address | Email
Oscar Au | Origin Wireless Inc. | 7500 Greenway Center Drive, Suite 1070, Greenbelt, MD 20770 USA | oscar.au@originwirelessai.com
Beibei Wang |  |  | beibei.wang@originwirelessai.com
K.J. Ray Liu |  |  | 
Hung-Quoc Lai |  |  | 

## Slide 2: Background
In our previous submission (xxxxr0),
we proposed “local” reporting of sensing measurement in the sensing receiver via an MLME primitive so that sensing measurement can be consumed locally in the sensing receiver.
According to specification framework SFD (0504r3),
a sensing receiver receives PPDUs sent by a sensing transmitter and performs sensing measurements in a sensing procedure.
the sensing receiver can use a sensing measurement reporting frame to report sensing measurements. We call this “nonlocal” reporting.

## Slide 3: Optional threshold-based (nonlocal) reporting
According to specification framework SFD (0504r3),
Optional threshold-based measurement and reporting procedure is defined such that sensing receiver would only send feedback using sensing measurement reporting frame (“nonlocal” reporting) when CSI variation is larger than a threshold.
Should this be used for local reporting of sensing measurement? Should it be optional? We try to address this in this proposal.

## Slide 4: Optional Threshold-based Local Reporting
We propose to extend the threshold-based procedure from nonlocal reporting to local reporting of sensing measurement.
Optional “threshold-based local reporting” to be defined for local reporting.
The optional “threshold-based local reporting” (and associated threshold) shall be selected/deselected by an MLME primitive.

## Slide 5: Straw Poll 1
Do you agree with the following statement?
  Assuming sensing measurements can be reported locally in sensing receiver,
  “Threshold-based local reporting” shall be applied to local reporting in the sensing receiver ,
  Threshold-based local reporting means a sensing measurement will be reported locally when “sensing measurement variation” is larger than a threshold.
Yes
No
Abstain

## Slide 6: Straw Poll 2
Assuming threshold-based local reporting can be applied in the sensing receiver, which manner should it be applied?
Optional
Mandatory
Abstain

## Slide 7: Straw Poll 3
Do you agree with the following statement?
  The threshold used in “threshold-based local reporting” shall be set via an MLME in the sensing receiver.
Yes
No
Abstain

## Slide 8: Straw Poll 4
Do you agree with the following statement?
  At least one “sensing measurement variation” (SMV) shall be available to “threshold-based local reporting”.
  One of the at least one SMV shall be selected via an MLME in the sensing receiver.
Yes
No
Abstain