## Slide 1: Selection of Nonlocal Reporting and Local Reporting
Date: 2021-11-19
Authors:
–
Name | Affiliations | Address | Email
Oscar Au | Origin Wireless Inc. | 7500 Greenway Center Drive, Suite 1070, Greenbelt, MD 20770 USA | oscar.au@originwirelessai.com
Beibei Wang |  |  | beibei.wang@originwirelessai.com
K.J. Ray Liu |  |  | 
Hung-Quoc Lai |  |  | 

## Slide 2: Background
In our previous submission (xxxxr0),
we proposed “local” reporting of sensing measurement in the sensing receiver via an MLME primitive so that sensing measurement can be consumed locally in the sensing receiver.
According to specification framework SFD (0504r3),
a sensing receiver receives PPDUs sent by a sensing transmitter and performs sensing measurements in a sensing procedure.
the sensing receiver can use a sensing measurement reporting frame to report sensing measurements. We call this “nonlocal” reporting.

## Slide 3: 4 Methods of Reporting of Sensing Measurement
Non-local reporting only. No local reporting.
  Good for centralized sensing system
Local reporting only. No non-local reporting.
  Good for fully distributed sensing system
Both local reporting and non-local reporting.
  Good for hybrid sensing system
None. No reporting. Reporting paused/stopped.
  Perhaps pause sensing measurement/session for privacy protection??
  But pausing can be achieved by terminating a measurement setup, and then resuming later by starting a new measurement setup.
  Not useful??

## Slide 4: Method 1 Reporting
Method 1: Non-local reporting only using sensing measurement report frame. No local reporting.
  All sensing measurement are transmitted elsewhere, consumed nonlocally.
  Useful in centralized sensing system, in which sensing responder does not participate in the consumption of the sensing measurement, i.e. it does NOT perform high level WLAN sensing computation (such as detecting/monitoring motion, breathing, fall down, etc).
  Significant network traffic, air-time, or resources spent on transmitting raw sensing measurements (e.g. CSI).
  Considerable time delay (for sensing initiator to collect all sensing measurements).
  Central computing. High computing/storage requirement for sensing initiator.
  Good for “cooperating” sensing receivers who are only willing to help to generate and send back sensing measurements.

## Slide 5: Method 2 Reporting
Method 2: Local reporting only. No non-local reporting.
  All sensing measurement consumed locally, not sent to sensing initiator.
  Useful in distributed case, in which each sensing receiver performs high level WLAN sensing computation (such as detecting/monitoring motion, breathing, fall down, etc) associated with the (local) sensing measurement.
  Sensing initiator serves to set up the sensing responders to form a WLAN sensing network. The sensing initiator may serve as a sensing transmitter or a sensing receiver.
  Sensing receivers may share the computed sensing result (require little network bandwidth, air-time or resource) with sensing initiator for fusion/further processing.
  Local computing. Lower computing/storage requirement than Method 1.
  NO network resources used to transmit demanding raw sensing measurements.
  Good for “partner” sensing receivers who will help to perform part of high level computing.

## Slide 6: Method 3 Reporting
Case 3: Both local reporting and non-local reporting.
  Sensing measurement consumed both locally and nonlocally.
  Useful in hybrid case, in which both the sensing responder and sensing initiator participate in the consumption of the sensing measurement, i.e. it shares some high level WLAN sensing computation with the sensing initiator.
  Similar to Method 1, significant network traffic, air-time, or resources spent on transmitting raw sensing measurements (e.g. CSI).
  Perform both centralized computing and distributed computing. Computational /memory requirement for sensing initiator similar to Method 1. Those for sensing receivers similar to Method 2.
  But hybrid cases are rare.

## Slide 7: Some “recipe” for central/distributed computing
Suppose an AP is sensing initiator and there are many IoT devices serving as sensing responders. (Or AP is requested to be a proxy.)
A “recipe” for central computing. AP uses TB sensing measurement by using TF to solicit NDP from the IoT devices such that measurement results are generated at the AP. Then local-only reporting is sufficient for central computing. No transmission of measurement results over the air.
A “recipe” for distributed computing. AP can use non-TB sensing measurement by sending NDPA+NDP to the IoT devices such that measurement results are generated at the IoT devices. Then local-only reporting is sufficient for distributed computing at the IoT devices. No transmission of measurement results over the air.

## Slide 8: Straw Poll 1
Which reporting should a sensing receiving support?
  (i) nonlocal reporting only, no local reporting,
  (ii) local reporting only, no nonlocal reporting,
  (iii) both local reporting and nonlocal reporting.
  Wherein Nonlocal reporting means transmission of sensing measurement results to sensing initiator using sensing measurement reporting frame
  Wherein Local reporting means reporting of sensing measurement results locally in sensing receiver via an MLME
Only (i), but not (ii) and (iii)
One of (i) and (ii), but not (iii)
One of (i), (ii) and (iii)
None of the above
Abstain

## Slide 9: Straw Poll 2
Do you agree with the following statement?
  Selection of local reporting and nonlocal reporting shall remain the same for measurement instances with the same measurement setup ID.
Yes
No
Abstain

## Slide 10: Straw Poll 3
At which granularity should local/nonlocal reporting be selected?
Session setup level (i.e. local/nonlocal reporting selection applied to ALL measurement setups in a session)
Measurement setup level (i.e. local/nonlocal reporting selection applied to ONE measurement setups)
Both (a) and (b) (i.e. 1 bit in session level to indicate session level or measurement setup level. Then select at corresponding level.)
Abstain