## Slide 1: Measurement Instance Sharing
Date: 2021-11-19
Authors:
–
Name | Affiliations | Address | Email
Oscar Au | Origin Wireless Inc. | 7500 Greenway Center Drive, Suite 1070, Greenbelt, MD 20770 USA | oscar.au@originwirelessai.com
Beibei Wang |  |  | beibei.wang@originwirelessai.com
K.J. Ray Liu |  |  | 
Hung-Quoc Lai |  |  | 

## Slide 2: Background
In our previous submission (xxxxr0),
we proposed “local” reporting of sensing measurement in the sensing receiver via an MLME primitive so that sensing measurement can be consumed locally in the sensing receiver.
According to specification framework SFD (0504r3),
a sensing receiver receives PPDUs sent by a sensing transmitter and performs sensing measurements in a sensing procedure.
the sensing receiver can use a sensing measurement reporting frame to report sensing measurements. We call this “nonlocal” reporting.

## Slide 3: Measurement Instance Sharing within a Session
According to SFD, one measurement instance is associated with one measurement setup.
However, it may be useful to associate a measurement instance with more than one measurement setups, with measurement performed using “shared” measurement setup
  E.g. two measurement setups with large amount of measurement instances coinciding
  E.g. two measurement setups that differs only in sounding frequency, F1 being a factor of F2 (e.g. 10Hz vs 20Hz, all other settings being identical). 30 instances/s => 20 instances/s
  E.g. two measurement setups that differs only in sounding frequency, with large greatest common factor (GCF) (e.g. 20Hz vs 30Hz, all other settings being identical, GCF=10). 20+30=50 instance/s => 40 instance/s. If GCF=N, instance saving=N.
  E.g. two measurement setups that differs in sounding frequency and number of antennas (e.g. 10 Hz/3 antennas vs 20Hz/2 antennas, “shared” measurement setup=3 antennas)
Sensing measurement sharing can reduce the total amount of measurement instances which implies less air time/bandwidth/network resources for sensing, less buffering memory, lower power, longer battery life, etc.

## Slide 4: Measurement Instance Sharing across Sessions
It may be useful to share measurement instances of different sensing sessions (e.g. diff. initiator-responder pairs), with measurement performed using “shared” measurement setup.
When initiator is an AP, and responders are IoT devices. Some “common”/“good” settings may likely be used by many IoT, causing their measurement setup parameters to be very similar. TB-based
  E.g. two measurement setups that differs only in sounding frequency, one being a factor of the other (e.g. smart TV wants 10Hz while smart speaker wants 20Hz, all other settings being identical)
  E.g. two measurement setups that differs in sounding frequency and number of antennas (e.g. smart TV wants 10 Hz for 3 antennas while smart speaker wants 20Hz for 2 antennas, “shared” measurement setup=3 antennas)
Sensing measurement sharing can reduce the total amount of measurement instances which implies less air time/bandwidth/network resources for sensing, less buffering memory, lower power, longer battery life, etc.

## Slide 5: Optional Measurement Instance Sharing
We propose to perform “measurement instance sharing” in an optional manner.
Sensing initiator shall negotiate with a sensing responder to enable or disable “measurement instance sharing”
Note:
If sensing initiator knows that it needs two or more measurement setups with significant “overlapping” sensing time, it can enable measurement instance sharing. Otherwise, it can disable it.
When sensing time for two measurement setups differ by less than a threshold, the corresponding two measurement instances can be marged/shared. The threshold is TBD.

## Slide 6: Sensing Measurement Sharing
We propose to allow sensing transmitter to associate a measurement instance with up to N measurement setup ID. The N is TBD. Among the N measurement setup ID, local/nonlocal reporting is performed in predefined order (e.g. increasing) of measurement setup ID. The predefined order is TBD.

## Slide 7: Straw Poll 1
Do you agree with the following statement?
  “Measurement instance sharing” shall be allowed in a sensing session,
  “Measurement instance sharing” allows an instantaneous (individual) measurement instance to be associated with N sensing measurement setup ID, and to perform the associated sensing measurement with an instantaneous “common” setup which enables the sensing measurement to satisfy all requirement/specification of the N sensing measurement setup ID.
  N>1. N is TBD.
Yes
No
Abstain

## Slide 8: Straw Poll 2
Should measurement instance sharing be optional or mandatory in a session?
  “Measurement instance sharing” shall be optional in a sensing session.
  “Measurement instance sharing” allows an instantaneous (individual) measurement instance to be associated with N sensing measurement setup ID, and to perform the associated sensing measurement with an instantaneous “common” setup which enables the sensing measurement to satisfy all requirement/specification of the N sensing measurement setup ID.
  N>1. N is TBD.
Yes
No
Abstain

## Slide 9: Straw Poll 3
Should measurement instance sharing be allowed across multiple sessions?
Yes
No
Abstain

## Slide 10: Straw Poll 4
Do you agree with the following statement?
  Sensing initiator shall negotiate with sensing responder in the sensing session setup to enable or disable “measurement instance sharing” in the sensing session.
  “Measurement instance sharing” allows an instantaneous (individual) measurement instance to be associated with N sensing measurement setup ID, and to perform the associated sensing measurement with an instantaneous “common” setup which enables the sensing measurement to satisfy all requirement/specification of the N sensing measurement setup ID.
  N>1. N is TBD.
Yes
No
Abstain

## Slide 11: Straw Poll 5
Do you agree with the following statement?
  Sensing initiator shall negotiate with sensing responder in the sensing session setup to enable or disable “measurement instance sharing” in the sensing session, and to select N if measurement instance sharing is enabled.
  “Measurement instance sharing” allows an instantaneous (individual) measurement instance to be associated with N sensing measurement setup ID, and to perform the associated sensing measurement with an instantaneous “common” setup which enables the sensing measurement to satisfy all requirement/specification of the N sensing measurement setup ID.
  N>1.
Yes
No
Abstain

## Slide 12: Straw Poll 6
Which set of choices would you prefer to be available for negotiation?
  Assume that sensing initiator will negotiate with sensing responder in the sensing session setup to choose one from a set of choices.
    Disable “Measurement instance sharing”
    Enable “Measurement instance sharing” with N=2
    Enable “Measurement instance sharing” with N=3
    Enable “Measurement instance sharing” with N=4
The set of choices are i and ii
The set of choices are i, ii and iii
The set of choices are i, ii, iii, and iv
None of the above
Abstain