## Slide 1: Time Stamping Measurement Results
Date: 2021-11-25
Authors:

## Slide 2: Abstract
Initial discussion on adding a Timestamp to Measurement Results

## Slide 3: Background
Use cases for sensing by Wi-Fi have been defined [1]. (Motion 7)
CSI is a type of measurement result for sub-7 sensing (Motion 20)
Results of measurement performed in a sensing session should be obtained by or reported to its initiator. (Motion 11)
A Sensing Measurement Report frame, which allows a sensing receiver to report sensing measurements, is defined. (Motion 21)
Transmission of the Sensing Measurement Report frame is initiated by an MLME primitive. Both immediate and delayed reporting are acceptable. (Motion 21)
In the reporting phase, measurement results from multiple measurement setups of a sensing responder may be included in a single measurement report frame for delayed reporting. (Motion 34)

## Slide 4: Time-Stamping Measurement Results
Time-of-measurement allows a sensing measurement to be “placed” in a system time frame
  Precise and accurate timestamps for a measurement can be provided to a sensing application
Time-of-measurement allows multiple sensing measurements from multiple sensing transmitters to be co-processed
  Multiple measurements of the same target likely to be more accurate or have greater integrity (multistatic approach)
  Multiple measurements of the same target from different angles allows novel processing such as 3-d location or 3-d visualization
  A time-stamp may allow multiple measurements to be propagated to a common time

## Slide 5: Time-Stamping Measurement Results
Periodic sensing measurements
  A sensing transmitter may schedule a periodic sensing transmission after a sensing setup phase and without a regular triggering procedure (for each sensing transmission).
  A time-stamp may allow jitter in the timing of the sensing transmission to be signaled or even compensated.
A proxy sensing initiator may be used which requests another device in the sensing network to initiate sensing measurements on its behalf [4]
  Measurement reports are forwarded by the sensing initiator to the proxy sensing initiator on a not-yet-determined timebase.
  Introduces another timing unknown variable.

## Slide 6: Time-Stamping Measurement Results
(Motion 21) A Sensing Measurement Report frame, which allows a sensing receiver to report sensing measurements, is defined. This new frame contains at least the following two fields:
  Measurement report control field: Contains information necessary to interpret the measurement report field.
  Measurement report field: Carries CSI measurements obtained by a sensing receiver.
A time-stamp may be added to either field which defines a time-of-validity of each CSI measurement
  If a Sensing Measurement Report contains multiple CSI measurements then the Measurement report field may be a more appropriate location.

## Slide 7: Available Timing References in IEEE 802.11
Requirement
  A common timing reference maintained within a Wi-Fi network. e.g., Within a Basic Service Set
Candidates
  Timing Synchronization Function (TSF)
    Available in all versions of 802.11
    Time synchronization between devices in a BSS is maintained by the existing Beacon messages
    Relatively low precision (1 μs)
  Fine Timing Measurement (FTM)
    Introduced in 802.11-2016
    High precision (0.1 ns)
    Designed to measure round trip time (RTT) and so does not require synchronization between devices
    Lack of synchronization means it cannot align measurements from sensing transmitters within a BSS/ESS

## Slide 8: Summary
Transmissions in an 802.11 network are not deterministic in time.
Some sensing algorithms require (or can be improved) by knowledge of when a sensing measurement was made.
Discussion of a time-stamp reflecting time-of-measurement for a sensing measurement result is presented.
Candidate timing references for the time-stamp are considered.

## Slide 9: SP1
Do you agree that:
  A timestamp reflecting a time-of-measurement shall be included as part of a Measurement Result for both MLME and the Sensing Measurement Report.
Y/N/A
Results: 18/7/17

## Slide 10: SP2
Which timing source shall be used to derive the time-stamp of the measurement:
  (A) Timing Synchronization Function (TSF)?
  (B) Fine Timing Mechanism (FTM)?
  (C) A new mechanism yet to be defined?
  (Abstain)
A/B/C/Abs.

## Slide 11: References
[1] 11-20-1712-02-00bf-wifi-sensing-use-cases
[2] 11-20-1851-04-00bf-overview-of-wi-fi-sensing-protocol
[3] 11-19-1850-00-SENS-wi-fi-sensing-technical-feasibility-standardization-gaps
[4] 11-21-1692-00-00bf-enhancing-client-based-sensing-sensing-by-proxy