## Slide 1: Collaborative WLAN Sensing – Definition and Operational Scenarios
Date: 2021-11-xx
Authors:
November, 2021
Name | Affiliation | Address | Phone | Email
Sang Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | sanggook.kim@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
WLAN sensing has drawn increasing attention due to its potential enormous opportunities to create many applications such as in home security, health care, enterprise, and building automation/management markets, etc. [1 – 9]
In [6] and [7], the importance of cooperating multiple STAs in terms of performance are noted.
In [8] and [9], we considered the WLAN sensing in which multitude of Wi-Fi devices are involved and collaborated termed as “collaborative WLAN sensing” and possible benefits are also addressed in addition to overhead to achieve them.
In this contribution, we propose the definition and operational scenarios for collaborative WLAN sensing .
November, 2021

## Slide 3: Brief Recap
Configurations:
Sensing
Initiator (AP)
Sensing
Responder 2
Sensing
Responder 1
Example configuration: One initiator (AP) and two responders.
AP is triggering the sensing transmissions and
requesting feedbacks.
Sensing transmission and feedback may be measurement instance-based [3] when a session consists of multiple measurement instances.
Illustration is based on measurement instance-based.
Each measurement instances has sensing measurement and feedback phases.
A WLAN sensing procedure may be comprised of multiple sensing measurement instances (Motion 14).
November, 2021

## Slide 4: Brief Recap (Cont’d)
Configurations:
Sensing
Initiator (AP)
Sensing
Responder 2
Sensing
Responder 1
1st measurement instance: Transmission
Initiator transmits and two responders receive.
Available channel information: Initiator to responder 1 and
initiator to responder 2
Sensing
Initiator (AP)
Sensing
Responder 2
Sensing
Responder 1
1st measurement instance: Feedback
Two responders feedback the measurements to initiator.
Sensing
Transmitter
Sensing
Receiver
Sensing
Receiver
November, 2021

## Slide 5: Brief Recap (Cont’d)
Configurations:
Sensing
Initiator (AP)
Sensing
Responder 2
Sensing
Responder 1
Sensing
Initiator (AP)
Sensing
Responder 2
Sensing
Responder 1
2nd measurement instance: Transmission
Responder 1 transmits, initiator and responder 2 receive.
Available channel information: Responder 1 to initiator and
responder 1 to responder 2.
2nd measurement instance: Feedback
Responder 2 feedbacks channel measurement between responder 1 and itself to initiator.
Sensing
Receiver
Sensing
Transmitter
Sensing
Receiver
November, 2021

## Slide 6: Rationale:
In 11bf PAR [10], the following is described:
  This amendment enables:
  Stations to perform one or more of the following: to inform other stations of their WLAN sensing capabilities, to request and setup transmissions that allow for WLAN sensing measurements to be performed, to indicate that a transmission can be used for WLAN sensing, and to exchange WLAN sensing feedback and information,
Stations in the above description can be AP and/or Non-AP STA.
  Non-AP STA may be acted as an initiator.
  Sensing transmission from non-AP STA to non-AP STA is not precluded.
November, 2021

## Slide 7: Rationale (Cont’d)
Through measurement campaigns, the importance of diversity transmission and reception was noted [6]:
  “Wi-Fi sensing may be improved with TX STA and RX STA diversity, which requires standard support”.
Full benefits of diversity transmission and reception will be obtained through the sensing procedure in which all STAs are involved in the transmission and reception.
  The transmission and reception among STAs should be coordinated. Otherwise, the benefits will be diminished.
  We term the coordinated WLAN sensing procedure with multiple STAs as “Collaborative WLAN Sensing”.
November, 2021

## Slide 8: Different Role Configuration by Multiple Measurement Setup IDs
Role of STAs as a transmitter and/or receiver during collaborative sensing may be configured by multiple measurement setup IDs:
  Each Measurement Setup ID corresponds to an attribute such as which STA is a transmitter and/or receiver.
  Multiple role configurations in parallel and one role configuration per measurement setup ID.
  Role of the STAs per Measurement Setup ID are fixed.
  Measurement Setup IDs may be determined during sensing session setup or measurement setup and delivered using elements in a frame (new or existing).
November, 2021

## Slide 9: Different Role Configuration by Multiple Measurement Setup IDs: Example
Assume that an AP and 3 non-AP STAs (STA 1, STA 2, and STA 3).
4 Measurement Setup IDs:
  Measurement Setup ID 1: TX: AP, RX: STA 1, STA 2, and STA 3.
  Measurement Setup ID 2: TX: STA1, RX: AP and STA 2.
  Measurement Setup ID 3: TX: STA 2, RX: STA 1 and AP.
  Measurement Setup ID 4: TX: STA 3, RX: STA 1, STA 2, and AP.
November, 2021

## Slide 10: Definition of Collaborative WLAN Sensing
Following motion has been incorporated into SFD:
  A WLAN sensing procedure may be comprised of multiple sensing measurement instances [Motion 14]
  More than one sensing responder may participate in a sensing measurement instance [Motion 16].
  The Measurement Setup ID may be used to identify attributes of the sensing measurement instances [Motion 24].
In lieu of aforementioned motion, we may define collaborative WLAN sensing as:
  WLAN sensing in which a sensing procedure may be comprised of multiple sensing measurement setups over which the same set of more than one sensing responder STAs is maintained, but their participation and/or roles as a transmitter and a receiver for a measurement instance may be configured by multiple measurement setup IDs in coordinated way.
  The same set of AID and/or UID is maintained in collaborative sensing.
  Multiple measurement setup IDs may be maintained until explicitly or implicitly terminated.
November, 2021

## Slide 11: Operational Scenarios
Sensing session may be initiated by AP or Non-AP STA.
Sensing session may be consisted of STAs associated or some non-associated.
For initial consideration, we confine ourselves to AP-initiated with associated STAs:
  AP as an initiator and Non-AP STAs as responders.
  AP and Non-AP STAs as transmitter and/or receiver.
Although AP-initiated sensing procedures are considered so far, Non-AP initiated sensing procedures cannot be excluded due to its potential use cases and benefits.
Consideration of other operational scenarios is TBD.
November, 2021

## Slide 12: Operational Scenarios (Cont’d):
Multiple STAs know their roles at each measurement instance (i.e., transmitter or receiver).
  This will be decided during the negotiation phase.
Multiple responding STAs deliver measurement results to AP.
  Measurement result between non-AP STAs may be delivered to AP.
  Non-AP STA acted as a receiver in non-AP to non-AP transmission may deliver the measurement result to AP.
November, 2021

## Slide 13: Summary
WLAN sensing has drawn increasing attention due to its possible and potential opportunities to create many applications such as in home security, health care, enterprise, and building automation/management markets, etc.
In this contribution, we proposed the definition of collaborative sensing and operation scenario under consideration.
November, 2021

## Slide 14: References
[1] Wi-Fi Sensing – A New Technology Emerges. v1.0, October 2019, Wireless Broadband Alliance (https://wballiance.com/wba-wi-fi-sensing/)
[2] 11-20/1239r0, Use Cases for Wireless LAN Sensing.
[3] 11-20/1232r0, Overview of WLAN sensing protocol.
[4] 11-20/1805r0, Discussion on WLAN Sensing Roles.
[5] 11-20/1804r0, Discussion on WLAN Sensing Procedure.
[6] 11-19/1416r0, Wi-Fi Sensing: Cooperation and Standard. Support.
[7] 11-19/1551r1, Wi-Fi Sensing in 60GHz band: Usage models, Performance and What is need in 802.11 Standard
[8] 11-20/1533r0, Collaborative WLAN Sensing.
[9] 11-21/0644r4, Sensing session and measurement exchange identification
[10] IEEE 802.11-19/2103r12, 802.11 SENS SG Proposed PAR
November, 2021

## Slide 15: SP #1
Do you support to adopt the following definition of collaborative WLAN sensing into SFD:
  WLAN sensing in which a sensing procedure may be comprised of multiple sensing measurement setups over which the same set of more than one sensing responder STAs is maintained, but their participation and/or roles as a transmitter and a receiver for a measurement instance may be configured by multiple measurement setup IDs in coordinated way.
  The same set of AID and/or UID is maintained in collaborative sensing.
  Multiple measurement setup IDs may be maintained until explicitly or implicitly terminated.
November, 2021