## Slide 1: Discussion on Session Setup
Date: 2021-11-29
Authors:
Chaoming Luo (OPPO)
Name | Affiliation | Address | Phone | Email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Lei Huang |  |  |  | 
Pei Zhou |  |  |  | 

## Slide 2: Introduction
The SFD states that a sensing session is an agreement between a sensing initiator and a sensing responder to participate in a WLAN sensing procedure. [1]
This contribution discusses more about the detail of session setup procedure and frame formats.

## Slide 3: Overview and focus
WLAN Sensing procedure may comprise of several phases [1].
This contribution focus on Sensing Discovery and Sensing Session Setup.
Sensing Initiator
Sensing Responder
Sensing Measurement Setup
Sensing Measurement Instances
Sensing Measurement Setup Termination
Sensing Session Setup
Sensing Session Termination
Sensing Discovery

## Slide 4: Recap: Sensing Session Setup
Sensing Session setup in SFD:
  In the sensing session setup of a WLAN sensing procedure, a sensing session is established, and operational parameters associated with the sensing session are determined and may be exchanged between STAs.
  A sensing session is pairwise and is identified by MAC addresses and/or associated AID/UID.
  A sensing initiator may maintain multiple sensing sessions.

## Slide 5: Discussion: What is Sensing Session Setup?
If AP is involved in sensing measurement, then every session is an < non-AP, AP> session.
  3 typical cases shown below
Are there any possible operational parameters should be exchanged in session setup?
  No session specific operational parameter has been identified yet.
  Operational attributes are exchanged in measurement setup.
Proposal: session setup exchanges only the sensing capabilities.
case A
case B
case C

## Slide 6: Discussion: Sensing Discovery
In Discovery phase, the non-AP STA should know the essential sensing capabilities of the AP (e.g., whether the AP supports sensing or not), via Probe Response/Beacon.
  If the AP does not support sensing, then the non-AP STA should not initiate the sensing session setup.
In Discovery phase, the non-AP STA may report the essential sensing capabilities (e.g., whether the non-AP STA supports sensing or not) to the AP, via Probe Request.
  If the non-AP STA does not support sensing, then it should not initiate the sensing session setup.

## Slide 7: Discussion: Sensing Session Setup
For associated sensing capable STAs, it may initiate the session setup during the association (via (Re)Association Request/Response), or after the association (using new Public Action frames).
  Drawbacks of using (Re)Association Request/Response:
    Information may not be protected.
    Not applicable for unassociated STAs.
For unassociated sensing capable STAs, it may initiate the session setup procedure immediately after PASN, using new Public Action frames.
Proposal:
  Define a new Sensing Capabilities element or reuse Extended Capabilities element to carry sensing capability information.
  This IE may be used in (Re)Association Request and (Re)Association Response frames for associated STAs.
  This IE may be used in new Action frames for associated or unassociated STAs.

## Slide 8: Discussion: Sensing Capability Information
Sensing capability information may include:
  sensing measurement result types supported, e.g., CSI
  support of sensing receiver role
  support of sensing transmitter role
  support of sensing initiator role
  support of sensing responder role
    support of TB sensing responder role (for non-AP STA only)
    support of non-TB sensing responder role (may be for AP only)
  support of SBP procedure
    Support of SBP requester role (for non-AP STA only)
    Support of SBP responder role (for AP only)
  support of threshold based sensing
  support of aggregated reporting
    support of aggregated reporting as a initiator
    support of aggregated reporting as a receiver
Other capability information is TBD.

## Slide 9: Proposal: Session Setup Request/Response Frame
Public Action frame
  Sensing Subtype field indicates session setup request or response
Sensing Capabilities Info element carries sensing capability of the transmitting STA.
  Sensing Capabilities Info element can be a newly defined Sensing Capabilities element or the existing Extended Capabilities element.

## Slide 10: SP 1
Do you agree to add the following into 11bf SFD ?
  Sensing session setup exchanges only the sensing capabilities between the < non-AP, AP> pair.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 11: SP 2
Do you agree to add the following into 11bf SFD ?
  The element carrying sensing capabilities can be included in (Re)Association Request and (Re)Association Response frames for associated STAs, and can also be included in new Sensing Session Setup Request/Response frames for associated or unassociated STAs.
  Whether this element is a new Sensing Capabilities element or Extended Capabilities element is TBD.
  Note: Sensing Session Setup Request/Response frames are Public Action frames, format is TBD.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 12: Reference
[1] 11-21-0504-03-00bf-specification-framework-for-tgbf
[2] 11-21-1828-01-00bf-Mesurement setup frame formats
Chaoming Luo (OPPO)