## Slide 1: Discussion on Session Setup
Date: 2021-11-29
Authors:
Chaoming Luo (OPPO)
Name | Affiliation | Address | Phone | Email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Lei Huang |  |  |  | 
Pei Zhou |  |  |  | 

## Slide 2: Introduction
The SFD states that a sensing session is an agreement between a sensing initiator and a sensing responder to participate in a WLAN sensing procedure. [1]
This contribution discusses more about the detail of session setup procedure and frame formats.

## Slide 3: Overview and focus
WLAN Sensing procedure may comprise of several phases [1].
This contribution focuses on Sensing Discovery and Sensing Session Setup.
Sensing Initiator
Sensing Responder
Sensing Measurement Setup
Sensing Measurement Instances
Sensing Measurement Setup Termination
Sensing Session Setup
Sensing Session Termination
Sensing Discovery

## Slide 4: Recap: Sensing Session Setup
Sensing Session setup in SFD:
  In the sensing session setup of a WLAN sensing procedure, a sensing session is established, and operational parameters associated with the sensing session are determined and may be exchanged between STAs.
  A sensing session is pairwise and is identified by MAC addresses and/or associated AID/UID.
  A sensing initiator may maintain multiple sensing sessions.

## Slide 5: Discussion: What is Sensing Session Setup?
If AP is involved in sensing measurement, then every session is an < non-AP, AP> session.
  3 typical cases shown below
Are there any possible operational parameters should be exchanged in session setup?
  No session specific operational parameter has been identified yet.
  Operational attributes are exchanged in measurement setup.
Proposal: session setup is used to exchange the sensing capabilities.
case A
case B
case C

## Slide 6: Discussion: Discovery
Case 1: A non-AP STA broadcasts probe request due to any of the following reasons
  Finds another BSS to join (or catalog for roaming later), mostly because of communication.
  Finds an AP that supports SBP responding STA role, because the non-AP STA need an proxy to initiate sensing for it.
  Finds an AP that supports responder role, because the non-AP STA wants to initiate a non-TB sensing procedure.
  Finds an AP that supports sensing.
Case 2: A non-AP STA retrives information of an AP from Beacon. The non-AP STA may broadcast/unicast probe request to get more information.
  Information in Beacon could help the non-AP STA to hurry up the discovery process.

## Slide 7: Discussion: associated STAs
Sensing session setup for associated sensing capable STAs:
  Sensing capabilities are exchanged via Probe Request /Response, and/or (Re)Association Request/Response
  Communication capabilities and parameters are exchanged via Probe Request /Response, and (Re)Association Request/Response
AID of the STA is allocated by AP and sent to the STA in (Re)Association Response
  Note: to have a unified measurement setup (denoted as MS) request frame, AP may also send AID of the STA in MS request again. e.g., AP sends MS request to associated STA 1, carries AID1 of STA1 (AID1 was assigned during association)

## Slide 8: Discussion: unassociated STAs
Sensing session setup for unassociated sensing capable STAs:
  Sensing capabilities are exchanged via Probe Request /Response
  Communication capabilities and parameters are exchanged via Probe Request /Response
UID of the STA is allocated by AP and sent to the STA in measurement setup request
  AP initiated measurement setup: UID is in every measurement setup request, STA could reject if mismatch.
    e.g., AP sends MS request to unassociated STA 2, carries the UID2 assigned to STA 2.
  Non-AP initiated measurement setup: only one unassociated STA, no UID is needed.
    e.g., (associated or unassociated) STA 3 sends MS request to AP, carries AID of AP (it's always 0).

## Slide 9: Discussion: Invitation of sensing
Propose some more information in the unicast Probe Response:
  Invitation of STA to join a sensing measurement as a sensing responder
    The element carries this indication is TBD
    This indication could help the STA to be prepared for a subsequent sensing measurement setup, e.g.,
      Start the association procedure
      Or stand by for a predefined time to receive measurement setup request if the STA does not intend to associate.
      Or start the PASN procedure immediately if the STA does not intend to associate, and then stand by for a predefined time to receive measurement setup request
  Existing MFPR in RSNE and a new USNM-MFPR in RSNXE may be used for indication of frame protection.
    11az set MFPR and URNM-MFPR (Unassociated Ranging Negotiation and Measurement Management Frame Protection Required) to 1 if dot11RSTARequiresPMFActivated is true.

## Slide 10: Discussion: Example 1
Example 1 – unassociated STA wants to join as a sensing responder:
  AP invites STA2 to join a sensing measurement as a sensing responder, and carries such an invitation in unicast Probe Response;
  STA2, which does not intend to associate with the AP but wants to join as a sensing responder, stands by and optionally initiates PASN with the AP;
  The AP initiates measurement setup with STA2 within a predefined timeout. And the AP assigns UID to STA2 in the measurement setup request.

## Slide 11: Discussion: Example 2
Example 2 - unassociated STA wants to be a sensing initiator:
  STA2, which does not intend to associate with the AP, may initiates PASN and measurement setup with the AP no matter the invitation is 1 or 0, if STA2 wants to become an initiator knowing the AP can be a responder.
  Howerver, if both AP and STA2 can be initiators and responders, and the invitation is 1, it doesn’t matter which one starts the measurement setup request first, both exchanges should be treated as independent measurement setup.

## Slide 12: Discussion: Sensing Capability Information
Sensing capability information is carried in Sensing Capabilities element and include:
  sensing measurement result types supported, e.g., CSI, TCIR
  support of sensing receiver role
  support of sensing transmitter role
  support of sensing initiator role
  support of sensing responder role (Note to editor: replace it with its sub-bullets)
    support of TB sensing responder role (for non-AP STA only)
    support of non-TB sensing responder role (may be for AP only)
  support of SBP procedure (Note to editor: replace it with its sub-bullets)
    Support of SBP requester role (for non-AP STA only)
    Support of SBP responder role (for AP only)
  support of threshold based sensing
  support of aggregated reporting (Note to editor: replace it with its sub-bullets)
    support of aggregated reporting as a initiator
    support of aggregated reporting as a receiver
    Note: refer to motion 34 for the exact meaning of these two capabilities.
Other capability information is TBD.

## Slide 13: SP 1
Do you agree to add the following into 11bf SFD ?
  Probe request/response frame exchange can be used for sensing session setup between an AP and a non-AP STA intended not to be associated with the AP.
  Probe request/response frame exchange and (Re)association request/response frame exchange can be used for sensing session setup between an AP and a non-AP STA intended to be associated with the AP.
  The examples and figures in slide 10 and 11 are included as examples of sensing session setup.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 14: SP 2
Do you agree to add the following into 11bf SFD ?
  Unicast Probe Response frame comprises the following field:
    Invitation of responder for sensing (1 bit), which indicates whether or not to invite an intended STA to join a sensing measurement as a sensing responder.
  The element carrying the field is TBD.
  A constant timeout is defined, which indicates the AP may initiate measurement setup with the unassociated STA within the timeout after the Probe Response. The value of the timeout is TBD.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 15: SP 3
Do you agree to add the following into 11bf SFD ?
  A Sensing Capabilities element is defined, which carries sensing capability information as shown in slide 12.
  Other sensing capability information is TBD.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 16: SP 4
Do you agree to add the following into 11bf SFD ?
  Measurement setup request frame includes an AID/UID field. The AID/UID field indicates the AID/UID assigned to the intended non-AP STA by the AP, or the AID of the intended AP.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 17: SP 5
Do you agree to add the following into 11bf SFD ?
  An USNM-MFPR (Unassociated Sensing Negotiation and Measurement Management Frame Protection Required) field, which specifies whether sensing frames are required to be protected without association, is defined in the RSNXE.
  dot11SensingRequiresPMFActivated is defined as a MIB variable. When true, it indicates that the station requires Management Frame Protection for all management frames exchanged during the negotiation and sensing measurement procedure.
  A STA sets the USNM-MFPR field to 1 if dot11SensingRequiresPMFActivated is true. Otherwise the STA sets the USNM-MFPR field to 0.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 18: Reference
[1] 11-21-0504-03-00bf-specification-framework-for-tgbf
[2] 11-21-1828-03-00bf-mesurement-setup-frame-formats
Chaoming Luo (OPPO)

## Slide 19: Backup: Example 3
Example 3 – STA intends to associate with the AP:
  Probe Request/Response might be one the approaches before association, and the invitation is not the condition for the association.
  However, if STA2 can be a responder, and the invitation is 1, STA2 may get better prepared for the upcoming measurement setup initiated by the AP.