## Slide 1: Discussion on Session Setup
Date: 2022-4-13
Authors:
Chaoming Luo (OPPO)
Name | Affiliation | Address | Phone | Email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Lei Huang |  |  |  | 
Pei Zhou |  |  |  | 

## Slide 2: Introduction
The SFD states that a sensing session is an agreement between a sensing initiator and a sensing responder to participate in a WLAN sensing procedure. [1]
This contribution discusses more about the detail of session setup procedure and frame formats.

## Slide 3: Overview and focus
WLAN Sensing procedure may comprise of several phases [1].
This contribution focuses on Sensing Session Setup.
Sensing Initiator
Sensing Responder
Sensing Measurement Setup
Sensing Measurement Instances
Sensing Measurement Setup Termination
Sensing Session Setup
Sensing Session Termination
Sensing Discovery

## Slide 4: Abstract
Sensing Session is an agreement between a non-AP STA and an AP to allow the establishment of forthcoming measurement setups (denoted as MS).
Upon a successful Sensing Session Setup, both sides know and store the parameters, including AID/UID and mutual sensing capabilities. At Sensing Session Termination, the resources that keep the parameters get released. The whole procedure is discussed.
  Associated STA (denoted as A-STA): A sensing session is established implicitly after 4-way HS, and is terminated implicitly when disassociation.
  Unassociated STA (denoted as U-STA): After PASN, an exchange of MS Query by non-AP STA and MS Request by AP establishes a sensing session. The session may be terminated implicitly when timeout, or explicitly by MS Termination.
Note:
  We mainly discuss the case of U-STAs in this contribution.
  Please keep in mind that U-STAs may go away or enter power save mode at any time, while the AP may not know about this.

## Slide 5: Discussion: Essential Sensing Capabilities
Essential Sensing capabilities are carried in Extended Capabilities element and includes:
  support of WLAN Sensing (in D0.01)
    support of TB measurement procedure (TBD)
    support of non-TB measurement procedure (TBD)
    support of STA-STA measurement procedure (TBD)
  support of SBP procedure (in D0.01)
    Note: Support of SBP procedure for a non-AP STA means the non-AP STA supports SBP initiator role
    Note: Support of SBP procedure for an AP means the AP supports SBP responder role
Other sensing capabilities in Extended Capabilities element are TBD.

## Slide 6: Discussion: Detailed Sensing Capabilities
Detailed sensing capabilities are carried in Sensing Capabilities element and includes:
  sensing measurement result types supported, e.g., CSI, TCIR
  support of sensing receiver role
  support of sensing transmitter role
  support of sensing initiator role
  support of sensing responder role (Note to editor: replace it with its sub-bullets)
    support of TB sensing responder role (for non-AP STA only)
    support of non-TB sensing responder role (whether it’s for AP only is TBD)
  support of threshold based sensing
  support of reporting
  support of aggregated reporting (Note to editor: replace it with its sub-bullets)
    support of aggregated reporting as a sensing initiator
    support of aggregated reporting as a sensing receiver
    Note: refer to motion 34 for the exact meaning of these two capabilities.
Other capabilities in Sensing Capabilities element are TBD.

## Slide 7: session setup
Beacon and Probe Response shall carry AP’s detailed capabilities, in case U-STA wants to be an initiator.
session established before T1 expires.
Predefined session timeout T2: both sides reset the timer after each successful sensing handshake, and clear session related resources if T2 expires. The definition of sensing handshake is TBD.
Predefined frame exchange timeout T1: it’s a time limit the AP STA shall respond with the MS Request/Termination. The U-STA does not wait for the MS Request/Termination for a longer time than T1 after it delivers the MS Query frame.
  Note: this is the same as the timeout used in the exchange of MS Request and MS Response.

## Slide 8: session setup-cont.
If the AP is not ready to initiate MS with the U-STA in T1, it may tell the U-STA to comeback later. The U-STA may resend MS Query frame at least once before T2 expires, or the U-STA may just go away and will not comeback to resend a MS Query.
session established before T2 expires.
No, I don’t need you now, but maybe later.

## Slide 9: session setup-cont.
If the AP does not want the U-STA, it may kick the U-STA out and the session setup fails.
Session termination: this bit is set to one when used to terminate a session between an U-STA and an AP. It is set to zero when the MS Termination frame is used to terminate one or more or all MSs while the session keeps alive.

## Slide 10: more MS
Please hold on and send me an MS Query after the instance, I may initiate a frame exchange with you.
If the AP want to initiate a new MS or terminate existing MS or terminate the session with the U-STA, it may carry the indication in the Polling TF within a measurement instance.

## Slide 11: session termination
Case 1: An U-STA may terminate the established sensing session using a MS Termination frame.

## Slide 12: session termination-cont.
Case 2: The AP may also terminate the established sensing session.
Please hold on and send me an MS Query after the instance, I may initiate a frame exchange with you.
Well, unfortunately I don’t need you anymore.
I’m awake now.

## Slide 13: SP 1
Do you agree to add the following into 11bf SFD?
  An MS Query frame is defined.
    An unassociated STA (denoted as U-STA) transmits the measurement setup (denoted as MS) Query frame to solicit an MS Request frame from an AP.
      The MS Query frame may contain the detailed sensing capabilities of the U-STA.
    The AP responds with the MS Request frame to the U-STA.
      The MS Request frame contains the UID assigned to the U-STA.
      The MS Request frame contains one bit to inform the U-STA to comeback before session timeout expires to solicit an MS Request frame.
    The AP can also send a MS Termination frame to the U-STA, which contains one bit indicating termination of the sensing session.
  The Polling TF within a measurement instance contains one bit to inform the U-STA to transmit an MS Query frame outside the measurement instance.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 14: SP 2
Do you agree to add the following into 11bf SFD?
  The timeout (value is TBD) used in the exchange of MS Request and MS Response is reused as a timeout T1, which is the time limit the AP shall respond with the MS Request. The U-STA does not wait for the MS Request for a longer time than T1 after it delivers the MS Query frame.
  A session timeout T2 is predefined (value is TBD), which is the time limit the U-STA and the AP keep the agreed UID, mutual capabilities, and PASN keys (TBD). The timer for T2 is restarted at each successful handshake between the U-STA and the AP. The definition of sensing handshake is TBD.
  The U-STA should transmit the MS Query frame at least once before T2 expires.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 15: SP 3
Do you agree to add the following into 11bf SFD?
  Sensing Session is an agreement between a non-AP STA and an AP to allow the establishment of forthcoming measurement setups.
  Upon a successful Sensing Session Setup, both sides know and store the parameters, including AID/UID and mutual sensing capabilities. At Sensing Session Termination, the resources that keep the parameters get released.
  For an associated STA, a sensing session is established implicitly after 4-way HS, and is terminated implicitly when disassociation.
  For an unassociated STA, after PASN, if there is, an exchange of MS Query by non-AP STA and MS Request by AP establishes a sensing session. The session may be terminated implicitly when timeout, or explicitly by an MS Termination frame.
  The figures shown in slide 7, 8, 9, 10, 11, 12 are included as examples.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 16: SP 4
Do you agree to add the following into 11bf SFD ?
  The Extended Capabilities element carries essential sensing capabilities as shown in slide 5.
  A Sensing Capabilities element is defined, which carries detailed sensing capabilities as shown in slide 6.
  Other sensing capability information is TBD.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 17: Reference
[1] 11-21-0504-03-00bf-specification-framework-for-tgbf
[2] 11-21-1828-03-00bf-mesurement-setup-frame-formats
Chaoming Luo (OPPO)

## Slide 18: Backup: capability exchange
Case 1: A non-AP STA broadcasts probe request due to any of the following reasons
  Finds another BSS to join (or catalog for roaming later), mostly intend for communication.
  Finds an AP that supports SBP responding STA role, because the non-AP STA needs an proxy to initiate sensing procedure for it.
  Finds an AP that supports responder role, because the non-AP STA wants to initiate a non-TB sensing procedure.
  Finds an AP that supports sensing.
Case 2: A non-AP STA retrives information of an AP from Beacon. The non-AP STA may broadcast/unicast probe request to get more information.
Case 3: A non-AP STA exchanges capability information with AP using Associate Request/Response.

## Slide 19: Option 1: session setup
Session timeout T2: both sides reset the timer after ANY successful sensing frame exchange, and clear session related resources if T2 expires.
An unified sequence for session setup

## Slide 20: Option 1: first MS case 1
The U-STA may send a MS Query frame just after the sensing session setup to trigger the first MS.
Predefined timeout T1: both sides reset the timer after successful MS Query frame exchange. U-STA may go to sleep if T1 expires w/o receiving MS request.
An unified sequence for MS initiated by the AP with the U-STA

## Slide 21: Option 1: first MS case 2
The AP may not ready to start a MS with an U-STA just after session setup. The U-STA may go to power save mode. And before T2 expires, the U-STA may repeat MS Query frame at least once to trigger the first MS.

## Slide 22: Option 1: more MS
The AP may also telling the U-STA to hold on after a measurement instance and send the MS Query frame to trigger a new MS.

## Slide 23: Option 1: session termination
Case 1: An U-STA may terminate the sensing session actively by sending a Sensing Session Termination frame.
Case 2: The AP may terminate the sensing session by telling the U-STA to trigger.

## Slide 24: Comparision
Chaoming Luo (OPPO)
 | Pros. | Cons. | Notes
Option 1 | Separate and unified procedure Functionality of each frame is simple and clear. Session Setup Reponse carries AP’s detailed capabilities, which could be protected. | Four new Action frames (Session Setup Request, Session Setup Response, MS Query, Session Termination) Separate frame exchange for session setup. Separate frame exchange for session termination. | 
Option 2 | One new Action frame (MS Query) Reduce frame exchange for session setup. May reduce frame exchange for session termination. | The procedure is combined and a little bit complex. Three frames (MS Request, MS Query, Polling TF) have the same functionality of session termination. These frames have multiple functionalities and cause confusion. Beacon/Probe Response has to carry AP’s detailed capabilities, which is unprotected. |