## Slide 1: Discussion on Session Setup
Date: 2022-4-25
Authors:
Chaoming Luo (OPPO)
Name | Affiliation | Address | Phone | Email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Lei Huang |  |  |  | 
Pei Zhou |  |  |  | 

## Slide 2: Introduction
The SFD states that a sensing session is an agreement between a sensing initiator and a sensing responder to participate in a WLAN sensing procedure. [1]
This contribution discusses more about the detail of session setup procedure and frame formats.

## Slide 3: Overview and focus
WLAN Sensing procedure may comprise of several phases [1].
This contribution focuses on Sensing Discovery and Sensing Session Setup.
Sensing Initiator
Sensing Responder
Sensing Measurement Setup
Sensing Measurement Instances
Sensing Measurement Setup Termination
Sensing Session Setup
Sensing Session Termination
Sensing Discovery

## Slide 4: Abstract
Sensing Capability Exchange is the exchange of sensing capabilities (essential and detailed) between a STA and an AP.
Sensing Session is removed, correspondingly Sensing Session Setup and Sensing Session Termination phases are removed.
  No session specific operational parameter has been identified yet.
Typical procedures for associated STA (denoted as A-STA) and unassociated STA (denoted as U-STA) are illustrated, including:
  Sensing Capability Exchange, Measurement Setup (denoted as MS), MS Termination.
Note:
  Please keep in mind that U-STAs may go away or enter power save mode at any time, while the AP may not know about this.

## Slide 5: Discussion: Essential Sensing Capabilities
Essential Sensing capabilities are carried in Extended Capabilities element and includes:
  support of WLAN Sensing (in D0.01)
    support of TB measurement procedure (TBD)
    support of non-TB measurement procedure (TBD)
    support of STA-STA measurement procedure (TBD)
  support of SBP procedure (in D0.01)
    Note: Support of SBP procedure for a non-AP STA means the non-AP STA supports SBP initiator role
    Note: Support of SBP procedure for an AP means the AP supports SBP responder role
Other sensing capabilities in Extended Capabilities element are TBD.

## Slide 6: Discussion: Detailed Sensing Capabilities
Detailed sensing capabilities are carried in Sensing Capabilities element and includes:
  sensing measurement result types supported, e.g., CSI, TCIR
  support of sensing receiver role (TBD)
  support of sensing transmitter role (TBD)
  support of sensing initiator role (TBD)
  support of sensing responder role (Note to editor: replace it with its sub-bullets) (TBD)
    support of TB sensing responder role (for non-AP STA only)
    support of non-TB sensing responder role (whether it’s for AP only is TBD)
  support of threshold based sensing
  support of reporting
    Note: refer to motion 60 for the exact meaning of optional reporting.
  support of aggregated reporting (Note to editor: replace it with its sub-bullets)
    support of aggregated reporting as a sensing initiator
    support of aggregated reporting as a sensing receiver
    Note: refer to motion 34 for the exact meaning of these two capabilities.
Other capabilities in Sensing Capabilities element are TBD.

## Slide 7: A-STA: MS case 1
Sensing Capability Exchange
Predefined frame exchange timeout T1: timeout used in the exchange of MS Request and MS Response (already in D0.1).
AP may initiates an MS at anytime.
Possibly 4-way handshake (Ref: clause 12.7.6) is excuted.

## Slide 8: A-STA: MS case 2
A-STA may initiates an MS at anytime.

## Slide 9: A-STA: MS Termination
A sensing initiator (or sensing responder) may initiate termination of one or more sensing measurement setups. (Already in D0.1)

## Slide 10: U-STA: MS case 1
Sensing Capability Exchange
AP may initiates the first MS before T1 expires.
PASN may be excuted.
I need you to join my MS.
Predefined session timeout T2: both sides reset the timer after each successful sensing handshake, and clear session related resources if T2 expires. The definition of sensing handshake is TBD.

## Slide 11: U-STA: MS case 2
No, I don’t need you now, but please comeback later.
AP may initiates the first MS.
The U-STA may resend MS Query frame at least once before T2 expires.
Predefined timeout T2: both sides reset the timer after the successful t.

## Slide 12: U-STA: MS case 3
If the AP does not want the U-STA when it receives the MS Query, it may kick the U-STA out.
I don’t need you now, e.g., I’ve already got the right guy.

## Slide 13: U-STA: MS case 4
No, I don’t need you now, but please comeback later.
It’s possible that U-STA may go away and never comeback.

## Slide 14: U-STA: MS case 5
If the U-STA wants to initiate a non-TB MS, it just send the MS Request. The AP does not need to know the sensing capabilities of the U-STA in this case.
Beacon and Probe Response shall carry AP’s detailed capabilities, in case U-STA wants to be an initiator.
It’s possible there are one or more MSs as shown in other slides.
It’s possible there are one or more MSs as shown in other slides.

## Slide 15: U-STA: more MS
Please hold on and send me an MS Query after this instance, I may initiate a frame exchange with you.
If the AP want to initiate a yet another MS or terminate existing MS or terminate the session with the U-STA, it may carry the indication in the Polling TF within a measurement instance.
MS instance of a running MS 1
A new MS 2.

## Slide 16: U-STA: MS termination case 1
Case 1: The AP may initiate termination of one or more sensing measurement setups.
Please hold on and send me an MS Query after the instance, I may initiate a frame exchange with you.
Well, let’s terminate one or more MSs.
I’m awake now.

## Slide 17: U-STA: MS termination case 2
Case 1: An U-STA may initiate termination of one or more sensing measurement setups.

## Slide 18: SP 1
Do you agree to add the following into 11bf SFD?
  An unassociated STA (denoted as U-STA) transmits the measurement setup (denoted as MS) Query frame to solicit an MS Request frame from an AP.
    The MS Query frame may contain the detailed sensing capabilities of the U-STA.
  Upon receiving an MS Query frame, the AP responds with an MS Request frame to the U-STA.
    The MS Request frame contains the UID assigned to the U-STA.
    The MS Request frame contains one bit to inform the U-STA to comeback before TBD timeout expires to solicit an MS Request frame.
  Upon receiving an MS Query frame, the AP can also send a MS Termination frame to the U-STA, which contains one bit indicating termination of all the MSs.
  The Polling TF within a measurement instance contains one bit to inform the U-STA to transmit an MS Query frame outside the measurement instance.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 19: SP 2
Do you agree to add the following into 11bf SFD?
  The timeout (value is TBD) used in the exchange of MS Request and MS Response is reused as a timeout T1, which is the time limit the AP shall respond with the MS Request. The U-STA does not wait for the MS Request for a longer time than T1 after it delivers the MS Query frame.
  A timeout T2 is predefined (value is TBD), which is the time limit the U-STA and the AP keep the agreed UID, mutual capabilities, and PASN keys (TBD). The timer for T2 is restarted at each successful handshake between the U-STA and the AP. The definition of sensing handshake is TBD.
  The U-STA should transmit the MS Query frame at least once before T2 expires.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 20: SP 3
Do you agree to add the following into 11bf SFD?
  Sensing Session is removed, correspondingly Sensing Session Setup and Sensing Session Termination phases are removed.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 21: SP 4
Do you agree to add the following into 11bf SFD ?
  The Extended Capabilities element carries essential sensing capabilities as shown in slide 5.
  A Sensing Capabilities element is defined, which carries detailed sensing capabilities as shown in slide 6.
  Other sensing capability information is TBD.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 22: SP 5
Do you agree to add the following into 11bf SFD ?
  Unicast Probe Response frame comprises the following field:
    Invitation of responder for sensing (1 bit), which indicates whether or not to invite an intended STA to join a sensing measurement as a sensing responder.
  The element carrying the field is TBD.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 23: Reference
[1] 11-21-0504-03-00bf-specification-framework-for-tgbf
[2] 11-21-1828-03-00bf-mesurement-setup-frame-formats
Chaoming Luo (OPPO)

## Slide 24: Backup: capability exchange
Case 1: A non-AP STA broadcasts probe request due to any of the following reasons
  Finds another BSS to join (or catalog for roaming later), mostly intend for communication.
  Finds an AP that supports SBP responding STA role, because the non-AP STA needs an proxy to initiate sensing procedure for it.
  Finds an AP that supports responder role, because the non-AP STA wants to initiate a non-TB sensing procedure.
  Finds an AP that supports sensing.
Case 2: A non-AP STA retrives information of an AP from Beacon. The non-AP STA may broadcast/unicast probe request to get more information.
Case 3: A non-AP STA exchanges capability information with AP using Associate Request/Response.

## Slide 25: Option 1: session setup
Session timeout T2: both sides reset the timer after ANY successful sensing frame exchange, and clear session related resources if T2 expires.
An unified sequence for session setup

## Slide 26: Option 1: first MS case 1
The U-STA may send a MS Query frame just after the sensing session setup to trigger the first MS.
Predefined timeout T1: both sides reset the timer after successful MS Query frame exchange. U-STA may go to sleep if T1 expires w/o receiving MS request.
An unified sequence for MS initiated by the AP with the U-STA

## Slide 27: Option 1: first MS case 2
The AP may not ready to start a MS with an U-STA just after session setup. The U-STA may go to power save mode. And before T2 expires, the U-STA may repeat MS Query frame at least once to trigger the first MS.

## Slide 28: Option 1: more MS
The AP may also telling the U-STA to hold on after a measurement instance and send the MS Query frame to trigger a new MS.

## Slide 29: Option 1: session termination
Case 1: An U-STA may terminate the sensing session actively by sending a Sensing Session Termination frame.
Case 2: The AP may terminate the sensing session by telling the U-STA to trigger.

## Slide 30: Comparision
Chaoming Luo (OPPO)
 | Pros. | Cons. | Notes
Option 1 | Separate and unified procedure Functionality of each frame is simple and clear. Session Setup Reponse carries AP’s detailed capabilities, which could be protected. | Four new Action frames (Session Setup Request, Session Setup Response, MS Query, Session Termination) Separate frame exchange for session setup. Separate frame exchange for session termination. | 
Option 2 | One new Action frame (MS Query) Reduce frame exchange for session setup. May reduce frame exchange for session termination. | The procedure is combined and a little bit complex. Three frames (MS Request, MS Query, Polling TF) have the same functionality of session termination. These frames have multiple functionalities and cause confusion. Beacon/Probe Response has to carry AP’s detailed capabilities, which is unprotected. |