## Slide 1: Discussion on Session Setup
Date: 2022-7-25
Authors:
Chaoming Luo (OPPO)
Name | Affiliation | Address | Phone | Email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Lei Huang |  |  |  | 
Pei Zhou |  |  |  | 

## Slide 2: Introduction
The SFD states that a sensing session is an agreement between a sensing initiator and a sensing responder to participate in a WLAN sensing procedure. [1]
This contribution discusses more about the detail of session setup procedure and frame formats.

## Slide 3: Overview and focus
WLAN Sensing procedure may comprise of several phases [1].
This contribution focuses on Sensing Discovery and Sensing Session Setup.
Sensing Initiator
Sensing Responder
Sensing Measurement Setup
Sensing Measurement Instances
Sensing Measurement Setup Termination
Sensing Session Setup
Sensing Session Termination
Sensing Discovery

## Slide 4: Abstract
Propose to remove Sensing Session, correspondingly Sensing Session Setup and Sensing Session Termination phases are removed.
  No session specific operational parameter has been identified yet.
Example of typical procedures for associated STA (denoted as A-STA) and unassociated STA (denoted as U-STA) are illustrated, including:
  Sensing Capability Exchange, Measurement Setup (denoted as MS), MS Termination.
A state machine for U-STA is introduced.
Note:
  Please keep in mind that U-STAs may go away or enter power save mode at any time, while the AP may not know about this.

## Slide 5: Discussion
What is the information shared among different MSs of a STA?
  PTKSA (result of 4-way handshake or PASN)
    PTKSA shall not be affected by the termination of sensing measurement setup.
  AID/UID
    UID, as an identifier of the U-STA, is better to be shared among multiple services (ranging, sensing), otherwise the number of identifiers AP maintains will increase when more services are introduced. The RSID of an U-STA used in ranging should be the same as the UID of an U-STA used in sensing.
  peer’s communication capabilities (e.g., supported HE-MCS and NSS set)
    A <HE-MCS, NSS> tuple in the mandatory HE-MCS and NSS set may be used, so exchange of communication capabilities is not required.
  peer’s sensing capabilities
For A-STA, the exchange and cleanup for the information above are straightforward, which is association and disassociation.
For U-STA, an MS query / MS request frame exchange and a state machine is proposed.

## Slide 6: A-STA: TB MS
Sensing Capability Exchange
Frame exchange timeout T1 (applies to both A-STA and U-STA): timeout used in the exchange of MS Request and MS Response (already in D0.1).
AP may initiates an MS at anytime.
Possibly 4-way handshake (Ref: clause 12.7.6) is excuted.

## Slide 7: A-STA: non-TB MS
A-STA may initiates an MS at anytime.

## Slide 8: A-STA: MS Termination
A sensing initiator (or sensing responder) may initiate termination of one or more sensing measurement setups. (Already in D0.1)

## Slide 9: U-STA: T2 and T3
U-STA inactivity timer T2: the U-STA is considered as inactive when T2 expires. Both the AP and U-STA maintain the inactivity timer locally. Both sides reset the timer when
  an MS (TB or non-TB) between the AP and U-STA succeeds.
  the U-STA participates in a running measurement instance.
U-STA comeback timer T3: the U-STA is expected to transmit the MS Query frame at least once before T3 expires. Both the AP and U-STA maintain the comeback timer locally. Both sides reset the timer when
  the exchange of the MS Query and the MS Request with ‘comeback=1’ has completed.
  or the exchange of the Polling TF with ‘comeback=1’ and CTS within the polling phase of a measurement instance has completed.
Note: the value of T3 could be the same as T2.

## Slide 10: U-STA: state machine
Frame exchange timer T1: applies to A-STA and U-STA, including the exchange of MS-Q/MS-REQ, MS-REQ/MS-RESP.
U-STA inactivity timer T2: T2 >= T4, T2 is a singleton between an U-STA and an AP
U-STA comeback timer T3: T3 >= T4, T3 is a singleton between an U-STA and an AP
MS expiration timer T4: reset on each instance of this MS, the value may be different for each MS.
  implied in D0.1 as “Expiration of the predefined inactivity time may terminate the sensing measurement setup. (Detailed protocol is TBD.)”

## Slide 11: U-STA: active and inactive state
Inactive state for sensing: T2 is NOT running, T3 may be running.
Examples of inactive state:
  U-STA never sends MS Query (so no TB MS) and MS Request (so no non-TB MS) .
  U-STA never sends MS Query (so no TB MS) and all non-TB MS get terminated.
  T3 started by MS Request with ‘comeback=1’, and the first TB MS has not been initiated yet.
  All MSs get terminated and T2 expired.
Active state for sensing: T2 is running, T3 may be running.
Examples of active state:
  The first non-TB MS succeeds.
  The first TB MS succeeds.
  One measurement instance is running.
  T3 started by TF Poll with ‘comeback=1’, at least one MS has not been terminated.
  All MSs get terminated and T2 has not expired.
When the U-STA transits from active to inactive state in sensing, both sides clean up the UID of the U-STA and the cached capability information of the peer.
In the inactive state, when T3 expires, both sides clean up the cached capability information of the peer.

## Slide 12: U-STA: TB MS case 1
MS Query shall carry the U-STA’s sensing capability since the AP needs the information in order to initiate a TB MS.
T2 starts when MS succeeds.
PASN may be excuted.
I need you to join my MS.
AP may initiates the first MS before T1 expires.
U-STA inactivity timer T2: see slide 9.

## Slide 13: U-STA: TB MS case 2
No, I don’t need you now, but please comeback later.
AP may initiates the first MS.
The U-STA may resend MS Query frame at least once before T3 expires.
U-STA comeback timer T3: see slide 9.
T2 starts when MS succeeds.

## Slide 14: U-STA: TB MS case 3
If the AP does not want the U-STA when it receives the MS Query, it may kick the U-STA out.
I don’t need you now, e.g., I’ve already got the right guy.

## Slide 15: U-STA: TB MS case 4
No, I don’t need you now, but please comeback later.
It’s possible that U-STA may go away and never comeback.
So the T3 expires and resources get released.

## Slide 16: U-STA: TB MS case 5
Please comeback and send me an MS Query after this instance, I may initiate a frame exchange with you.
If the AP want to initiate a yet another MS or terminate existing MS or terminate the session with the U-STA, it may carry the indication in the Polling TF within a measurement instance.
Measurment instance of MS 1, it also causes reset of T2.
A new MS 2.

## Slide 17: U-STA: non-TB MS
If the U-STA wants to initiate a non-TB MS, it just send the MS Request. The AP does not need to know the sensing capabilities of the U-STA in this case.
Beacon and Probe Response shall carry AP’s sensing capabilities, in case U-STA wants to be an initiator.
It’s possible there are one or more MSs as shown in other slides.
It’s possible there are one or more MSs as shown in other slides.

## Slide 18: U-STA: MS termination case 1
Case 1: The AP may initiate termination of one or more sensing measurement setups.
Please comeback and send me an MS Query after the instance, I may initiate a frame exchange with you.
Well, let’s terminate one or more MSs.
Measurment instance of MS 1, it also causes reset of T2.

## Slide 19: U-STA: MS termination case 2
Case 1: An U-STA may initiate termination of one or more sensing measurement setups.

## Slide 20: SP 1
Do you agree with the following?
  An unassociated STA (denoted as U-STA) and an AP maintain a state machine as shown in slide 9.
  An associated STA (denoted as A-STA) and an AP does NOT maintain the state machine shown in slide 9.
  The timeout (value is TBD) used in the exchange of measurement setup (denoted as MS) Request and MS Response is named as frame exchange timeout T1, which is also the time limit the AP shall respond the received MS Query with the MS Request. The U-STA does not wait for the MS Request for a longer time than T1 after it delivers the MS Query frame.
  An U-STA inactivity timeout T2 is predefined (value is TBD), when which expires the U-STA is considered as inactive. Both the AP and U-STA maintain this inactivity timer locally. Both sides reset the timer when
    an TB/non-TB MS between the AP and U-STA succeeds.
    or the U-STA participates in a running measurement instance.
  An U-STA comeback timeout T3 is defined (value is TBD), before which expires the U-STA is expected to transmit an MS Query frame at least once. Both the AP and U-STA maintain this comeback timer locally. Both sides reset the timer when
    the exchange of the MS Query and the MS Request with ‘comeback=1’ has completed.
    or the exchange of the Polling TF with ‘comeback=1’ and CTS within the polling phase of a measurement instance has completed.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 21: SP 2
Do you agree with the following?
  An unassociated STA (denoted as U-STA) transmits the measurement setup (denoted as MS) Query frame to solicit an MS Request frame from an AP.
  Upon receiving an MS Query frame, the AP responds with an MS Request frame to the U-STA.
    The MS Request frame contains the UID assigned to the U-STA.
    The MS Request frame contains one bit to inform the U-STA to comeback before the U-STA comeback timeout T3 expires to solicit an MS Request frame.
  Upon receiving an MS Query frame, the AP can also send a MS Termination frame to the U-STA, which indicates termination of one or more MSs.
  The Polling TF within the polling phase of a measurement instance contains one bit to inform the U-STA to comeback before the U-STA comeback timeout T3 expires to transmit an MS Query frame outside the measurement instance.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 22: SP 3
Which of the following options do you prefer?
  Option A: Remove Sensing Session, add a subclause to describe sensing capability exchange for all STAs, and describe the active/inactive state machine for U-STA only.
  Option B: Keep Sensing session for all STAs, describe sensing capability exchange in sensing session setup for all STAs, and describe the active/inactive state machine in sensing session for U-STA only.
  Option C: Abstain
  A/B/C
Chaoming Luo (OPPO)

## Slide 23: SP 4
Do you agree with the following?
  Beacon，Probe Response and (Re)Association Response frames shall carry the AP’s sensing capabilities.
  (Re)Association Request frame shall carry the non-AP STA’s sensing capabilities.
  MS Query frame shall carry the non-AP STA’s sensing capabilities.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 24: SP 5
Do you agree with the following?
  Unicast Probe Response frame comprises the following field:
    Invitation of responder for sensing (one bit), which indicates whether or not to invite an intended STA to join a sensing measurement as a sensing responder.
  The element carrying the field is TBD.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 25: Reference
[1] P802.11bf_D0.1
[2] 11-21-1828-03-00bf-mesurement-setup-frame-formats
Chaoming Luo (OPPO)

## Slide 26: Backup: capability exchange
Case 1: A non-AP STA broadcasts probe request due to any of the following reasons
  Finds another BSS to join (or catalog for roaming later), mostly intend for communication.
  Finds an AP that supports SBP responding STA role, because the non-AP STA needs an proxy to initiate sensing procedure for it.
  Finds an AP that supports responder role, because the non-AP STA wants to initiate a non-TB sensing procedure.
  Finds an AP that supports sensing.
Case 2: A non-AP STA retrives information of an AP from Beacon. The non-AP STA may broadcast/unicast probe request to get more information.
Case 3: A non-AP STA exchanges capability information with AP using Associate Request/Response.

## Slide 27: Option 1: session setup
Session timeout T2: both sides reset the timer after ANY successful sensing frame exchange, and clear session related resources if T2 expires.
An unified sequence for session setup

## Slide 28: Option 1: first MS case 1
The U-STA may send a MS Query frame just after the sensing session setup to trigger the first MS.
Predefined timeout T1: both sides reset the timer after successful MS Query frame exchange. U-STA may go to sleep if T1 expires w/o receiving MS request.
An unified sequence for MS initiated by the AP with the U-STA

## Slide 29: Option 1: first MS case 2
The AP may not ready to start a MS with an U-STA just after session setup. The U-STA may go to power save mode. And before T2 expires, the U-STA may repeat MS Query frame at least once to trigger the first MS.

## Slide 30: Option 1: more MS
The AP may also telling the U-STA to hold on after a measurement instance and send the MS Query frame to trigger a new MS.

## Slide 31: Option 1: session termination
Case 1: An U-STA may terminate the sensing session actively by sending a Sensing Session Termination frame.
Case 2: The AP may terminate the sensing session by telling the U-STA to trigger.

## Slide 32: Comparision
Chaoming Luo (OPPO)
 | Pros. | Cons. | Notes
Option 1 | Separate and unified procedure Functionality of each frame is simple and clear. Session Setup Reponse carries AP’s detailed capabilities, which could be protected. | Four new Action frames (Session Setup Request, Session Setup Response, MS Query, Session Termination) Separate frame exchange for session setup. Separate frame exchange for session termination. | 
Option 2 | One new Action frame (MS Query) Reduce frame exchange for session setup. May reduce frame exchange for session termination. | The procedure is combined and a little bit complex. Three frames (MS Request, MS Query, Polling TF) have the same functionality of session termination. These frames have multiple functionalities and cause confusion. Beacon/Probe Response has to carry AP’s detailed capabilities, which is unprotected. |