## Slide 1: Group-address-frame-enhancements for MLD
Date: 12/08/2021
Authors:

## Slide 2: Background
Multicast is a type of communication where messages are sent to a group of receiving devices simultaneously. In WiFi, multicast transmissions saves device power consumption and air-time by targeting multiple devices in one transmission.
WiFi 7 introduces a new class of devices called MLD (Multi-link Devices). Access points simultaneously connect in 2.4Ghz, 5GHz, and 6Ghz to a device offering increased aggregated throughput and reliability, but also have some disadvantages for Multicast traffic.
IANA (Internet Assigned Numbers Authority) has reserved 224.0.0.0 – 239.255.255.255 for multicast groups, with 239.0.0.0/8 commonly used on the intranet. A device that wishes to join a multicast group sends an IGMP (Internet Group Management Protocol) Membership Report / Join message for that given group. Devices can send "join group" or "leave group" messages at any point.
AP MLD can manage the multicast traffic more efficiently and offer better performance when it manages the multicast transmission with respect to the multicast groups

## Slide 3: Introduction
In this submission, we improve the delivery of multicast frames in WiFi by
  Letting AP MLD manage traffic as per the Multicast Groups
  Reducing transmitting duplicate frames there by saving Airtime and Power.
  Letting AP MLD schedule multicast traffic during TWT service period.

## Slide 4: WiFi Multicast Flow
Ethernet Bridge ports connected to VAPs.
Multicast data is transmitted to all associated VAP clients on a radio link (Only one VAP per radio link is shown in the picture).
Multicast transmission must be done with the best MCS that can be received by all associated STAs.
Associated STAs receive all multicast traffic.
STAs receives multicast/unicast only from one Radio link.
VAP rules for sending multicast data:
  In case STAs are not in Power Save mode, the AP should/may send the transmission immediately.
  Otherwise, multicasts should be transmitted only after DTIM Beacon.

## Slide 5: MLD Multicast in 802.11 be (WiFi 7)
Ethernet Bridge ports connected to AP MLD and they in turn are connected to VAPs.
AP MLD is required to duplicate the multicast traffic to all VAPs associated with its affiliated AP.
Multicast data is sent to all associated VAP clients on a radio link.
Multicast transmission must be done with the best MCS that can be received by all associated clients.
Associated STAs receive all multicast traffic.
STAs may receives multicast/unicast from multiple Radio link.
AP MLD rules for sending multicast data:
  In case STAs are not in Power Save mode, the AP should send the transmission immediately.
  Otherwise, multicasts should be transmitted only after DTIM Beacon.
  In case EMLSR non-AP MLD is associated, Multicast traffic likely would be sent after DTIM Beacon.

## Slide 6: Inefficiencies in Wi-Fi 7 Multicast
Wastes bandwidth
  Multicast frames are duplicated on all affiliated links irrespective of the link in which the non-AP MLD stations choose to receive it.
    The AP must send Multicast duplications to all VAPs since it doesn't know on which link the MLD station decide to receive the multicast
  Multicast frames are duplicated on all affiliated links irrespective of the link quality.
  Multicast frames are transmitted to all the affiliated STAs on all connected link even if the STAs might discard the frame.
Wastes client power
  Identical multicast frames are transmitted on multiple links even if the both the link quality is good.
  Associated STAs who are not the targeted recipient of the multicast frames are also required to stay active and receive all multicast frames (Packet discarding happens at other protocol stack layers)
Suffers from long latency:
  If one client is in Power Save or EMLSR non-AP MLD mode all multicast traffic on the link will be delayed to the next DTIM (typically 300-400ms)

## Slide 7: Improving efficiency in Wi-Fi 7 Multicast
Do not sent unnecessary duplicate frame.
  The AP may pick best possible MCS for all the recipient of the multicast group frames and not target all the STAs on the link.
  Associated STAs who are not the targeted recipient of the multicast frames are allowed to go to Power saving mode.

## Slide 8: Improving efficiency in Wi-Fi 7 Multicast
Let AP MLD manage multicast traffic as per the Multicast Group IDs
  AP may direct STAs of same Multicast Group ID to receive multicast frames on all or specific links based on link availability, quality or other criteria.
AP MLD can schedule the transmission for multicast traffic during TWT service period.
  STAs that are part of the Multicast Group ID can listen during the TWT period. Scheduling packets during TWT saves the client's power.
  AP may deliver the multicast frames after the low latency traffic during a TWT service period.
  AP MLD may not need to buffer the Multicast Traffic for DTIM
STAs may follow AP MLD recommendation in lieu of lower performance (latency, power)

## Slide 9: SP
Do you approve the outlined Multicast power saving and airtime usage enhancement in R2
  Y
  N
  A

## Slide 10: Backup

## Slide 11: Routing Table
The AP snoops the IGMP/MLD packets and populated the status of the multicast routes, as shown in the table.
As you can see if the proposed method is used, the AP ends up sending the multicast packet at the best rate which is MSC-7.

## Slide 12
Acronyms:
MLD: Multi link device
AP: Access point
VAP: Virtual AP
Legacy: Wi-Fi technology 802.11ax and before
AP MLD: Access point which is a Multi link device
Non-AP MLD: Station which is a Multi link device
STA: Station or Wireless Device
MCS: Modulation and Coding Scheme
TIM: Traffic indication map
DTIM: Delivery traffic indication message
eMLSR: enhanced Multilink Single Radio
TWT: Target wake time.
KPI: key performance indicator
IGMP: Internet Group Management Protocol
IANA: Internet Assigned Numbers Authority
NAV: network allocation vector
PHY: Physical Layer