## Slide 1: TWT for WLAN Sensing
Date: 2021-12-12
Authors:

## Slide 2: Motivation
A broad range of wireless local area network (WLAN) sensing applications require long-term, periodic sensing measurement and reporting of measurement results.
In these applications, low power consumption is a key requirement for battery-powered WLAN sensing devices.
A previous contribution (11-21/1532) provided a high-level overview of Target Wake Time (TWT) for periodic sensing measurement and power saving.
This contribution presents more details.

## Slide 3: A Brief Overview of TWT
“Target wake time (TWT) allows an AP to manage activity in the BSS in order to minimize contention between STAs and to reduce the required amount of time that a STA utilizing a power management mode needs to be awake. This is achieved by allocating STAs to operate at nonoverlapping times and/or frequencies, and concentrate the frame exchanges in predefined service periods.” (Clause 26.8 of 802.11ax-2021)
With the TWT mechanism, a STA can agree with an AP on a wake schedule, allowing it to wake up only when required.
[1] M. Nurchis and B. Bellalta, “Target Wake Time: Scheduled Access in IEEE 802.11ax WLANs”, IEEE Wireless Communications Magazine, April 2019.

## Slide 4: Types of TWT
Implicit TWT (TWT negotiation decides the start time of TWT and TWT wake interval) vs. explicit TWT (not supported in 11ax/be)
  Implicit TWT enables a periodic wake schedule.
Individual TWT vs. broadcast TWT
  Mandatory support by HE/EHT AP for individual TWT
  Optional support by HE/EHT non-AP STA for individual TWT
  Optional support by HE/EHT AP/non-AP STA for broadcast TWT
  Since a sensing session is pairwise (Motion 23), individual TWT fits naturally.
Trigger-enabled TWT (The AP transmits at least one trigger in each TWT service period (SP) to schedule STA’s transmissions) vs. non-trigger-enabled TWT (No trigger is transmitted in any TWT SP, thus allowing the STA to decide when to transmit autonomously inside the TWT SP)
Announced TWT (The TWT requesting STA may be at the doze state at the beginning of TWT SP and the AP transmits frames to the STA after receiving a PS-Poll/APSD trigger from the STA) vs. unannounced TWT (The TWT requesting STA shall wake up at the beginning of TWT SP)

## Slide 5: TWT Negotiation
To initiate the negotiation, the TWT-requesting STA communicates its waking schedule information to the AP via a TWT request message.
The AP devises a schedule and delivers TWT parameter values in a response message to the STA.
  TWT: the next time at which the STA should wake up for the TWT session
  TWT wake interval: the time interval between subsequent TWT sessions for the STA
It may require more than one pair of request-response messages to conclude the agreement negotiation phase.
Once the TWT parameters are agreed, the STA can go to sleep until the next TWT SP starts.
The STA wakes up and participates in sensing measurement periodically according to the schedule.
TWT Setup/Teardown/Information frames are used to set up, tear down, and update a TWT agreement, respectively.
TWT negotiation should be included in the sensing measurement setup for a sensing initiator and a sensing responder to exchange and agree on the TWT parameters associated with sensing measurement instances.

## Slide 6: Example 1 – TWT for Trigger Frame Sounding
TWT-responding/scheduling AP: sensing initiator/receiver
TWT-requesting/scheduled STA: sensing responder/transmitter
After the STA agrees with the AP on a wake schedule for a trigger-enabled TWT, it transitions to the doze state.
At the beginning of the first TWT SP, the AP transmits a trigger frame (TF) to solicitate NDP transmissions.
The station wakes up, receives the TF, and transmits an NDP frame to the AP.
The AP receives the NDP frame and performs sensing measurement.
The STA goes to sleep until the start of the next TWT SP.
The AP and the STA repeat the above process during each TWT SP.
If unannounced TWT is used, the polling phase is not needed.
TWT
Request
TWT
Response
TWT wake interval
NDP
doze
TWT SP
TWT SP
TF
TF
NDP
doze
AP
(initiator)
STA
(responder)

## Slide 7: Example 2 – TWT for NDPA Sounding
TWT-responding/scheduling AP: sensing initiator/transmitter
TWT-requesting/scheduled STA: sensing responder/receiver
After the STA agrees with the AP on a wake schedule for an individual TWT, it transitions to the doze state.
At the beginning of the first TWT SP, the AP transmits an NDPA frame followed by an NDP frame to the STA.
The STA wakes up, receives the NDPA and NDP frames, performs measurement, and feedbacks measurement result.
The STA goes to sleep until the start of the next TWT SP.
The AP and the STA repeat the above process during each TWT SP.
If unannounced TWT is used, the polling phase is not needed.
TWT
Request
TWT
Response
TWT wake interval
NDP
measurement feedback
doze
TWT SP
TWT SP
NDPA
NDPA
NDP
measurement feedback
doze
AP
(initiator)
STA
(responder)

## Slide 8: Example 3 – TWT for Non-TB Sensing Measurement
Recently, a non-AP STA-initiated non-trigger based (non-TB) sensing measurement instance received significant support (see DCN 11-21/1433r2).
In 11az, availability window is not specifieded for non-TB ranging measurement exchange.
TWT can be used to schedule periodical non-TB sensing measurement.
  It could be difficult to obtain periodical sensing measurements without TWT (i.e. the coordinated scheduling with the AP).
This also improves the overall scheduling performance of the AP (e.g. to schedule data communication and/or sensing measurement with all STAs).
doze
TWT
request
TWT
response
TWT wake interval
Sensing NDPA
AP
(responder)
STA
(initiator)
doze
TWT service period
I2R NDP
R2I NDP
Report
Sensing NDPA
TWT service period
I2R NDP
R2I NDP
Report

## Slide 9: Example 4 – TWT for Multiple Sensing Frequencies
It is highly useful for the sensing measurement frequency to be adapted quickly to environment changes.
This can be accomplished with TWT (as shown in the figure below):
  The AP and the STA can setup multiple TWT agreements between them.
  Each TWT agreement has a unique TWT wake interval corresponding to a unique sensing measurement frequency.
  A TWT Information frame can be exchanged to suspend the current active TWT agreement and resume a new TWT agreement.
TWT wake interval for
low sensing frequency
Sensing measurement instance
TWT wake interval for
high sensing frequency
TWT Information
frame exchange

## Slide 10: Example 5 – TWT for Multiple Sensing Procedures
An AP and a STA may have more than one sensing measurement procedure between them.
Sensing measurement procedure 1:
  The STA initiates a non-TB measurement (without reporting) with a high measurement frequency
Sensing measurement procedure 2:
  The AP operates a sensing by proxy procedure (for a client) and receives NDPs from the STA with a low measurement frequency
As shown in the figure below, two TWT agreements are negotiated, one for each sensing measurement procedure.
  They may have different TWT service periods and TWT wake intervals.
TWT wake interval for sensing measurement procedure 2
Measurement instance for procedure 1
Measurement instance for procedure 2
TWT wake interval for sensing measurement procedure 1

## Slide 11: Example 6 – TWT for Joint Sensing and Communication
Joint sensing and communication (JSAC) has been a hot topic in the literature.
It is most common that a STA has dual functions: data communication and sensing.
TWT is a useful tool for scheduling joint sensing and data communication.
  TWT was originally defined for data communication.
As shown in the figure below, two TWT agreements are negotiated: one for data communication and the other for sensing.
  They may have different TWT service periods and TWT wake intervals.
TWT wake interval for data
TWT wake interval for sensing
Data
Sensing

## Slide 12: Target Wake Time versus Availability Window
 | Availability Window | TWT
Standards | 11az | 11ax/11be
Association | Associated and non-associated STAs | Associated STAs only
Support of data communication | No | Yes
Number of active agreements | Single | Up to 8
Support of TB measurement | Yes | Yes (polling may not be needed)
Support of Non-TB measurement | No | Yes
Flexibility | Limited | High

## Slide 13: Summary
A follow-up discussion on TWT-based WLAN sensing measurement has been presented.
Being specified in 11ax and 11be, TWT is a versatile suite of scheduling tools.
Using TWT, each sensing STA negotiates awake periods with the sensing AP to transmit and/or receive NDPs for sensing measurement and reporting, saving energy the rest of the time as the STA remains in the doze state.
  Enables scheduling of periodic wake time for sensing measurement
  Leads to low energy consumption for the participating sensing STAs
  Provides flexibility in how the transmission period can be used for exchange of sensing information
  Facilitates joint sensing and communication
To summarize, TWT is a unique tool for the highly useful combination of efficiency, power saving, and flexible schedules.

## Slide 14: SP
Do you agree with the following?
  11bf shall add the following to the WLAN sensing procedure to facilitate the use of the Target Wake Time (TWT) mechanism specified in 11ax/11be:
    TWT setup is included in the sensing measurement setup.
    At least one sensing measurement instance is scheduled in each TWT service period.
    The termination of a sensing measurement setup shall result in the teardown of all the TWT agreement(s) associated with the sensing measurement setup. (The details of this teardown is specified in the handshake protocol for sensing measurement termination, which is TBD.)
    The teardown of any TWT agreement does not result in termination of the associated sensing measurement setup.
    Support of types of TWT are TBD.