## Slide 1: P802.11bc - Enhanced Broadcast Services Panel Presentation at IEEE Standards Summit 2021(collocated with IEEE CSCN)
Date: 2021-12-15
Authors:

## Slide 2: Abstract
Summary of Use Cases and Key Features of P802.11bc - Enhanced Broadcast Services.
The most recent version of this presentation is available at: M. Emmelmann. P802.11bc - Enhanced Broadcast Services. IEEE Standards Summit 2021, collocated with IEEE CSCN IEEE Conference on Standards for Communications and Networking. Virtual Conference, December 15-17, 2021. Online: https://mentor.ieee.org/802.11/documents?is_dcn=2010&is_group=00bc&is_year=2021 .

## Slide 3: 802.11bc specifies 9 use cases
Downlink Broadcast
Stadium Video Distribution (UC1)
Broadcast Services for Event Production (UC4)
Multi-lingual Emergency Broadcast (UC5)
VR eSports Distribution (UC6)
Multi-channel Data Distribution (UC7)
Lecture Room Slide Distribution (UC8)
Regional Broadcast TV Services (UC9)
Uplink Broadcast
Low Power Sensor Uplink (UC2)
AP Tagged Uplink (UC10)
Uplink Broadcast
Intelligent Transportation Broadcast (UC3)
Challenges:
End devices might not be able to associate to a single AP due the massive amounts of end devices  Resource constrains at AP
Sender (AP or STA) might not know that a receiver exists
Security or privacy constrains  registration not required

## Slide 4: 802.11bc – Architecture & Key Feature Overview
Support of unassociated STAs; as well as associated STAs
Higher Layer Data (Traffic Stream) mapped to content ID: STAs subscribe / select content to receive
EBCS DL provides frame authentication mechanisms that use public key algorithm and hash chain.
Router
AP
AP
Broadcast Source
Internet
Broadcast
Source
STA
STA
LAN
BC Source reside on network.
EBCS traffic stream mapper maps data (content ID) to/from sink/source to EBCS content.
EBCS Filter filters data by its content ID.
EBCS traffic stream mapper
EBCS Filter
EBCS traffic stream mapper
EBCS Filter
Router
AP
AP
Broadcast Sink
Internet
Broadcast
Sink
STA
STA
LAN
BC Sink reside on network.
EBCS proxy decapsulates data from EBCS UL frames and forward to the specified BC sink.
EBCS proxy
EBCS proxy
Downlink
Uplink
Sources: 11-21/1540 Topology and Address Mapping (M. Montemurro)

## Slide 5: References
IEEE P802.11 TGbc - ENHANCED BROADCAST SERVICES (eBCS) TASK GROUP (TG) - MEETING UPDATE. Online: https://grouper.ieee.org/groups/802/11/Reports/tgbc_update.htm
11-18-0825 Project Authorization Request (PAR). Online: https://mentor.ieee.org/802.11/documents?is_dcn=825&is_group=0bcs&is_year=2018
11-19/0135 TGbc Selection Procedure. Online: https://mentor.ieee.org/802.11/documents?is_dcn=135&is_group=00bc&is_year=2019
11-19/0151 TGbc Functional Requirements. Online: https://mentor.ieee.org/802.11/documents?is_dcn=151&is_group=00bc&is_year=2019
11-19/268 TGbc UseCase Document. Online: https://mentor.ieee.org/802.11/documents?is_dcn=268&is_group=00bc&is_year=2019
11-18/2123 TGbc Motion Booklet. Online: https://mentor.ieee.org/802.11/documents?is_dcn=2123&is_group=00bc&is_year=2018
P802.11bc Draft D2.0 will be publicly available for sale in the next weeks. Please search for it at: https://www.techstreet.com/