## Slide 1: Sensing NDP Announcement
Date: 2022-01-22
Authors:

## Slide 2: Motivation
Ranging NDP defines NTB ranging and TB ranging where NDPA solicits NDP.
TGbf discussed the usage of NDP for sensing measurement.
This presentation discusses the NDP Announcement for sensing in order to avoid introducing significant changes compared with 11az.

## Slide 3: Recap: NDP Announcement in 802.11 Baseline
Four types of NDP Announcement frames are defined.
Each STA Info field of VHT NDP Announcement has 2-byte length.
Each STA Info field of HE/EHT/Ranging NDP Announcement has 4-byte length.
nn2 or n4
NDP Announcement
Sounding Dialog Token
STA Info field in Ranging NDP Announcement

## Slide 4: Recap: Sensing Frame Exchange Sequences
Trigger Frame
AP (initiator)
STA (responder)
CTS-to-self
SIFS
Poll
Trigger Frame
SIFS
R2I NDP
SIFS
I2R NDP
AP (initiator)
STA (responder)
Measurement Report
SIFS
Sensing NDPA
SIFS
SIFS
CTS-to-self
Poll
Trigger Frame
SIFS
Measurement Report
AP (respondor)
STA (initiator)
Sensing NDPA
SIFS
R2I NDP
SIFS
SIFS
I2R NDP

## Slide 5: Ranging NDP Announcement for Sensing - Option 1
Sensing NDP Announcement is derived from Ranging NDP Announcement:
  Reusing the NDP Announcement Variant value 01 of Ranging NDP Announcement
The STA Info field (e.g. B26 and/or B31 in STA Info field) indicates the sensing frame exchange sequence is solicited.
  Option 1.1:
    Sensing Indication being 0 means Ranging NDP Announcement
    Sensing Indication being 1 means Sensing NDP Announcement
      The different sensing frame exchange sequences are decided by whether the NDP Announcement is transmitted by an AP or a non-AP STA.
  Option 1.2:
    Sensing Indication 1 and Sensing Indication 2 being 00 means Ranging NDP Announcement.
    Sensing Indication 1 and Sensing Indication 2 being 01 means Sensing NDP Announcement for NDPA + I2R NDP + Report
    Sensing Indication 1 and Sensing Indication 2 being 02 means Sensing NDP Announcement for NDPA + I2R NDP + R2I NDP + Report
With this NDP Announcement, the change compared with 11az is small.

## Slide 6: Ranging NDP Announcement for Sensing – Option 2
Sensing NDP Announcement is derived from Ranging NDP Announcement:
  Reusing the NDP Announcement Variant value 01 of Ranging NDP Announcement
A specific STA Info field indicates the sensing frame exchange sequence is solicited.
  For example, AID11 has a specific value.
With this NDP Announcement, the change compared with 11az is more than Option 1 of Ranging NDP Announcement for Sensing.

## Slide 7: New Subtype for Sensing NDP Announcement
A new Subtype value is used for control frame extension.
  Instead of using B11 to B8 of Frame Control field as the Control Frame Extension for more subtype values, in frame body of control frame with the new Subtype value, the additional Subtype field is defined.
    One value of the additional Subtype field indicates the control frame is Sensing NDP Announcement.
This method can avoid the usage of reserved bits in Frame Control field of a control frame, so the legacy STAs that receive the control frame will not be confused.
While this option provides a cleaner design, the change compared with 11az is more than Option 2 of Ranging NDP Announcement for Sensing.

## Slide 8: Summary
Various methods to design sensing NDP Announcement frame have been presented.
  Reuse current ranging NDP Announcement where the STA Info field for a specific STA indicates whether the NDP Announcement is for sensing NDP
  Reuse current ranging NDP Announcement where a specific STA Info field indicates whether the NDP Announcement is for sensing NDP
  Define sensing NDP Announcement by using a new control subtype
The reuse of ranging NDP Announcement for sensing leads to small change compared with 11az.