## Slide 1: DMG Multi-Static procedure instance
Date: 7-Oct-21
Author:

## Slide 2: Agenda
This presentation proposes the structure of an instance of a Multi-Static sensing procedure.

## Slide 3: Reminder: A Generic View of a DMG sensing/radar session
Based on the procedure already presented in 11-21-2015 and the 11az procedure
Terminations not shown

## Slide 4: This is an example of a multi-static instance
There may be several multi-static sensing PPDU in an instance
In this presentation we discuss the “instance request” frames and resp and the sense FB/poll frames

## Slide 5: Instance Request/Rsp Frame
Functions:
  Initiate the instance, make sure the responder directs its RX antennas toward the initiator
  Fine Time Schedule:
    Indicate which STAs are part of the instance and in which order
    Indicate how many multi-static sensing PPDUs frames
Needs to be either a control frame or BRP Frame
  because of tight scheduling, needs to be performed at lower MAC.
  possible implementation
    New control frame – preferably not.
    Modified TDD BF frame
    RTS with control trailer
RSP frame –
  either Ack or CTS or TDD BF frame of type TDD-SSW-ACK

## Slide 6: Sense Report-Poll/Sense Report frame
Once in an instance
Can have a similar structure to the 11ay MIMO FB-poll and MIMO FB frame.
  may need to define a new type of (Unprotected DMG Action) frame to facilitate the concept of transmitting the results of the pervious measurement.

## Slide 7: Strawpoll 1
Do you agree to add to the SFD the following text:
A multi-static EDMG sensing measurement instance has the following parts:
  An instance request frame (frame type TBD) sent to each STA sequentially, and each STA responds to it.
  A multi-static EDMG sensing PPDU. The format of the EDMG sensing PPDU is undefined.
  A feedback part in which the initiator polls each responding STA for a report and the responders respond with a report.