## Slide 1: Wi-Fi and TSN enabling deterministic wireless for time-sensitive applications
Date: 2022-01-18
Authors:

## Slide 2: Introduction
Growing interest in wireless for time-sensitive applications
  Factory/process automation, robotics, XR are a few examples
  A wide range latency/reliability KPIs, but “determinism” is a common need
  Time-sensitive and other types of applications need to work in a converged network
  Interoperability/standards-based connectivity is needed for practical/wide scale adoption
Wi-Fi with TSN capabilities is a solution for time-sensitive applications in managed enterprise/industrial networks
This presentation will discuss
  Time-sensitive application requirements
  Existing Wi-Fi capabilities including 802.11ax and TSN support
  Evolution of Wi-Fi capabilities (802.11be)
  Examples/demonstrations of Wi-Fi enabling industrial applications

## Slide 3: Application Classes
Monitoring & Analytics
Closed-loop Control Systems
Autonomous & Mobile Robots
Connected Workers
Delay-Tolerant
Time/Safety-Critical
(Hard Real-Time & Isochronous)
Soft or Firm Real-Time

## Slide 4: Time synchronization and timeliness requirements for Isochronous applications
Isochronous Industrial Control
Sensing
Actuation
Control
Applications need trusted time with quantified accuracy
Distributed applications also depend on information delivered within deadlines
https://www.iiconsortium.org/pdf/IIC_TSN_Testbed_Traffic_Whitepaper_20180418.pdf
ISOCHRONOUS TRAFFIC: The applications in each device are synchronized to a common time, which is strictly monotonic and steadily increasing, without jumps or leaps. Devices synchronously sample inputs and apply outputs by exchanging data at a defined periodic rate or cycle.

## Slide 5: Use cases and requirements (802.11 RTA TIG Report)
Ref: https://mentor.ieee.org/802.11/dcn/18/11-18-2009-06-0rta-rta-report-draft.docx
Use cases |  | Intra BSS latency/ms | Jitter variance/ms [4] | Packet loss | Data rate/ Mbps
Real-time gaming [2] |  | < 5 | < 2 | < 0.1 % | < 1
Cloud gaming [15] |  | < 10 | < 2 | Near-lossless | <0.1 (Reverse link) >5Mbps (Forward link)
Real-time video [3] |  | < 3 ~ 10 | < 1~ 2.5 | Near-lossless | 100 ~ 28,000
Robotics and industrial automation [1] | Equipment control | < 1 ~ 10 | < 0.2~2 | Near-lossless | < 1
 | Human safety | < 1~ 10 | < 0.2 ~ 2 | Near-lossless | < 1
 | Haptic technology | <1~5 | <0.2~2 | Lossless | <1
 | Drone control | <100 | <10 | Lossless | <1 >100 with video

## Slide 6: Use cases and requirements (5G ACIA White Paper)
Ref: https://5g-acia.org/wp-content/uploads/5G-ACIA_WP_5G-for-Connected-Industries-and-Automation-Second-Edition_SinglePages.pdf

## Slide 7: Leading Use Cases and Requirements (Avnu Alliance WTSN Working Group)
 | Mobile Robots | Live Events | Closed loop Control | AR/VR
Typical area of service | Small/medium/large | Medium/large | Small/medium/large | Small/Medium
End stations per area of service | 100 | 100-500 | 50 | <5 devices/group
Traffic Profile | Cyclic and Event | Continuous stream | Cyclic and Isochronous | Cyclic (UL), video (DL)
Time Synchronization Accuracy | ~1 µsec | 1 µsec or better | 1 µsec or better | ~1 µsec
Bounded Latency | 10 – 1msec (cyclic) 100 – 10 msec (events) | 1msec | 10 – 1 ms (Cyclic) 10 – 100 ms (Events) | 3 to 10 msec
Reliability | 99.9 to 99.99% | 99.9 to 99.99% | 99.9 to 99.9999% | 99.9 to 99.99%
Security | Authentication, integrity and resilience to DOS/Interference | Authentication, privacy, resilience to DOS/Interference | Auth., integrity and resilience to DOS and time/QoS attacks | Auth., integrity and resilience to DOS.
Ref: https://avnu.org/wirelessTSN/

## Slide 8: Requirement considerations
Wide range of latency/reliability KPIs
  Many use cases in the 1 to 50 msec latency range
  Some use cases (e.g., motion control) need even lower latency 10’s to 100’s microsecs
Most (industrial) applications that need “deterministic” service have predictable behavior
  Devices need service at periodic intervals for a fixed amount of data (known a priori)
  Time-critical data needs to be delivered within a deadline
Practical scenarios are managed enterprise/industrial Wi-Fi networks
  Networks are carefully planned and managed, including coverage tools, frequency planning, admission control policies, etc.

## Slide 9: Deterministic Wi-Fi
Wireless TSN
Time synch (.1AS)
Time-aware scheduling (.1Qbv)
Redundancy (.1CB)
Network
E2E wireless-wired integration Management & scheduling
Enablers
6 GHz Multi-radio clients/ APs
Core Capabilities
QoS management
802.11ax: OFDMA, Triggered access
802.11be MLO,320 MHz, Restricted TWT
Deterministic Wi-Fi Enabling Tools

## Slide 10: Unlicensed 6 GHz Worldwide Regulatory Status
The 48 CEPT countries individually implement the European Commission’s final decision to open spectrum for unlicensed. Some will proceed by consultations, while others will adopt the decision by an administrative change.
The 27 European Union Member States, all of which are also CEPT members, will implement the European Commission’s final decision to open spectrum for unlicensed on or before December 1st, 2021.
African Telecommunications Union (ATU) recommended regulation close to that CEPT. African countries started adoption or considering.
Taiwan
Jordan, Qatar, Oman
Costa Rica,
Guatemala,
Honduras
1200 MHz
1200 MHz Consultation
500 MHz
500 MHz Consultation
TBD (early in process)
No formal activity yet

## Slide 11: 802.11ax in 6 GHz
Huge contiguous clean spectrum
  Up to 1200 MHz
Ideal for deterministic, low latency operation
  Many more gigabit Wi-Fi options (more channels)
Exclusive to products based on the 802.11ax specification supporting 6 GHz band
  No legacy (pre-802.11ax) devices

## Slide 12: A simple 802.11 latency analysis
PPDU tx times as a function of RU* size and MCS
  802.11 over the air latency can be very low for various bandwidth/MCS configurations
  latency vs. reliability tradeoffs are possible considering channel conditions
* Resource Units (RU)s smaller than 20 MHz only with 802.11ax

## Slide 13: Latency and predictability enhanced with 802.11ax scheduled access
Single user transmission from 9 STAs will take ~ 1.3 msec
Single User transmission
Dave Cavalcanti, Intel
Scheduled (Trigger-based) OFDMA mode in 802.11ax avoids contention between clients enabling predictable access with higher efficiency/lower latency
Assuming: 802.11ac, 20 MHz BW, AC_VO (default parameters), average backoff (31µs), A-MPDU size (256 bytes), MCS 8 with SISO transmission
(1 STA)
With 802.11ax trigger-based Multi-User UL transmissions, the same amount of data will take approximately 758 µs.

## Slide 14: TSN “toolbox” and 802.11 (Wi-Fi) support
Bounded Latency
Reliability
Synchronization
Resource Mgmt
TSN toolbox
Time synchronization (802.1AS profile of IEEE 1588)
Time-aware scheduling (802.1Qbv)
…
Redundancy (802.1CB)
Redundant time (802.1AS-Rev)
…
TSN Config (802.1Qcc)
Stream reservation (802.1Qat)
…
802.1AS over 802.11 TM, FTM
802.1Q bridging (802.11ak)
802.11be Multi-link
Scheduling (802.11ax)
Low latency Enhancements (802.11be)
Example TSN tools (not a complete list) enabled by 802.11 and relevant 802.11 capabilities
Time-Sensitive Networking (TSN) = deterministic data delivery with bounded latency without loss due to congestion or errors. Standards defined by the IEEE 802.1 TSN Task Group.

## Slide 15: Time Synchronization (802.1AS) & Time-Aware Shaping (802.1Qbv) over 802.11
802.1AS synchronization across wired-wireless TSN
  802.11 defined MAC specific support for 802.1AS:
    Fine Timing Measurement (FTM) – IEEE802.11-2016
Talker
Listener
STA 1
T
T
T
T
T
T
T
T
T
T
T
T
Shared medium
STA 2
Queues/Traffic Classes
AP
802.1Qbv time-aware scheduling
  A time-aware (Qbv) scheduler defines when gates open/close to ensure time-sensitive frames are not delayed by other traffic
  802.11ax triggered access can be used to provide deterministic latency

## Slide 16: 802.1Qbv Scheduling over 802.11ax
Schedule configuration: the CNC delivers a schedule to the 802.11ax AP (supporting TSN)
The AP uses the trigger-based mode to deliver the data according to the worst-case latency and reliability
Simulation Assumptions:
20 MHz channel, SISO, 100 Bytes packets, Channel model E, STAs randomly distributed in a 50 m radio, latency-optimized scheduling strategy, managed network (no OBSS).
Chart: Capacity vs. Latency bound (msec) for Target PDR = 99.999%
| 1 | 1.5 | 2 | 2.5 | 3
Capacity | 9 | 18 | 28 | 35 | 45
Low latency/high reliability and capacity tradeoffs can be achieved
(Simulation Results)

## Slide 17: Network Configuration & Management
(3) Hybrid Model
WTSN domain can be physical or logical
CNC is aware of WTSN domain via WTSN-CS (Configuration and Scheduling)
The CNC can discover wireless-specific parameters and manage/configure end-to-end TSN resources
CUC
TSN-CS
Talker End Stations
TSN Bridges
Listener End Stations
Stream Data
Stream Data
End Station Configuration
UNI
End Station Configuration
End Station Configuration
End Station Configuration
Wired-TSN
CNC
Wireless Talker End Stations
Stream Data
Wireless-TSN
AP
Wireless Listener End Stations
Stream Data
AP
WTSN-CS
Notes: 1) Wireless and Wired share the same TSN Reference Stack
2) Logical is similar to 5G
Add notion of I/F Translator similar to 5G

## Slide 18: 802.11be enhancements for low latency & TSN
AP1
AP2
AP3
Multi-link device A (AP)
STA1
STA2
Multi-link device (STA)
Data
Data
Link 1 (Channel X, Band Y)
Link 2 (Channel L, Band M)
STA3
Enables lower latency and redundancy at the 802.11 MAC
New tools to avoid congestion delay
MLO (Multi-Link Operation)
Potential features for deterministic low latency
QoS provisioning for low latency traffic streams
Restricted TWT service periods for low latency traffic
Time-Aware (Qbv) scheduled access aligned with the 802.11 MAC protected service periods

## Slide 19: Wi-Fi and TSN Evolution
TSN Enabling Capabilities
2019
2021
2023
Time Synchronization
Traffic shaping over
EDCA
802.11ac + TSN
802.11ax + TSN
802.11be + TSN
Traffic shaping and bounded latency with scheduled OFDMA operation
Deterministic low latency enhancements
TSN Configuration and management
Redundancy over multi-NiC
Redundancy over MLO
…
…
802.11 and TSN will continue to evolve and introduce new TSN tools

## Slide 20
Examples and Demonstrations of Wi-Fi enabling Industrial Applications

## Slide 21: Wi-Fi in Industrial IOT
Network latencies (TUL, TDL) with 802.11ax
(msec) |  |  |  |  | 
Average | 8.85 | 2.17 | 0.83 | 2.43 | 37.6
Std. Dev. | 4.66 | 0.20 | 0.20 | 0.33 | 1.79
99 Perc. | 16.0 | 2.50 | 1.20 | 2.98 | 40.0
(msec) |  |  |  |  | 
Average | 8.85 | 2.17 | 0.83 | 2.43 | 37.6
Std. Dev. | 4.66 | 0.20 | 0.20 | 0.33 | 1.79
99 Perc. | 16.0 | 2.50 | 1.20 | 2.98 | 40.0

## Slide 22: Fine manipulation over Wi-Fi
(20 MHz Channel, 5 GHz)
* Robotic application demo provided by the Intel Labs Human & AI Robotics and Wireless Systems teams

## Slide 23: Ecosystem activities in WBA and Avnu Alliance
Workgroup launched Feb. 2021 - https://wballiance.com/wi-fi-6-6e-for-industrial-iot/
Continue the IIOT work :
https://wballiance.com/resource/wi-fi-6-trial-report-industrial-manufacturing/
https://www.mettisgroup.com/wifi6/
Wireless TSN WG
https://avnu.org/wirelessTSN/
Defining use cases, market requirements and TSN capability testing specifications
https://avnu.org/wireless-tsn-paper/

## Slide 24: Conclusions
802.11 is already used as connectivity solution in enterprises/industrial networks
New capabilities (802.11ax and TSN) are enabling support for time-sensitive applications
  Can meet isochronous communication requirements
  802.11be is introducing new deterministic low latency and reliability enhancements
  Next generation Wi-Fi will continue improving latency/reliability/efficiency
Wi-Fi and TSN trials, testing and deployments are in progress (WBA and Avnu Alliance)