## Slide 1: The need to define Frame Exchange Sequences (”FES”)
Date: 2022-01-17
Authors:
Name | Affiliations | Address | Phone | email
Harry Bims | Bims Laboratories, Inc. |  | 650-283-4174 | harrybims@me.com

## Slide 2: The problems with frame exchange sequences in normative text
The term “frame exchange sequence” is not used in any 802 standard besides 802.11
First use of “frame exchange sequence” - 802.11 1999 Base Standard
  Annex G does not exist yet
  §9 says “The allowable frame exchange sequences are listed in 9.7”
  §9.7 merely lists all allowed frame exchange sequences along with the context in which each is used. This is not a definition of the term
The understanding of frame exchange sequences in the normative text has changed over time without our realizing it
  Because §9.7 was not properly maintained, many listed sequences would NOT be considered frame exchange sequences today (e.g., the 1 frame sequences)
  Also, many frame exchange sequences today are not on the list
Attempting to modify the normative text to resolve ”inconsistencies” could have unintended consequences
  We should attempt to explain what is, rather than attempt to “correct”
  This may lead to Clause and/or STA type-specific definitions

## Slide 3: Example: Figure 10-13 (VHT MU PPDU transmissions)
Behavior of STA #1 after its ACK is not specified in the standard.
  Is it required to wait until the end of the TXOP? Or can a STA change channels, change power state, etc. after its ACK?
  Only our communal knowledge of how this scenario should work prevents a potential problem
  This does not mean the normative text is “broken”, as there is no requirement or suggestion that STA #1 transmit after its ACK in this scenario
  It does mean the lack of a definition and/or complete explanation opens the door for problems if our communal knowledge is never codified

## Slide 4: Example: §10.29.2 Reverse direction (RD) exchange sequence
Normative text conflicts with a definition of FES that assumes the TXOP holder controls the medium
The “RD exchange sequence” is an FES
  (although it is not expressly labeled as such in the normative text)
In this example, the TXOP holder or SP source is not controlling the medium during a burst,
  the RD responder is controlling the medium
Normative text allows for error recovery during a TXOP
  During a backoff period in a TXOP, neither the RD initiator nor the RD responder is controlling the medium

## Slide 5: Example: §10.29.2 Reverse direction (RD) exchange sequence
If the responder finishes early in the TXOP, and the initiator does not have another PPDU to transmit,
has the FES finished, or do all STAs have to wait until the end of the TXOP before power-save, channel change, etc?
  If the TXOP reservation is the duration of an FES, this can be used for a DOS attack (initiator can reserve a TXOP for max duration and go to sleep. Responder cannot power save or change channels. Other STAs cannot transmit on the medium).
  If not, then other STAs can transmit on the medium during a TXOP, defeating its purpose.

## Slide 6: Problems with working definitions of the WG
The ARC SC has debated several potential definitions of an FES within the past 6 months, none of which are captured in the normative text
  This would not happen if the normative text conveyed a clear definition
  Further, the group is unconvinced that any of these definitions would not cause conflict or confusion in the normative text
  This could have serious unintended consequences going forward for the stability of the standard.
The normative text uses the term “frame exchange sequences” hundreds of times. However, the normative text does NOT
  Define the purpose of an FES
  Define an FES so it can be readily identified by all STAs, whether they are peer STAs to the FES or not
  Define the start and end of an FES, whether from the perspective of peer STAs to the FES, and non-peer STAs
If we don’t explain the above in the standard, a STA cannot properly indicate this mode without interoperability testing by select companies outside the standardization process

## Slide 7: “So What?”
The definition of FESs will likely continue to change without warning in future versions of IEEE 802.11
  Debate within the 802.11 demonstrates the fluidity of its definition
  Implementors need to know:
  when an FES starts, when it stops, and what behaviors are allowed/disallowed.
We owe it to the novice reader of the standard to define this unique term to 802.11, especially since 802.11 experts have differing interpretations of this term
  Ex. Some believe a TXOP defines the bounds of a FES. However, the normative text does not say this. Creates DOS issues when frame exchanges end early.

## Slide 8: “So What?”
Knowing the FES definition directly impacts the Draft P802.11REVme normative text, e.g. Power Mgmt, Synchronization, Initialization
  “§9.2.4.1.7 Power Management Field” says
    “The subfield is either reserved (as defined below) or remains constant in each frame from a particular STA within a frame exchange sequence (see Annex G). The value indicates the mode of the STA after the successful completion of the frame exchange sequence.”
  “§6.3.4.2.4 Effect of receipt” says
    “This primitive initiates a synchronization procedure once the current frame exchange sequence is complete.”
  “§6.3.11.2.4 Effect of receipt” says
    “This primitive initiates the BSS initialization procedure once the current frame exchange sequence is complete.”
  “§9.2.4.5.11 Mesh Power Save Level subfield
    “The Mesh Power Save Level subfield indicates whether the mesh STA’s peer-specific mesh power management mode will be deep sleep mode or light sleep mode after the successful completion of the frame exchange sequence.”
  “11.2.3.1 “General” says
    “Power management mode shall not change during any single frame exchange sequence, as described in Annex G.”

## Slide 9: Annex G
Introduced in 802.11-2007 Base Standard
Replaced the old §9.7 from the 1999 Base Standard
Was referenced by the normative text for a supplemental explanation of an FES that is consistent across all allowed FES
  Consistency enforced by construction using EBNF to support automated verification of each FES
However, the problems with Annex G are numerous, including:
  its use of an EBNF format that was overly burdensome to maintain
  it now contains FES definitions that are inconsistent with the normative text and our communal knowledge
  It has failed to ensure that each FES introduced in the normative text is explained in a consistent manner without conflict with the other clauses.
  In some places, peer STAs are identified, in others they are not
  In some places, the duration of the FES is identified, in others they are not
  In some places, a figure is used to explain the FES, in others they are not
These problems are also in the normative text, and will not disappear simply by deleting Annex G
  To the contrary, they are likely to grow in secrecy

## Slide 10: Annex B1 (normative)
Also lists Frame Exchange Sequences – see §B.4.4.3
  As part of the PICS proforma
  they are the “Basic Frame Exchange Sequences” for item FS1
  Though this list is incomplete, it reinforces the need for a definition

## Slide 11: Way Forward
The TXOP definition constrains behavior of peer STAs addressed in the TXOP
The NAV definition constrains behavior of peer and non-peer STAs not addressed during the NAV period
A definition of an FES, in my view, should similarly capture
  how peer and/or non-peer STA behavior is constrained (power mgmt, channel switching, synchronization, BSS initialization)
  and for what time period (which may be different for different STAs)