## Slide 1: Initial Privacy Enhancement Requirements
Date: 2022-01
Authors:

## Slide 2: Abstract
This presentation contains an initial list of high-level requirements for Privacy Enhancements (PE)
  Privacy Enhancements for OTA MAC Addresses (TA & RA) for non-MLO and MLO scenarios
    OTA MAC Addresses for Pre-association STA/non-AP MLD
    OTA MAC Addresses for Post-Association STA/non-AP MLD
    OTA MAC Addresses for AP/AP MLD requirements
  Privacy Enhancements for SA and DA

## Slide 3: Terminology (for this presentation)
Abbreviation Meaning
Generic Terms
OTA MAC Addresses Over-the-Air MAC Addresses (TA and RA)
PE Privacy Enhancements = Features specified by 11bi
PE BSS BSS providing PE features
PE [Device Abbr] PE-capable [Device, E.g. STA]
Non-MLO Terms
PE STA PE-capable non-MLO non-AP STA (legacy scanning/auth/assoc)
PE AP PE-capable non-MLO AP (legacy scanning/auth/assoc)
MLO Terms
PE AP MLD PE-capable AP Multi Link Device (2+ Links)
PE non-AP MLD PE-capable non-AP Multi Link Device (2+ Links)
affiliated AP the APs that are controlled by the AP MLD
affiliated STA the STAs that are controlled by the non-AP MLD

## Slide 4: Very-High level PE System Assumptions/Requirements
Assumption-BSS Privacy Enhancement features shall be provided in a PE BSS where all 802.11 Devices are PE Capable.
REQ-Struct. Privacy Enhancement features shall work with and without MLO (802.11be).

## Slide 5: What shouldn’t change
Confirming where there is no change to existing behaviour
Existing-OTA-non-MLO. The transmitting STA (or AP respectively) and receiving AP (or STA respectively) of a frame shall be identified using TA and RA (“OTA MAC addresses”).
Existing-OTA-MLO. (Confirming no change to existing behaviour) The transmitting affiliated STA (or affiliated AP respectively) and receiving affiliated AP (or affiliated STA respectively) of a frame shall be identified using TA and RA.
Existing-OTA-Retrans. (Confirming no change to existing behaviour) If a first frame is retransmitted as a second frame, then the OTA MAC addresses in the second frame shall be identical to the OTA MAC addresses in the first frame.

## Slide 6: MLD fallback to non-MLO
MLDs behave as MLO Devices when interacting with MLO Devices and behave as non-MLO Devices when interacting with non-MLO Devices. There are four combinations/cases here. Suggest focus on requirements for two cases: PE AP with PE STA (both non-MLO); and PE AP MLD with PE non-AP MLD (both MLO). Then invoke the following requirements which reduce the requirements of the remaining two cases (PE AP with PE non-AP MLD, and PE AP MLD with PE STA) to the requirements of the PE AP with PE STA case.
REQ-MLD-Fallback-non-AP. For those operations that a PE non-AP MLD performs as if it were a PE STA (e.g. when interacting with a PE AP), the PE non-AP MLD shall satisfy the same requirements as a PE STA.
REQ-MLD-Fallback-AP. For those operations that a PE AP MLD performs as if it were a PE AP (e.g. when interacting with a PE STA), the PE AP MLD shall satisfy the same requirements as a PE AP.

## Slide 7: OTA MAC Addresses & non-MLO
PE Requirements on OTA MAC Addresses for non-MLO Devices and non-MLO interactions
These mirror the PE requirements for MLO scenarios

## Slide 8: OTA MAC Address of Pre-Association PE STA
REQ-OTA-Pre-STA-1. For each scan iteration (definition TBD), a PE non-AP shall generate/derive a new random or pseudo-random “scanning” OTA MAC address for itself.
REQ-OTA-Pre-STA-2. For each sequence of authentication frames and association frames (and 4-way handshake? TBD) between a PE STA and PE AP, the PE STA shall generate/derive a new random or pseudo-random “pre-association” OTA MAC address for itself.
In this document, “random or pseudorandom” implies that any other device is unable to correlate the value to any identifier for the device, except where there are explicit PE requirements.

## Slide 9: OTA MAC Address of Post-Association PE STA
REQ-OTA-Post-STA-1. A PE STA and PE AP shall support a process for a PE STA and a PE AP to transition seamlessly from using the pre-association OTA MAC address for the PE STA (see REQ-OTA-Pre-STA-2) to using a new random or pseudorandom “post-association” OTA MAC address.
REQ-OTA-Post-STA-2. A PE STA and PE AP shall support a post-association process for a PE STA and a PE AP to transition seamlessly from using the current post-association OTA MAC address for the PE STA (see REQ-OTA-Pre-STA-2) to using a new post-association OTA MAC address.
REQ-OTA-Post-STA-3a. The process in REQ-OTA-Post-STA-2 shall support being initiated by the PE STA.
REQ-OTA-Post-STA-3b. The process in REQ-OTA-Post-STA-2 may support being initiated by the PE AP.

## Slide 10: OTA MAC Address of PE AP
REQ-OTA-AP-1. At any point in time, a PE AP shall be identified by one OTA MAC Address.
  NOTE: At any point in time, all pre-association and post-association PE STA identify the PE AP with identical OTA MAC Address.
REQ-OTA-AP-2. A PE STA and PE AP shall support a post-association process for a PE AP and its associated PE STA(s) to transition seamlessly from using the current OTA MAC address for the PE AP to using a new OTA MAC Address.
  NOTE: If this transition occurs while an un-associated PE STA is communicating with the PE AP, then the communications might fail, and the PE STA might need to perform the pre-association process from the beginning.
REQ-OTA-AP-3a. The process in REQ-OTA-AP-2 shall support being initiated by the PE AP.
REQ-OTA-AP-3b. The process in REQ-OTA-AP-2 may support being initiated by the PE STA.

## Slide 11: OTA MAC Addresses & MLO
PE Requirements on OTA MAC Addresses for MLO Devices and MLO interactions These mirror the PE requirements for non-MLO scenarios

## Slide 12: OTA MAC Address Pre-Association PE non-AP MLD
REQ-OTA-Pre-non-AP-MLD-1. For each scan iteration (definition TBD), a PE non-AP MLD shall generate/derive a new random or pseudo-random “scanning” OTA MAC address for each of its affiliated STAs.
REQ-OTA-Pre-non-AP-MLD-2. For each sequence of authentication frames and association frames (and 4-way handshake? TBD) between a PE non-AP MLD and a PE AP MLD, a PE non-AP MLD shall generate/derive a new random or pseudo-random “pre-association” OTA MAC address for each of its affiliated STAs.

## Slide 13: OTA MAC Address Post-Association PE non-AP MLO
REQ-OTA-Post-non-AP-MLD-1. A PE STA and PE AP shall support a process for a PE non-AP MLD and a PE AP MLD to transition seamlessly from using the pre-association OTA MAC addresses for the affiliated STAs of the PE STA MLD (see REQ-OTA-Pre-non-AP-MLD-2) to using a new random or pseudorandom “post-association” OTA MAC addresses.
REQ-OTA-Post-non-AP-MLD-2. A PE non-AP MLD and PE AP MLD shall support a post-association process for the PE non-AP MLD and a PE AP MLD to transition seamlessly from using the current set of post-association OTA MAC addresses for the affiliated STAs of the PE non-AP MLD to using a new set of post-association OTA MAC addresses.
REQ-OTA-Post-non-AP-MLD-3a. The process in REQ-OTA-Post-non-AP-MLD-2 shall support being initiated by the PE non-AP MLD.
REQ-OTA-Post-non-AP-MLD-3b. The process in REQ-OTA-Post-non-AP-MLD-2 may support being initiated by the PE AP MLD.

## Slide 14: OTA MAC Address Requirements: PE AP MLD
REQ-OTA-AP-MLD-1. At any point in time, each affiliated AP of the PE AP MLD shall be identified by one OTA MAC Address.
  NOTE: At any point in time, all PE STAs (pre-association and post-association), as well as all affiliated STAs of PE non-APs (pre-association and post-association) identify an affiliated AP with identical OTA MAC Address.
REQ-OTA-AP-MLD-2. A PE non-AP MLD and PE AP MLD shall support a post-association process for a PE AP MLD and associated PE non-AP MLD(s) to transition seamlessly from using the current set of OTA MAC addresses for the affiliated APs of the PE AP MLD’s to using a new set of OTA MAC addresses.
  NOTE: If this transition occurs while an un-associated PE non-AP MLD is communicating with the PE AP MLD, then the communications might fail, and the PE non-AP MLD might need to perform the pre-association process from the beginning.
REQ-OTA-AP-MLD-3a. The process in REQ-OTA-AP-MLD-2 shall support being initiated by the PE AP MLD.
REQ-OTA-AP-MLD-3b. The process in REQ-OTA-AP-MLD-2 may support being initiated by the PE non-AP MLD.

## Slide 15: Other Addressing Scenarios
SA and DA

## Slide 16: SA and DA Requirements
REQ-SA-1 If the source of a frame is different from the transmitting 802.11 radio (including MLO cases where the PE AP/non-AP MLD is the source and the affiliated AP/STA is the transmitting 802.11 radio), then the source MAC Address shall not be transmitted in the clear.
REQ-DA-1 If the destination of a frame is different from the receiving 802.11 radio (including MLO cases where the PE AP/non-AP MLD is the destination and its affiliated AP/STA is the receiving 802.11 radio), then the destination MAC Address shall not be transmitted in the clear.