## Slide 1: Enhanced Randomized and Changing MAC address (ERCM)
Date: 2022-05-10
Authors:

## Slide 2: Revisions
R0 – Initial Version –
R1 Includes modifications according to received comments : addition of a transition period for the MAC address change, and mechanism to avoid exposing the date of the MAC address change in a frame.
R2 Includes requirements mapping and SP.
R3 Updated requirement text according to 622r7 (agenda)

## Slide 3: Abstract
Current contribution describes a method to change the public MAC Address of an associated STA using a standard pseudo random generator based on shared private information. The change can be at the AP STA or non-AP STA initiative. This method makes correlation between a MAC address and a given STA very difficult for non registered STA.

## Slide 4: Overview
Specifying a Seamless Enhanced RCM (SERCM) procedure allowing the dynamic change of the MAC address of a non-AP STA when it is associated with an AP.
  During, or after association, encrypted information (SERCM key) is shared between AP and non-AP STA.
    Note: the PMK may be used as ERCM key.
  Upon AP or non-AP STA request, both AP and non-AP STA compute a new transient MAC address for the changing STA, without sharing it, by using same pseudo random generator with same parameters.
    Alternative scenario without any exchange between AP and non-AP STA (see slide 9)
  At the starting of the transition period, both AP and non-AP STA initiate the MAC address change for the changing non-AP STA.
  During the transition period, both current and new values for the MAC address are valid.

## Slide 5: ERCM Key exchange (optional)
After association, encrypted information (ERCM key) is shared between AP and non-AP via specific action frames
    Note: the PMK may be used as ERCM key.

## Slide 6: New transient MAC address
Upon AP or non-AP STA request, both AP and non-AP STA compute a new transient MAC address for the changing STA, without sharing it, by using the standardized PRF-128 (section 12.7.1.2 -IEEE Std 802.11-202) with same parameters.
@MAC (n+1) = PRF-128/46( ERCM Key, “ERCM”, @MAC (n) , 128)
  From the generated 128 bits, the leftmost 46 bits (i.e. the 46 most significant bits) are selected
  In addition to the 46 bits, the U/L bit of the new MAC address is set to 1, the I/G bit is set to 0
  @MAC (n) corresponds to the current address MAC of the non-AP STA

## Slide 7: Synchronous change of the MAC address
At the request for changing the MAC address of the non-AP station initiated by the AP or the non-AP STA, both AP and non-AP STA apply the MAC address change for the changing STA.
AP Initiation
  SERCM intended to all the non-AP stations SERCM-capable
  Use of a new ERCM IE to be included in the beacon frame including an SERCM Change counter corresponding to the number of TBTTs until the next transient MAC address is effective
Non-AP Initiation
  Use of a new action frame including an SERCM Change date corresponding to the number of TBTTs until the next transient MAC address is effective

## Slide 8: Main principle
AP Initiation
Non-AP Initiation

## Slide 9: Alternative without explicit signalling
Synchronous MAC address generation:
  No exchange of any SERCM Change Request to compute a new transient MAC address for the changing STA.
Calculate a SERCM counter value (CC) (4 bits) using the standardized PRF-128 (section 12.7.1.2 -IEEE Std 802.11-202) with same parameters as to compute the new transient MAC address (new set of bits).
  CC (n+1) = PRF-128/4( ERCM Key, “ERCM”, CC (n) , 128)
  From the generated 128 bits, the new set of 4 bits (different from the leftmost 46 bits used for the new transient MAC address) are selected.
  The SERCM counter value defines a number of TBTTs before applying the new transient MAC address.
Synchronous management of the SERCM counter value
  No exchange of the SERCM Change counter value in the beacon frame.
  Synchronous decrease of the SERCM Change counter value starting after the first beacon following the SERCM initiation procedure or after the previous transient MAC address validation.
  Beacon
@mac(n+1)
CC(n+1)
AP
Non-AP STA
  Beacon
  Beacon
…
  ERCM initiation procedure
@mac(n+1)
CC(n+1)
ERCM counter value = 0
ERCM counter value = CC(n+1)
ERCM counter value = 0
Change
@mac(n+2)
CC(n+2)
Change
@mac(n+2)
CC(n+2)
ERCM counter value = CC(n+1)
ERCM counter value = CC(n+1) -1
ERCM counter value = CC(n+1) -1

## Slide 10: ERCM regarding Client Privacy Enhancements Requirements [4]
Req ID | Client OTA MAC Address randomization Requirement | Status
6 | 11bi shall define a mechanism for a CPE Client to change its own OTA MAC Address when reassociating from a CPE AP to another CPE AP | Not addressed at the current stage but compatible
7 | 11bi shall define a mechanism for a CPE Client to initiate changing its own OTA MAC Address used with a CPE AP in Associate STA State 4 without any loss of connection. | Addressed
8 | 11bi shall define a mechanism for a CPE AP to initiate changing the OTA MAC Addresses of a set of associated CPE Client’s in the BSS (those CPE Clients in Associate STA State 4) without any loss of connection | Addressed
39 | 11bi shall define a mechanism to for BPE AP and BPE Client to change the OTA MAC addresses, SN and PN they use for unicast transmissions at STA specific schedule. | Addressed Partially (OTA MAC address part)

## Slide 11: Benefits
The user privacy is now ensured also when the non-AP STA is associated.

## Slide 12
Straw Poll #1
Is there interest within the 802.11bi WG to pursue the idea of defining and specifying the use of a pseudo random generation of OTA MAC address as defined is slides 4 to 9 ?
Yes
No
Abstain

## Slide 13: References
[1] IEEE 802.11-21/1854r1 – Association MAC Address based on AID (A-AMAC)
[2] IEEE 802.11-21/1539r0 – Rotating MAC Addresses Over the Air
[3] IEEE 802.11-21/1848r7 – Requirements Document
[4] IEEE 802.11-22/0622r7 – EDP – TGbi -Agenda- April 2022

## Slide 14: ERCM Capability
An ERCM Capability field is used in the STA and AP to advertise their capability to support ERCM
Bit | Information | Notes
<ANA> | Enhanced RCM Capabilitiy | The STA sets Enhanced RCM Capabilities bit to 1 to indicate support for Enhanced RCM and sets to 0 if Enhanced RCM is not supported.
Insert new row in Table 9-153—Extended Capabilities field, Clause 9.4.2.26
1431
Element ID | Length | Extended Capabilities
Insert new row in Table 9-153—Extended Capabilities field, Clause 9.4.2.26

## Slide 15: ERCM Action frame
Category
ERCM Action
ERCM Key delivery Request
Category
ERCM Action
ERCM Key delivery Response
830
Category
ERCM Action
832
ERCM Key delivery Confirm
ERCM Key
840
Category
SERCM Action
SERCM change Request
Category
ERCM Action
ERCM change Response
SERCM Change start Date
843
Code | Meaning
<ANA> | Enhanced RCM
  added in the Table 9-51—Category values
Insert new clause at end of 9.6 Action frame format details
Action Field value | Meaning
1 | ERCM Key delivery Request
2 | ERCM Key delivery Response
3 | ERCM Key delivery Confirm
4 | ERCM change Request
5 | ERCM change Response
SERCM max transition period