## Slide 1: Secure Device ID Exchange concept
Date: 2022-01-18
Authors:

## Slide 2: Abstract
Proposal of enable the exchange an encrypted unique device identifier over secure or non-secure link
This proposal is an extension to 11-21/1378 & 11-21/1379r3
* Add additional field to MLME SAP primitives.
* Modify MLME descriptions as defined in 11-21/1379r3

## Slide 3: Background
Randomized and Changing MAC (RCM) has been introduced to increase user privacy and reduce the ability of device tracking
MAC has been used by Wi-Fi technologies and services as the method to identify a device
RCM impacts many services that made use of the MAC as the device identity

## Slide 4: Allow an AP to request an ID from a STA and the STA to return the ID in an encrypted format
This proposal expands the Client ID Query (11-21/1378 & 11-21/1379r3) proposal
The exchange can happen over a non-secure or secure link
The ID form is not defined but recommended to be unique to the device
There is a requirement that a keypair rooted in the AP
  The keypair can be static or dynamically generated
  AP shares the public key with the STA for ID encryption, private key maintained by the AP and is used to decrypt the ID

## Slide 5: Allows the STA to request information to share the STA ID in the encrypted form
Unlike Client ID Query (11-21/1378 & 11-21/1379r3) proposal this would allow the STA to request a public key from the AP to enable the ID encryption.
This is where the two proposal differ in flow.
The STA send message to the AP which triggers the AP to start the request of STA ID
This allows the STA to provide the ID pre-association

## Slide 6: Request Frame Format for AP (Modify from 11-21/1378)
The Request frame allows an AP to query an associated STA for a unique identifier.
Category | ID Query Action | Public key to be used to encrypt ID
Octets: 1 1 Variable

## Slide 7: Response Frame Format (as defined in 11-21/1378)
The Response Frame format allows the responding STA to indicate either that it will not provide an ID or that it will.
The Response includes optional ID and TTL fields, if the STA decides to provide an ID.
The Response includes a Length field to allow for variable sized ID, and extensibility for vendor specific information, etc.
A Vendor Specific field is also included in the Response to allow vendor differentiation.
Octets: 1 1 1 2 Variable 2 Variable
Category | ID Query Action | Response | Length | ID (optional) | TTL (optional) | Vendor Specific (optional)

## Slide 8: Key Request Frame Format for STA
The Key Request frame allows a STA request the AP to share public key for encrypting ID. This triggers the AP to start the ID Request flow.
Category | ID Query Action
Octets: 1 1

## Slide 9: Advertisement of Support for ID Query (as defined by 11-21/1378)
An Extended Capability bit is proposed.
The ID Query_Support bit set to 1 indicates that a STA can support an ID Query action frame.
At a higher layer, a user may direct a STA to not share a permanent or semi-permanent identifier, so a STA may still decline to provide an ID even though it indicates support for the message.
  For example, such a decision might be based on the network being associated, and the level of trust in the networks’ provider(s).

## Slide 10: Summary
The device MAC has been used to identify a device, while MAC was not intended for this prepose, RCM has forced that the MAC cannot be used for device identification.
There needs to be a secure way to share a device ID that eliminates that ability for 3rd parties to identify a device or trace a device beyond a BSS service area.
By use of a keypair, the STA can use the public key to encrypt the ID and only the AP (holder of the private key) is able to decrypt the ID.
The STA could still ignore the message or decline to provide a unique identifier.
The AP could ignore the request from the STA to request the device ID
The STA can provide the ID without need for solicited request.