## Slide 1: Discussion on Measurement Setup ID Setting in SBP Case
Date: 2022-01-19
Authors:
Name | Affiliation | Address | Phone | Email
Pei Zhou | OPPO |  |  | zhoupei1@oppo.com
Chaoming Luo |  |  |  | 
Lei Huang |  |  |  | 
Ning Gao |  |  |  | 

## Slide 2: Background
According to [1] and [2], the following Measurement Setup ID related rules/contents are agreed by TGbf:
  The Measurement Setup ID identifies the attributes/parameters agreed upon between the initiator and one or more responders.
  According to [2] and [3], the following SBP related rules/contents are agreed by TGbf:
  An optional sensing by proxy (SBP) procedure is defined in which:
    An “SBP request” consists of a non-AP STA sending an SBP Request frame to an SBP-capable AP STA.
      A STA that sends an SBP Request frame to invoke SBP (and, as a result, WLAN sensing) is denoted by “SBP requesting STA”.
    An AP STA that receives an SBP request shall send to the SBP requesting STA an SBP Response frame to accept or reject the request.
    An AP STA that accepts an SBP request shall initiate a WLAN sensing procedure with one or more non-AP STAs using operational parameters derived from those indicated within the SBP Request frame.
      Whether the SBP requesting STA participates or not in the WLAN sensing procedure as a sensing responder is TBD.
    Measurement results obtained in a WLAN sensing procedure resultant from an SBP request shall be reported to the SBP requesting STA.

## Slide 3: Measurement Setup in SBP Case
According to [3], STA 3 (as SBP Requesting STA) requests AP (as Sensing Proxy) to perform sensing measurement for it through SBP Request frame.
  SBP Requesting STA (e.g., STA 3) is not Sensing Initiator.
  SBP Responding STA (i.e., AP) is Sensing Initiator.
Then, AP (as Sensing Initiator) initiates Measurement Setup with one or more STA(s) and assigns Measurement Setup ID.
This contribution discusses two methods for SBP Requesting STA to identify a specific measurement setup.

## Slide 4: Measurement Setup ID Setting Methods
Method 1: AP manages the mapping between Dialog Token and Measurement Setup ID.
Example:
  Dialog Token in SBP Request: a (applicable in SBP Request & Response frames);
  Dialog Token in SBP Response: a;
  Measurement Setup ID set by AP: 1 (applicable between AP and Sensing Responders);
  Mapping information managed in AP: a ↔ 1;
  Measurement Setup ID in Measurement Report received from Sensing Responders: 1;
  So, AP translates 1 to a, then transmits SBP Report with Dialog Token a to STA 3.
  Therefore, SBP Requesting STA can use dialog token to identify a specific measurement setup.
Summary:
  Dialog token is only used between SBP Requesting STA and Proxy (AP);
  Measurement Setup ID is only used between Proxy (AP) and Sensing Responders;
  Proxy (AP) manages the mapping between Dialog Token and Measurement Setup ID.
Key point: AP shall cache all the mapping information for all the SBP Requesting STAs.

## Slide 5: Measurement Setup ID Setting Methods
Method 2: AP shares the Measurement Setup ID in its SBP Response frame ahead of time.
Example:
  STA 3 requests AP as Sensing Proxy to perform WLAN Sensing through SBP Request frame;
  AP pre-assigns the Measurement Setup ID (i.e., 1) for STA 3 and puts the ID in SBP Response frame;
  Then, AP initiates measurement setup with STA1 and STA 2 using the Measurement Setup ID = 1;
  Therefore, SBP Requesting STA can use Measurement Setup ID to identify a specific measurement setup.
  Key points:
  Additional overhead: SBP Response frame may need to carry both dialog token and Measurement Setup ID.
  It is inappropriate that the Measurement Setup ID is pre-assigned to the SBP Requesting STA if the measurement setup procedure is failed (e.g., the proxy AP can’t find suitable STAs based on the operational parameters of the SBP Request frame).
  If however, AP manages to never find (perhaps we need to have some timeout specified) Sensing Responders to proceed with measurement instances, then it would need to send termination message to the SBP Requesting STA and release the Measurement Setup ID.

## Slide 6: Method 1 v.s. Method 2
The pros. and cons. of method 1 and method 2 are shown below:
Method 1 is preferred because it consumes lower signaling overhead and has no issue when the measurement setup fails.
 | Pros. | Cons.
Method 1 | Lower overhead in SBP Response frame: only carries dialog token, no need to carry Measurement Setup ID. No issue when the measurement setup fails. | Needs more storage because AP shall cache and manage all the mapping information (Dialog Token ↔ Measurement Setup ID) for all the SBP Requesting STAs.
Method 2 | No need to cache and manage mapping information (Dialog Token ↔ Measurement Setup ID). | Higher overhead in SBP Response frame: needs to carry both dialog token and Measurement Setup ID. Complicated to deal with the measurement setup failure issue.

## Slide 7: Summary
We discussed two methods for SBP Requesting STA to identify a specific measurement setup in SBP case:
  Method 1: AP manages the mapping between Dialog Token and Measurement Setup ID.
  Method 2: AP shares the Measurement Setup ID in its SBP Response frame ahead of time.

## Slide 8: SP
Which option do you prefer when defining the method for a SBP Requesting STA to identify a specific measurement setup in Sensing by proxy (SBP) procedure?
  Option 1: Dialog token is used between SBP Requesting STA and Proxy (AP). Measurement Setup ID is used between Proxy (AP) and Sensing Responders. Proxy (AP) manages the mapping between Dialog Token and Measurement Setup ID.
  Option 2: AP shares the Measurement Setup ID in its SBP Response frame ahead of time.
Option 1/Option 2/Abstain

## Slide 9: Reference
[1] 11-21-1701-01-00bf-measurement-setup-termination.pptx
[2] 11-21-0504-04-00bf-specification-framework-for-tgbf.docx
[3] 11-21-1692-04-00bf-enhancing-client-based-sensing-sensing-by-proxy.pptx