## Slide 1: Parameters for sub-7 GHz Sensing NDPA
Date: 2022-01-20
Authors:
Name | Affiliation | Address | Phone | Email
Junghoon Suh | Huawei |  |  | junghoon.suh@huawei.com
Mengshi Hu |  |  |  | 
Rui Du |  |  |  | 
Yan Xin |  |  |  | 

## Slide 2: Background
Sensing parameters are negotiated during the Sensing Session Set-up phase [1]
It was discussed what sensing parameters need to be transmitted during the Sensing Measurement Set-up phase [2,3]
We try to summarize what parameters are needed for the Sensing NDPA

## Slide 3: Sensing NDPA format
It is not determined how the Sensing NDPA format may be designed yet, however, there have been two directions in Sensing NDPA design [4,5]
  Using the same subtype in the Frame Control field as in the baseline 802.11 NDPA
  Using the different subtype in the Frame Control field from the baseline 802.11 NDPA
Regardless of whichever direction to choose for the Sensing NDPA, there could be Common Info field and STA Info field

## Slide 4: Common Info field
The name of this field is TBD, which can be called a Special STA Info field, NDPA Variant field, etc.
Presence of Common Info field
  Depending on the proposal, this can be TBD bits
  Special STA Info field case: 11bits for dummy AID are needed
Session Set-up ID: MAC Address and/or AID/UID
  MAC Address (48 bits)
  AID/UID (11bits)
Measurement Set-up ID: 1 byte
  In case we need to indicate the different Measurement Set-up ID for each STA listed in the STA Info field, the Measurement Set-up ID can go into the STA Info field
Measurement Instance ID: Sounding Dialog Token Number may play a role of this ID
  6 bits enough (?)
  In case it is necessary to carry more than 6 bits for this ID, this needs to be carried in the Common Info field as well
  In case we need to indicate the different Measurement Instance ID for each STA listed in the STA Info field, the Measurement Instance ID can go into the STA Info field
NDPA Version ID
  1 byte will be enough
Disambiguation bit: 1 bit every two byte, Reserved subfield for future extension
Approximately, 10~12 bytes are needed for the Common field

## Slide 5: STA Info field
AID11: (11bits)
Bandwidth: (9 bits) Indicates the sub-channels CSI FB is required
Number of TX Streams: (4 bits)
Number of RX Streams: (4 bits)
CSI FB Type: (1 or 2 bits) depending on how many options we need for “CSI_ESTIMATE”
Ng: (2 bits – 8, 16, 32, 64 tones)
Disambiguation: 1 bit per every two bytes (No need this if we use the different subtype)
Scale Factor: (1 bit – 3 or 6 bits)
CSI FB Bit Size: (2 bits – 6, 8, 10, 12 bits)
TX Power: (2 bits) Impact on the Sensing Range
Number of Taps for TCIR: (6 bits) (TBD)
Threshold for CSI FB: (4 bits)
Measurement Set-up ID (MSI): (8 bits) It is needed when the different MSI is needed per STA Info field
Measurement Instance ID (MII): (8 bits) It is needed when the different MII is needed per STA Info field
Reserved subfield for future extension: TBD bits
Total: 60 to 70 bits are needed

## Slide 6: Summary
In case Measurement Set-up ID and Measurement Instance ID can be different per each STA Info field
  10~12 bytes are needed for Common field
  60+ bits are needed for STA Info field

## Slide 7: References
[1] 11-20-1851-01-00bf-overview-of-wi-fi-sensing-protocol
[2] 11-21-0365-02-00bf-wi-fi-sensing-parameters
[3] 11-21-2029-01-00bf-definitions-of-some-sensing-operational-parameters
[4] 11-21-1896-02-00bf-ndpa-for-sensing
[5] 11-21-1751-01-00bf-condideration-for-ndpa-in-11bf