## Slide 1: Interaction between R-TWT and SCS (CC36 resolution for CID 4121)
Date: 2021-05-18
Authors:
Name | Company | Address | Phone | Email
Liangxiao Xin | Sony Corporation |  |  | Liangxiao.Xin@sony.com
Mohamed Abouelseoud |  |  |  | Mohamed.Abouelseoud@sony.com
Li-Hsiang Sun |  |  |  | Li-Hsiang.Sun@sony.com

## Slide 2: Related CID
CID | Commenter | Clause Number(C) | Comment | Proposed Change | 
4121 | Akira Kishida | 35.6.2.1 | Priority in latency sensitive traffic or TID should be clarified when operating on restricted service periods. In other words, some prioritization between TIDs in restricted service periods should be clarified. | As in comment. | 

## Slide 3: Introduction
Current tools for improving latency performance in TGbe
  SCS procedure: differentiate latency sensitive traffic stream under a QoS characteristics from other regular traffic or other latency sensitive traffic stream under different QoS characteristics in a same TID  traffic is tied to SCSID
  R-TWT procedure: channel reservation for latency sensitive traffic  traffic is tied to SCSID
The above two tools play different roles, and they should interact to achieve the best latency performance.
  R-TWT can use QoS characteristics of SCS traffic stream(s) for scheduling.
  SCS traffic stream might need R-TWT to provide channel resource reservation service.
However, the interaction between R-TWT and SCS is not well defined.
  The current draft does not define how to use SCS information for R-TWT scheduling
  The current draft does not define if SCS information is required before/during the R-TWT setup
  R-TWT setup is currently tied to TID not SCSID
We discuss adding parameters to facilitate the SCS and R-TWT interoperation

## Slide 4: Goal and difficulty
If a R-TWT is to be scheduled based on the QoS characteristics of a SCS traffic stream, It should prioritize the SCS traffic stream of concern during the R-TWT SPs instead of all the traffic in the same TID of a STA.
  For example, STA has two SCS traffic streams, e.g., SCS1 and SCS2 of TID=6, with different QoS characteristics. SCS1 traffic stream requires R-TWT for channel reservation and SCS2 traffic stream does not. During a R-TWT SP for SCS1 traffic stream, STA should prioritize SCS1 traffic stream only.
One concern when R-TWT procedure is prioritizing SCSID in a specific TID in the operation of BA
  The assignment of new MPDUs SN should prioritize the SCSID of concern. All previously assigned SN should be transmitted without interruption.

## Slide 5: Gap between R-TWT and SCS
R-TWT is link level signaling while SCS is ML level signaling.
  A SCS traffic stream is established on any link first. Then, the QoS Characteristics element of the SCS traffic stream can be used for the R-TWT scheduling.
  When the non-AP STA initiates the R-TWT membership negotiation with the AP, it does not know which link to request R-TWT membership.
  Therefore, it is better for AP to assign R-TWT membership for the SCS traffic stream on one link.
SCS Req
SCS Resp
R-TWT membership
STA1
(Link1)
STA2
(Link2)
AP1
(Link1)
AP2
(Link2)
R-TWT is Requested
AP2 assigns a R-TWT membership for the SCS

## Slide 6: Proposal 1
A SCS traffic stream should indicate whether it requires R-TWT scheduling for it during the SCS setup procedure
Proposal: Add R-TWT Request field in QoS Characteristics element to indicate whether SCS traffic stream requires R-TWT scheduling
  When STA sets the “R-TWT Request” to 1 in a SCS request frame, it requires AP to schedule R-TWT for the SCS traffic stream. AP assigns a R-TWT membership to STA for the SCS traffic stream.
Element ID
Length
Element ID Extension
Control Info
Min SI
Max SI
Minimum Data Rate
Delay Bound
Maximum MSDU Size
Service Start Time
Mean Data Rate
Burst Size
MSDU Lifetime
MSDU Delivery Ratio
MSDU Count Exponent
Medium Time
R-TWT Request
QoS Characteristics element

## Slide 7: Proposal 2
R-TWT setup procedure contains SCS traffic information to indicate which SCS traffic streams are prioritized during the R-TWT SPs.
Proposal: Add one (or more) SCSID field in the Broadcast TWT parameter set field
R-TWT SPs are scheduled based on the QoS characteristics of the SCS traffic stream.
  R-TWT SP interval should be between min service interval and max service interval of SCS
  R-TWT SP duration should be greater or equal to medium time of SCS
  If the SCSID is UL or P2P, AP can use the R-TWT for scheduling TF or MU RTS TX
Request Type | … | Broadcast TWT Info | SCS ID
Broadcast TWT parameter set field

## Slide 8: SP1
Do you support to add R-TWT request field in QoS Characteristic element to indicate whether SCS traffic stream requires R-TWT scheduling?
  Note: this SP aims to trigger resolution of CID 4121

## Slide 9: Proposed Text Change for SP1 (1/2)
  9.4.2.316 QoS Characteristics element
  TGbe editor: Add the below paragraph to the end of the definition of the Control Info field:
  The R-TWT Request field indicates whether R-TWT should be scheduled for the SCS traffic stream under the QoS Characteristics element. The R-TWT Request field set to 1 indicates that the non-AP MLD requests the AP MLD to schedule R-TWT for the SCS traffic stream under the QoS Characteristics element and one of the APs affiliated with the AP MLD should schedule an R-TWT for the SCS traffic stream and send unsolicited TWT response frame to assign the R-TWT membership to the non-AP STA affiliated with the non-AP MLD on the same link. The R-TWT Request field set to 0 indicates that the non-AP MLD does not request the AP MLD to schedule R-TWT for the SCS traffic stream under the QoS Characteristics element. The STAs affiliated with the non-AP MLD should send TWT initiating frame to request a R-TWT membership for the SCS traffic stream if needed.
  TGbe editor: Modify Figure 9-1002al (Control Info field format) as follows:
 | B0 B1 | B2 B5 | B6 B8 | B9 B24 | B25 B28 | B29 | B30 B31
 | Direction | TID | User-Priority | Presence Bitmap of Additional Parameters | LinkID | R-TWT Request | Reserved
Bits: | 2 | 4 | 3 | 16 | 4 | 1 | 76
 | Figure 9-1002al – Control Info field format |  |  |  |  |  | 

## Slide 10: Proposed Text Change for SP1 (2/2)
  35.3.22 Multi-link SCS procedure
  TGbe editor: Add the below paragraph to the end of the subclause:
  The non-AP EHT STA affiliated with the non-AP MLD may send an SCS request that contains a QoS characteristics element whose R-TWT request field is set to 1 to its associated EHT AP affiliated with the AP MLD only if the non-AP EHT STA is an R-TWT scheduled STA and the EHT AP is an R-TWT scheduling AP (see 35.8 (Restricted TWT (r-TWT))) . If the requested SCS with R-TWT request field set to 1 in the QoS Characteristics element is accepted by the EHT AP, one of the EHT APs affiliated with the AP MLD that is an R-TWT scheduling AP (see 35.8 (Restricted TWT (r-TWT))) should schedule an R-TWT for the SCS traffic stream and send an unsolicited TWT response frame to assign the membership of the R-TWT to the corresponding non-AP STA affiliated with the non-AP MLD that is an R-TWT scheduled STA (see 35.8 (Restricted TWT (r-TWT))) on the same link before timeout. Before the timeout or receiving the unsolicited TWT response frame, all the non-AP EHT STAs affiliated with the non-AP MLD shall not initiate the R-TWT membership negotiation with the EHT APs affiliated with the AP MLD for the SCS traffic stream.

## Slide 11: SP2
Do you support to add one or more SCSID fields in the Broadcast TWT parameter set field to indicate the SCS traffic streams that are prioritized during the R-TWT SPs?
  Note: this SP aims to trigger resolution of CID 4121

## Slide 12: Proposed Text Change for SP2
  9.4.2.199 TWT element
  TGbe editor: Add the below paragraph to the end of this subclause:
  (#4121)The SCSID Valid subfield indicates if the Restricted TWT SCSID field has valid information. When the value is set to 0, it indicates that the Restricted TWT SCSID field is reserved.
  (#4121)The Restricted TWT SCSID subfields specify which SCSID(s) are identified by the TWT scheduling AP or the TWT scheduled STA as latency sensitive traffic streams in the downlink, uplink, and direct link direction.
  35.8.5 Traffic delivery
  TGbe editor: change the below paragraph in this subclause:
  An r-TWT scheduling AP or a member r-TWT scheduled STA that has initiated or participated in a frame exchange during a restricted TWT SP shall ensure QoS Data frames of r-TWT TID(s) and R-TWT SCSID(s) (#4121) to be first delivered during the r-TWT SPs. In a trigger-enabled restricted TWT SP, when scheduling the transmission of Trigger frames, the r-TWT scheduling AP shall first trigger member r-TWT scheduled STAs to facilitate them to first deliver their QoS Data frames of r-TWT UL TID(s) and R-TWT SCSID(s) of UL and direct link direction(#4121), if any.
 | B0 | B1 | B2 | B3 B7
 | DL TID Bitmap Valid | UL TID Bitmap Valid | SCSID Valid | Reserved
Bits: | 1 | 1 | 1 | 65
 | Figure 9-770b – Traffic Info Control field format |  |  | 
 | Traffic Info Control | Restricted TWT DL TID Bitmap | Restricted TWT UL TID Bitmap | Restricted TWT SCSID
Octets: | 1 | 1 | 1 | 1
 | Figure 9-770a – Restricted TWT Traffic Info field format |  |  |