## Slide 1: Technical issues 6) and 8)
Date: 2022-02-07
Authors:

## Slide 2: Abstract
During January IEEE meeting the 802.11bi task group discussed on the technical issues 6) and 8).
This submission provides updated technical issues 6) and 8) to be added to the 21/641r6 Proposed Issues document.

## Slide 3: 6) Soft/Mobile AP privacy
Issue
Soft/Mobile APs are commonly implemented on mobile devices
Soft/Mobile APs transmit exchange persistent identifiers that can be used to track the user
  APs send unprotected broadcast frames, e.g., Beacon, Probe Response
    SSID field contains explicit PII (or, at least, a static identifier over the BSS’s lifetime)
    Elements in these frames can be used for fingerprinting
  BSSID (in MAC headers) and BSS Color (in PHY preambles) of all frames are long-term static in the Soft/Mobile AP’s BSS
Status of issue
  Issue presented at IEEE 802.11bi session on 9/15/2021
Document references
  11-21-1396r1

## Slide 4: 8) PHY/RF related privacy
Issue
CSI is signaled in unprotected action frames (Beamforming reports) and might be used to facilitate inference of user behavior
  e.g., when CSI is high quality, channel perturbations caused by keystrokes might be detected
Some PHY/RF characteristics of a transmitting device can be identifiable and used to track a device
  e.g., CFO, spectral characteristics, channel estimation from a transmitting device (as opposed to channel estimation from a CSI sent in the payload)
  in general, these PHY/RF characteristics may not need to be addressed in the standard
Status of issue
  Issue presented at IEEE 802.11bi session on 9/15/2021
Document references
  11-21-1396r1