## Slide 1: TGbh proposals
Date: 2022-02-08
Authors:

## Slide 2: Abstract
This submission suggests a template that can be filled in to describe P802.11bh proposals with a one slide summary and a comparison table against use cases/features/properties. Authors’ of proposals are welcome to update the document with their proposals added. Suggestions for additional comparison/feature/property items are also welcome.
R1 – MAAD MAC scheme added

## Slide 3: Use case/feature comparison table
 | 1 | 2 | 3 | 4 | 5
4.1 (pre-assoc client steering) | no | no | yes |  | 
4.2 (ESS recognizes returning STA) | yes | yes | yes |  | 
4.3 (post-assoc arrival detection) | yes | yes | yes |  | 
4.6 (grocery store frequent shopper) | yes | yes | yes |  | 
4.15 (support/troubleshooting) | part | part | yes |  | 

## Slide 4: Property comparison table
 | 1 | 2 | 3 | 4 | 5
Requires RSN | yes | yes | yes |  | 
Uses a new frame/exchange | no | no | yes |  | 
Independent of over-the-air MAC address | yes | yes | No but OK |  | 
Identifier generated by | STA | AP | AP |  | 

## Slide 5: Proposal 1
22/158r3 – STA generated Device ID
Non-AP STA generates the identifier (e.g., a random per-ESS value or a globally unique MAC address)
Uses existing exchanges (Association Response frame or EAPOL-Key msg 4/4) to send the identity
Identity is encrypted over-the-air
Identity is sent at the beginning of ESS association before normal data connectivity is started
Defines a capability bit for AP, and an IE and a KDE for sending the identifier

## Slide 6: Proposal 2
22/187r1 – Network generated Device ID
AP generates the opaque (to the STA) identifier; might be used to store an encrypted blob that the STA copies to other APs within the ESS
Uses existing exchanges (Association Request/Response frame or EAPOL-Key msg 2/4 and 3/4) to send the identity
Identity is encrypted over-the-air
Identity is sent at the beginning of ESS association before normal data connectivity is started
Defines a capability bit for AP, and an IE and a KDE for sending the identifier

## Slide 7: Proposal 3
22/0157r1 – MAAD MAC (MAC Address Designation)
STA associates, sends MAAD Request (at any time)
AP sends MAAD Response with a MAAD MAC address (random, locally administered MAC address)
When STA returns, it uses the MAAD MAC as TA
  Identified by AP
AP sees TA (MAAD MAC) pre-association.
STA, after association, sends MAAD Request and gets a new MAAD MAC
Simple, easily implemented, no crypto requirements
AP advertises support, STA does not.
3rd party does not know in use.

## Slide 8: Proposal 4
<doc id> – <title>
Summary..

## Slide 9: Proposal 5
<doc id> – <title>
Summary..