## Slide 1: TGbh proposals
Date: 2022-02-15
Authors:

## Slide 2: Abstract
This submission suggests a template that can be filled in to describe P802.11bh proposals with a one slide summary and a comparison table against use cases/features/properties. Authors’ of proposals are welcome to update the document with their proposals added. Suggestions for additional comparison/feature/property items are also welcome.
R1 – MAAD MAC scheme added

## Slide 3: Use case/feature comparison table
 | 1 | 2 | 3 | 4 | 5 | 
4.1 (pre-assoc client steering) | no | no | yes | no | yes | 
4.2 (ESS recognizes returning STA) | yes | yes | yes | yes | yes | 
4.3 (post-assoc arrival detection) | yes | yes | yes | yes | yes | 
4.6 (grocery store frequent shopper) | yes | yes | yes | yes | yes | 
4.15 (support/troubleshooting) | part | part | yes | yes | yes | 

## Slide 4: Property comparison table
 | 1 | 2 | 3 | 4 | 5 | 
Requires RSN | yes | yes | yes | no | yes | 
Uses a new frame/exchange | no | no | yes | depends | yes | 
Independent of over-the-air MAC address | yes | yes | no | yes | yes | 
Identifier generated by | STA | AP | AP | STA | STA | 
Uses additions to HS |  |  | no |  | no | 

## Slide 5: Proposal 1
22/158r3 – STA generated Device ID
Non-AP STA generates the identifier (e.g., a random per-ESS value or a globally unique MAC address)
Uses existing exchanges (Association Response frame or EAPOL-Key msg 4/4) to send the identity
Identity is encrypted over-the-air
Identity is sent at the beginning of ESS association before normal data connectivity is started
Defines a capability bit for AP, and an IE and a KDE for sending the identifier

## Slide 6: Proposal 2
22/187r1 – Network generated Device ID
AP generates the opaque (to the STA) identifier; might be used to store an encrypted blob that the STA copies to other APs within the ESS
Uses existing exchanges (Association Request/Response frame or EAPOL-Key msg 2/4 and 3/4) to send the identity
Identity is encrypted over-the-air
Identity is sent at the beginning of ESS association before normal data connectivity is started
Defines a capability bit for AP, and an IE and a KDE for sending the identifier

## Slide 7: Proposal 3
22/0157r1 – MAAD MAC (MAC Address Designation)
AP shows support for MAAD in Extended Capabilities
  STA does not indicate support. Third party observer does not know MAAD is in use.
STA associates
At any time while associated, STA sends MAAD request
  MAD Request Action fame – does not form part of association.
AP sends MAAD response which is a 48 bit MAC address
  Locally administered
  AP stores the allocated MAAD MAC for that STA
  STA stores the allocated MAAD MAC for that AP
When STA comes back it uses the MAAD MAC Address (or not)
AP instantly recognizes the STA from TA.
  AP can identify the STA pre-association – e.g. directed probe
STA Associates using the allocated MAAD MAC as TA
At any time, STA sends MAAD request and gets a new MAAD response with a new MAC Address
  Note that The request/response DOES NOT FORM PART OF ASSOCIATION.
Repeat steps 5 - 8

## Slide 8: Proposal 4
22/117r0 – Secure Device ID Exchange concept
A method of encrypting the device identifier
Could be used in either during association or after association
Is based on the AP sharing with the STA a public key used to encrypt the device identifier
This solution does not define what the device identifier is and treats the device identifier as a string glob

## Slide 9: Proposal 5
11-21/1379r3 – ID Query Action frame
Simple Action frame pair (request/response) that allow the non-AP STA to provide an ID of its choice.
AP can query for the ID, or the non-AP STA can provide it unsolicited
ID can be provided within any security link – either after association/security setup (RSN), or pre-association with PASN
ID can be of any format. Since client is expected to “know” and trust the network, it likely knows an ID that is relevant for the network/infrastructure.

## Slide 10: Proposal 6
<doc id> – <title>
Summary..