## Slide 1: TGbh proposals
Date: 2022-02-22
Authors:

## Slide 2: Abstract
This submission suggests a template that can be filled in to describe P802.11bh proposals with a one slide summary and a comparison table against use cases/features/properties. Authors’ of proposals are welcome to update the document with their proposals added. Suggestions for additional comparison/feature/property items are also welcome.
R1 – MAAD MAC scheme added
R8 – Merged all inputs (I hope! -mah), added Straw Poll results, re-ordered proposals to match the proposals list(s) in the agenda decks (the order in which they were submitted).

## Slide 3: Use case/feature comparison table
 | 1 | 3 | 5 | 7 | 8 | 9
4.1 (pre-assoc client steering) | yes | yes | no | no | yes | no
4.2 (ESS recognizes returning STA) | yes | yes | yes | yes | yes | yes
4.3 (post-assoc arrival detection) | yes | yes | yes | yes | yes | yes
4.6 (grocery store frequent shopper) | yes | yes | yes | yes | yes | yes
4.15 (support/troubleshooting) | yes | yes | yes | part | yes | part

## Slide 4: Property comparison table
 | 1 | 3 | 5 | 7 | 8 | 9
Requires RSN | yes | yes | no | yes | yes | yes
Uses a new frame/exchange | no | yes | depends | no | yes | no
Independent of over-the-air MAC address | yes | yes | yes | yes | no | yes
Identifier generated by | STA | STA | STA | STA | AP | AP
Uses additions to HS |  | no |  |  | no | 

## Slide 5: Proposal 1
11-21/1083r0 - A Signature-based Method for Identifying STAs
Non-AP STA has a pair of private key and public key
Uses existing exchanges (Authentication frame or EAPOL-Key msg 4/4) to send the public key (i.e. the identifier)
The identifier is encrypted over-the-air if it is carried in EAPOL-Key msg 4/4
The identifier is sent at the beginning of ESS association before normal data connectivity is started
Non-AP STA can flexibly change its RMA and AP can identify the non-AP STA by using its identifier and the address signature

## Slide 6: Straw Poll #1 – Signature-based method
How much priority do you put on continuing work on the Signature-based method proposal (11-21/1083r0, 11-21/2039r0, 11-22/0054r0)?
  High
  Medium
  Low
Results: High: 2 Medium: 7 Low: 12

## Slide 7: Proposal 2
21/1585r1 – Identifiable Random MAC (IRM)
Summary:
STAs and APs indicate IRM capability
      First time association:
        STA provides key (IRMK) to AP
  AP stores STAs IRMK and STA stores IRMK for the AP
Subsequent Associations and pre-Associations:
  STA selects random “Identifiable” Random MAC address (IRMA)
  STA includes Hash in Association Request IE Hash = SHA 256/128{IRMA, IRMK}
  AP checks to see if IRMK already stored (calculates hash with stored IRMKs
  STA can provide a new IRMK to prevent spoofing
Pre-association or when associating again, or re-association, AP sees IRM capability and an IRMA. AP can calculate hash to identify STA IRMK.

## Slide 8: Straw Poll #2 – IRMA
How much priority do you put on continuing work on the IRMA proposal (11-21/1585r12, 11-21/1673r10, 11-21/1720r1, 11-21/2006r1, 11-22/0118r0, 11-22/0085r0)?
  High
  Medium
  Low
Results: High: 4 Medium: 8 Low: 8

## Slide 9: Proposal 3
11-21/1379r3 – ID Query Action frame
Simple Action frame pair (request/response) that allow the non-AP STA to provide an ID of its choice.
AP can query for the ID, or the non-AP STA can provide it unsolicited
ID can be provided within any security link – either after association/security setup (RSN), or pre-association with PASN
ID can be of any format. Since client is expected to “know” and trust the network, it likely knows an ID that is relevant for the network/infrastructure.

## Slide 10: Straw Poll #3 – Client ID Query
How much priority do you put on continuing work on the Client ID Query proposal (11-21/1378r0, 11-21/1379r3, 11-21/1853r2)?
  High
  Medium
  Low
Results: High: 6 Medium: 8 Low: 7

## Slide 11: Proposal 4
11-21/1839r1 – Transient STA ID
“TSID” generated from PTKSA, updated by knowing the previous one

## Slide 12: Straw Poll #4 – Transient STA ID
How much priority do you put on continuing work on the Transient STA ID proposal (11-21/1839r1, 11-22/0025r0)?
  High
  Medium
  Low
Results: High: 3 Medium: 4 Low: 13

## Slide 13: Proposal 5
22/117r0 – Secure Device ID Exchange concept
A method of encrypting the device identifier
Could be used in either during association or after association
Is based on the AP sharing with the STA a public key used to encrypt the device identifier
This solution does not define what the device identifier is and treats the device identifier as a string glob

## Slide 14: Straw Poll #5 – Secure Device ID
How much priority do you put on continuing work on the Secure Device ID proposal (11-22/0117r0)?
  High
  Medium
  Low
Results: High: 1 Medium: 2 Low: 15

## Slide 15: Proposal 6
11-22/0154r0 – Opaque Device ID
AP creates blob, STA returns it on future assocs
Informative Annex (?) for opaque device ID creation, that could be carried by, for example, Proposal 9

## Slide 16: Straw Poll #6 – Opaque Device ID
How much priority do you put on continuing work on the Opaque Device ID proposal (11-22/0154r0)?
  High
  Medium
  Low
Results: High: 8 Medium: 5 Low: 8

## Slide 17: Proposal 7
22/158r3 – STA generated Device ID
Non-AP STA generates the identifier (e.g., a random per-ESS value or a globally unique MAC address)
Uses existing exchanges (Association Response frame or EAPOL-Key msg 4/4) to send the identity
Identity is encrypted over-the-air
Identity is sent at the beginning of ESS association before normal data connectivity is started
Defines a capability bit for AP, and an IE and a KDE for sending the identifier

## Slide 18: Straw Poll #7 – STA Generated Device ID
How much priority do you put on continuing work on the STA Generated Device ID proposal (11-22/0158r3)?
  High
  Medium
  Low
Results: High: 7 Medium: 7 Low: 5

## Slide 19: Proposal 8
22/0157r1 – MAAD MAC (MAC Address Designation)
AP shows support for MAAD in Extended Capabilities
  STA does not indicate support. Third party observer does not know MAAD is in use.
STA associates
At any time while associated, STA sends MAAD request
  MAD Request Action fame – does not form part of association.
AP sends MAAD response which is a 48 bit MAC address
  Locally administered
  AP stores the allocated MAAD MAC for that STA
  STA stores the allocated MAAD MAC for that AP
When STA comes back it uses the MAAD MAC Address (or not)
AP instantly recognizes the STA from TA.
  AP can identify the STA pre-association – e.g. directed probe
STA Associates using the allocated MAAD MAC as TA
At any time, STA sends MAAD request and gets a new MAAD response with a new MAC Address
  Note that The request/response DOES NOT FORM PART OF ASSOCIATION.
Repeat steps 5 - 8

## Slide 20: Straw Poll #8 – MAAD
How much priority do you put on continuing work on the MAC Address Designation (MAAD) proposal (11-22/0157r3, 11-22/0301r0)?
  High
  Medium
  Low
Results: High: 8 Medium: 6 Low: 8

## Slide 21: Proposal 9
22/187r1 – Network generated Device ID
AP generates the opaque (to the STA) identifier; might be used to store an encrypted blob that the STA copies to other APs within the ESS
Uses existing exchanges (Association Request/Response frame or EAPOL-Key msg 2/4 and 3/4) to send the identity
Identity is encrypted over-the-air
Identity is sent at the beginning of ESS association before normal data connectivity is started
Defines a capability bit for AP, and an IE and a KDE for sending the identifier

## Slide 22: Straw Poll #9 – Network Generated Device ID
How much priority do you put on continuing work on the Network Generated Device ID proposal (11-22/0187r1)?
  High
  Medium
  Low
Results: High: 9 Medium: 3 Low: 9