## Slide 1: Restricted TWT SP Extension
Date: 2021-07-08
Name | Affiliations | Address | Phone | email
M. Kumail Haider | Meta |  |  | haiderkumail@fb.com
Chunyu Hu |  |  |  | 
Chitto Ghosh |  |  |  | 
Binita Gupta |  |  |  | 

## Slide 2: Abstract
For supporting latency sensitive traffic, r-TWTis defined in 11be. R-TWT membership is associated with a set of DL/UL TIDs.
If the traffic from r-TWT UL/DL TIDs is not fully delivered within the allocated r-TWT SP (e.g., if ongoing TXOP from legacy or OBSS STA(s) consume some time from start of SP), it can introduce significant delays for Latency Sensitive Traffic (LST).
In such cases, r-TWT STAs can benefit from the ability to extend the SP, if allowed, to deliver LST with priority.
In this contribution, we propose necessary signaling to support the r-TWT SP extension.
Related LB266 CIDs:
  10858, 10916, 12474, 13040, 13105, 13650

## Slide 3: Motivation
Without SP extension, if there is still latency sensitive traffic (LST) remaining at SP end, it can adversely affect latency
  If STA has policy to deliver LST only within an r-SP (and e.g., be in doze state outside for PS), it may have to wait until next SP to deliver remaining traffic, severely impacting latency
  STA could remain awake outside of SP until LST is delivered; however:
    Needs to indicate to AP it will be awake; e.g., by switching to Active Mode
    It may decide only based on its UL buffer status; STA doesn’t know if AP has more BUs in DL
    STA will not benefit from traffic prioritization if it simply stays awake instead of extending the SP
Proposal: If there is still latency sensitive traffic remaining at the AP or STA at r-TWT SP end, the SP should be allowed to be extended if the extended period does not overlap with any other scheduled SPs (TWT or others)

## Slide 4: Discussion: Using Existing Signaling (Implicit)
Indicate remaining pending buffer:
  Indication of non-empty buffer close to SP end may serve as implicit extension request
  Non-AP STA: If the non-AP STA has more packets to send, it delivers non-zero buffer info in QoS Control or BSR Control, meanwhile switch to Active mode with PM=0
    Option 1: TX of a Trigger frame by AP with MoreTF=1 serve as “Accept” indication by AP.
      Problem: MoreTF is interpreted by multiple STAs; cannot be addressed to single
    Option 2: Define reserved bit 7 of QoS Control (when sent by AP in QoS Null) as Accept indication
      Problem: Needs change in existing field
    After receiving “Accept” indication, STA remains awake until AP terminates SP explicitly or it decides to enter sleep by switching to PS with PM->1.
  AP: If AP still has more packets to the non-AP STA, it indicates non-zero buffer in ﻿AP PS Buffer State subfield in QoS Control1. This serves as “option to extend” signal
    If STA in PS, it can send QoS DATA/QoS NULL with PM=0 to switch to Active mode as acceptance of SP extension. It then remains in Active mode until AP indicates zero buffer or AP explicitly terminates the SP (using signaling defined in ﻿26.8.5 Power save operation during TWT SPs)
  Further discussion on slide 10
[1] REVme ﻿9.2.4.5.8: ﻿The AP Buffered Load subfield (of AP PS Buffer State) is used to indicate the total buffer size, rounded up to the nearest multiple of 4096 octets and expressed in units of 4096 octets, of all MSDUs and A-MSDUs buffered at the QoS AP (excluding the MSDU or A-MSDU of the present QoS Data frame).

## Slide 5: Limitations with using Existing Signaling
Problem 1: Info in current buffer status report is insufficient
  BSR Control reports buffer for AC and not TID, may create ambiguity in whether the remaining buffer is for r-TWT TID or not.
  AP PS Buffer State does not include a TID subfield
    Could use the 1 reserved bit to indicate buffer is for LST
Problem 2: Implicit indication may incur multiple rounds of signaling
  After indicating non-empty buffer, STA may have to wait for AP to trigger it without explicit “extension accepted” indication by AP. It may be awake for longer time if AP doesn’t/can’t extend SP
    Possible recommendation: AP should terminate SP if it gets non-empty buffer from STA close to SP and AP cannot extend the SP
  STA may have to switch to Active mode after receiving non-empty buffer from AP, to indicate it will be awake outside the SP. This requires additional signaling of changing PM.
Problem 3: How long is the SP extended?
  AP may want to enforce max extension time for fairness or upcoming SPs
  With implicit signaling, AP will have to explicitly terminate SP otherwise STA may remain awake, leading to higher power consumption

## Slide 6: Proposal: Signaling for SP Extension
Enable (R-)TWT STA to request/accept SP extension
Proposal: add a new HE-variant A-control field – TWT SP Command
This new A-control field could be used for both termination and extension signaling
Control ID
(4b)
Control Information (variable)
= value for <TWT SP Command>
Command
(3b)
Rsvd
(1b)
TID
(4b)
Last SN
(12b)
Command | Description | TID ¦ Last SN | Min Wake Duration
0 | Request the receiver to extend the SP until the receiver runs out of buffers of TIDs_L traffic for the transmitting STA. (Extension until explicitly terminated or zero-buffer) | Reserved. | Reserved
1 | Request the receiver to extend the SP until the receiver has received BUs of TIDs_L traffic for all SNs <= <Last SN> for <TID> and acknowledged them. |  | Reserved
2 | Request the receiver to extend the SP for Min Wake Duration (units of TU) beyond the current end time of on-going SP | Reserved | 
3 | Notify the receiver that SP has been extended (until MinWakeDuration if that field has non-zero value, otherwise extended until explicitly terminated) | Reserved | 
4-7 | Reserved |  | 
Additional Min Wake Duration
(8b)
Encoded similar to Nominal Minimum TWT Wake Duration in TWT element, units of TU

## Slide 7: Summary
Discuss the need for rTWT SP extension
Analyze how existing signaling may be used for indicating SP extension, and identify gaps
Propose a new explicit signaling mechanism for r-TWT SP extension

## Slide 8: Straw poll
SP1: Do you agree to add a new HE variant A-control field to signal TWT SP Extension (an example is described in Slide 6, but exact format/names are TBD)?

## Slide 9: Backup Slides