## Slide 1: Collaborative WLAN Sensing – Example Operations
Date: 2022-02-09
Authors:
February, 2022
Name | Affiliation | Address | Phone | Email
Sang Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | sanggook.kim@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In [1] and [2], the importance of cooperating multiple STAs in terms of performance are noted.
  In order to obtain certain performance, diversity transmissions and receptions of sensing signal among multiple STAs are crucial.
In [3 - 5], we considered the WLAN sensing in which multitude of Wi-Fi devices are involved and collaborated termed as “collaborative WLAN sensing” and possible benefits are also addressed in addition to overhead to achieve them.
  Full benefits of diversity transmissions and receptions can be achieved.
In this contribution, we illustrate one possible example operation of collaborative WLAN sensing using NDPA and NDP approach.
February, 2022

## Slide 3: Introduction (Cont’d)
The main purpose of this contribution is to show that collaborative sensing is feasible using existing approach.
Straw Poll in [5] is modified and reintroduced.
February, 2022

## Slide 4: Brief Recap
Configurations:
Sensing
Initiator (AP)
Sensing
Responder 2
Sensing
Responder 1
Example configuration: One initiator (AP) and two responders.
AP is triggering the sensing transmissions and
requesting feedbacks.
Sensing transmission and feedback may be measurement instance-based [3] when a session consists of multiple measurement instances.
Illustration is based on measurement instance-based.
Each measurement instances has sensing measurement and feedback phases.
A WLAN sensing procedure may be comprised of multiple sensing measurement instances (Motion 14).
February, 2022

## Slide 5: Brief Recap (Cont’d)
Configurations:
Sensing
Initiator (AP)
Sensing
Responder 2
Sensing
Responder 1
1st measurement instance: Transmission
Initiator transmits and two responders receive.
Available channel information: Initiator to responder 1 and
initiator to responder 2
Sensing
Initiator (AP)
Sensing
Responder 2
Sensing
Responder 1
1st measurement instance: Feedback
Two responders feedback the measurements to initiator.
Sensing
Transmitter
Sensing
Receiver
Sensing
Receiver
February, 2022

## Slide 6: Brief Recap (Cont’d)
Configurations:
Sensing
Initiator (AP)
Sensing
Responder 2
Sensing
Responder 1
Sensing
Initiator (AP)
Sensing
Responder 2
Sensing
Responder 1
2nd measurement instance: Transmission
Responder 1 transmits, initiator and responder 2 receive.
Available channel information: Responder 1 to initiator and
responder 1 to responder 2.
2nd measurement instance: Feedback
Responder 2 feedbacks channel measurement between responder 1 and itself to initiator.
Sensing
Receiver
Sensing
Transmitter
Sensing
Receiver
February, 2022

## Slide 7: Example Operation
Assumptions:
  3 STAs: AP, STA 1, and STA 2.
  Initiator: AP.
  AP is responsible for pairwise security key.
    Security key may be used for data encryption in measurement reporting.
  Measurement instances: 2
  Transmitter: AP and STA 1 in order.
  AP triggers sensing transmission.
  AP triggers a receiver(s) to transmit measurement report to AP (initiator).
  Channel reciprocity is assumed.
February, 2022

## Slide 8: Example Operation (Cont’d): Measurement Instance 1
AP
STA 1
STA 2
Sensing
NDPA
Request
Request
Sensing NDPA may carry information on transmitter and receiver(s).
In this example, AP is the transmitter of sensing transmission,
and STA 1 and STA 2 are receivers.
Each receiver is to report the measurement(s) (measurement results) to initiator (Request-Response).
AP
STA 1
STA 2
AP
STA 1
STA 2
NDP
Sensing
NDPA
NDP
Sensing
NDPA
NDP
Response
Response
Request
Request
Response
Response
February, 2022

## Slide 9: Example Operation (Cont’d): Measurement Instance 2
AP
STA 1
STA 2
Sensing NDPA may carry information on transmitter and receiver(s). In this example, STA 1 is the transmitter of sensing transmission, and AP and STA 2 are the receivers. It’s assumed that STA 2 obtained the time and Tx parameters of NDP transmission in advance.
AP
STA 1
STA 2
AP
STA 1
STA 2
AP obtains measurement
between itself and STA 1
by the transmission
from STA 1. No explicit
measurement report from STA 1
required. If required, then STA 1
transmits it after NDP transmission. Then AP (initiator) sends request to STA 2. STA 2 feedbacks the measurement between STA 1 and itself.
Sensing
NDPA
NDP
Sensing
NDPA
NDP
Sensing
NDPA
NDP
NDP
NDP
NDP
Request
Request
Response
Response
Channel information
between STA 1 and STA 2
February, 2022

## Slide 10: Considerations
Q: How does STA 2 anticipate the transmission from STA 1 and corresponding information?
A: One design approach is to use measurement setup phase. During the measurement setup phase, an initiator can decide which STA(s) will be a transmitter and which STA(s) will be a receiver per measurement instance, and its corresponding information for transmission can also be determined. This information can be delivered to all STAs being involved in the following measurement phase at the end of measurement setup phase by measurement setup ID(s). Similar approach may be considered in session setup phase. Which approach to take is TBD.
February, 2022

## Slide 11: Considerations (Cont’d)
Q: How may security context for collaborative sensing be set up?
A: One design approach is to use session setup phase. As already included in SFD, the session setup is pairwise between two STAs. After each session setup between an initiator and a STA(the secure connection is established), a group key for sensing can be delivered by using the established secure link (i.e., GTK), so that the STAs in collaborative sensing can share the key information by secured manner and use this for peer to peer transmission once they get it. This is similar to the group (multicast) key in IEEE 802.11(12.7 Keys and key distribution). Also more than one group keys may be generated to serve the seamless service regardless of STAs’ In/Out from the group. When there is a change in group members, e.g., some STAs are exited from collaborative sensing due to some reasons, another group key already generated may be used to replace the one used before exiting.
February, 2022

## Slide 12: Considerations (Cont’d)
AP
STA 1
STA 2
Pairwise secure link establishment
and session setup
1
1
Group key delivery to each STA
(by using the secure link)
2
2
3
P2P transmission
February, 2022

## Slide 13: Summary
WLAN sensing has drawn increasing attention due to its possible and potential opportunities to create many applications such as in home security, health care, enterprise, and building automation/management markets, etc.
In this contribution, we illustrated an example operation of collaborative sensing and addressed questions raised.
February, 2022

## Slide 14: References
[1] 11-19/1416r0, Wi-Fi Sensing: Cooperation and Standard. Support.
[2] 11-19/1551r1, Wi-Fi Sensing in 60GHz band: Usage models, Performance and What is need in 802.11 Standard
[3] 11-20/1533r0, Collaborative WLAN Sensing.
[4] 11-21/0145r5, Collaborative WLAN Sensing – Follow Ups.
[5] 11-21/1926r0, Collaborative WLAN Sensing – Definition and Operational Scenarios.
February, 2022

## Slide 15: SP
Do you support to include the following into SFD :
  Enhance the sensing procedure initiated by an AP to optionally allow sensing responder to sensing responder sounding.
February, 2022