## Slide 1: Partial Bandwidth NDP transmission in 11bf
Date: 2022-02-15
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Sang Kim |  |  |  | sanggook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Feb. 2022

## Slide 2: Introduction
In the sub-7 GHz band, to protect the incumbent users and to use the frequency channel efficiently, the 11ax and 11be support the PPDU transmission with preamble puncturing.
  In addition, it was also applied in the sounding protocol for HE and EHT.
Since 11bf inherits the PHY features for the sub-7GHz band, we can consider the use of NDP transmission with preamble puncturing for efficient sensing measurement.
In this contribution, we investigate the method to indicate the preamble puncturing for the NDP transmission in the sensing measurement.

## Slide 3: Support of Preamble puncturing (1/2)
The preamble puncturing is defined in 80MHz and 160MHz/80+80MHz bandwidth in 11ax
  The preamble puncturing enables the transmitter to exclude one or more non-primary 20MHz channels in the PPDU bandwidth
    No preamble transmitted in punctured channels
    RUs that overlap a punctured 20MHz channel are not allocated
Similarly to 11ax, the preamble puncturing is supported in 320MHz as well as 80MHz and 160MHz in 11be.
  The preamble puncturing is supported as a mandatory feature in 11be.
  Large size MRU is defined by considering the punctured channels in the bandwidth.
    The defined large size MRUs are as follows.
      484+242-tone MRU, 996+484-tone MRU, 996+484+242-tone MRU, 2x996+484-tone MRU, 3x996-tone MRU, and 3x996+484-tone MRU.

## Slide 4: Support of Preamble puncturing (2/2)
The information about the preamble puncturing is transmitted by using the various signaling defined in 11ax/11be.
  For example,
    The punctured channel information is conveyed through the followings
      In 11ax,
        The BW field in the HE-SIGA field
          Refer to Appendix A
      In 11be,
        The Disabled Subchannel Bitmap field in the EHT Operation element
        The Punctured Channel Indication field of the U-SIG field
          Refer to Appendix-B

## Slide 5: Preamble Punctured HE NDP
For the indication of NDP transmission with preamble puncturing and information of preamble puncturing, the HE NDPA contained the Disallowed Subchannel Bitmap subfield.
  The Disallowed Subchannel Bitmap subfield indicates the 20 MHz subchannels and the 242-tone RUs that are present in HE sounding NDPs announced by the HE NDP Announcement frame
  Also, it indicates the 242-tone RUs that are to be included in requested sounding feedback.
  A bit in the bitmap indicates whether the corresponding 20 MHz subchannel is available or not in the HE sounding NDP

## Slide 6: Preamble Punctured EHT NDP
Similarly to HE NDPA, to support the EHT NDP transmission with preamble puncturing, 11be NDPA consisted of the following.
  The Partial BW info is used to indicate the information of puncturing or request feedback
  The configuration of Partial BW info subfield
  The resolution bit indicates if the size of the sub-channel is 20MHz or 40MHz.
  Each bit in the Feedback Bitmap indicates the sub-channel corresponding to each resolution is present and requested for feedback.

## Slide 7: Punctured NDP transmission on the sensing measurement
For the NDP transmission, we can consider the use of the HE NDP or EHT NDP on the sensing measurement phase.
  Note that HE NDP or EHT NDP is transmitted in punctured Bandwidth.
And, as supporting the punctured transmission, we can utilize the channel more efficiently according to channel status in sensing measurement.
  In addition, since it gets more chances to obtain a large bandwidth when the punctured channel is assumed in sensing measurement, we can anticipate the enhanced sensing measurement results.
So, it seems very self-evident to consider punctured NDP transmission in sensing measurement.
  Also, since we consider the support of the punctured NDP transmission, we can take into account the use of the Partial bandwidth information in the sensing measurement.

## Slide 8: Partial Bandwidth feedback (1/2)
The STAs operating in the sub7 GHz band can participate in the sensing measurement and can have a different operating bandwidth when they participate in the sensing measurement.
  For example, the STA can perform the sensing measurement with the 20/40/80/160/320MHz operating bandwidth.
In addition, it should be considered that many low-end devices around us, for example, Home appliances, IoT devices can also participate in the sensing measurement.
  For the support of these devices, the 20MHz only operating STA was defined in the current 11specs.
So, it is desirable that STAs that have various bandwidth capabilities or operating bandwidth are allowed to participate in the sensing measurement.

## Slide 9: Partial Bandwidth feedback (2/2)
To support the various STAs have different operating bandwidths, we can consider the following.
  The STA that has a narrow operating BW that is smaller than the bandwidth of the NDP frame can participate in the sensing measurement.
  The partial Bandwidth feedback is requested by the sensing NDPA frame because some of the STAs participated in sensing measurement measured the part of the bandwidth of the NDP frame due to STA’s operating bandwidth.
    So, the Sensing NDPA frame should include the partial bandwidth information for the requested feedback.
  In addition, if the preamble puncturing is applied, it can be easily indicated by using the partial bandwidth information of the sensing NDPA.

## Slide 10: Summary
The preamble puncturing was applied to the current 11 specs to use the frequency channel efficiently.
  It also was applied to the channel sounding to measurement the channel status.
Also, we can consider the participation of various STAs that has different operating bandwidth in the sensing measurement.
We propose to consider the followings in 11bf.
  To do the channel measurement efficiently according to the channel status, the preamble puncturing should be considered in the sensing measurement.
  To indicate the punctured channel or the requested feedback in sensing measurement, the partial bandwidth information is included in the sensing NDPA frame.
  It is important that STAs who have smaller operating bandwidth than the NDPA frame are allowed to participate in the sensing measurement.

## Slide 11: Straw poll#1
Do you agree that 11bf SFD includes the following?
  11bf supports the Preamble puncturing in the sensing measurement.
    The preamble puncturing pattern is TBD.

## Slide 12: Straw poll#2
Do you agree that 11bf SFD includes the following?
  The sensing NDPA frame includes the partial BW info field.
    The partial BW info field indicated the punctured channel and RUs/sub-channels requested for feedback.
    The configuration of partial BW info field is TBD.
    The name of partial BW info field can be modified.

## Slide 13: Straw poll#3
Do you agree that 11bf SFD includes the following?
  11bf allows an STA that has an operating bandwidth smaller than the bandwidth of the NDP frame can participate in the sensing measurement.

## Slide 14: Appendix -A
BW subfield of HE-SIGA field

## Slide 15: Appendix-B (1/3)
Punctured channel information

## Slide 16: Appendix-B (2/3)

## Slide 17: Appendix-B (3/3)

## Slide 18: Appendix-C(1/2)

## Slide 19: Appendix-C(2/2)