## Slide 1: On Sensing by Proxy
Date: 2022-03-03
Authors:

## Slide 2: Motivation
There is little content in the subclause for SBP procedure reporting.
SBP procedure reporting is not identical to the reporting phase of TB sensing measurement instance.
  In an SBP procedure, the SBP responder initiates and coordinates sensing measurements.
This contribution discusses two issues of SBP procedure reporting which have not been addressed by TGbf.

## Slide 3: Issue 1: Frequency of Sensing Measurements
After an SBP procedure is established, the SBP responder needs to report a time series of CSI to the SBP initiator. In addition, the SBP responder needs to decide when to start each sensing measurement instance.
Question 1: How frequently should the sensing measurement results be reported to the SBP initiator?
Question 2: Who determines the frequency of sensing measurement reports?
  Option 1: the SBP initiator
  Option 2: the SBP responder
  Option 3: negotiated
Question 3: If the time instants of transmission of sensing NDP are aperiodic, should time stamps for CSI estimates be used in the reports?
Question 4: Should threshold-based reporting be used (i.e., only if the variation between consecutive CSI estimates is significant, then the current measurement results are reported to the SBP initiator)?
  Simpler than the threshold-based reporting for TB sensing measurement instance

## Slide 4: Issue 2: Consistent CSI Measurements over Time (I)
Question: Which non-AP STAs are selected by the AP to participate in sensing measurement for the SBP procedure?
Assume that two non-AP STAs participate in each sensing measurement instance.
Option 1: In each sensing measurement instance, the AP chooses two STAs from whoever responds to polling, which may lead to the following scenario:
  In sensing measurement instance #1, STA1 and STA2 are chosen. Thus CSI of STA1-AP and STA2-AP are estimated and reported.
  In sensing measurement instance #2, STA3 and STA4 are chosen. Thus CSI of STA3-AP and STA4-AP are estimated and reported.
  In sensing measurement instance #3, STA5 and STA6 are chosen. Thus CSI of STA5-AP and STA6-AP are estimated and reported.
  This time series of CSI estimate is not consistent.

## Slide 5: Issue 2: Consistent CSI Measurements over Time (II)
Option 2: In the 1st sensing measurement instance, the AP chooses two STAs from whoever responds to polling. In the subsequent sensing measurement instances, the AP attempts to poll the same two STAs as in the 1st sensing measurement instance.
However, there is no guarantee for those two STAs to be available at any of the subsequent sensing measurement instances, which may lead to the following scenario:
  In sensing measurement instance #1, STA1 and STA2 are chosen. Thus CSI of STA1-AP and STA2-AP are estimated and reported.
  In sensing measurement instance #2, neither STA1 nor STA2 responds to polling. Thus no CSI is estimated and reported.
  In sensing measurement instance #3, neither STA1 nor STA2 responds to polling. Thus no CSI is estimated and reported.
  This time series of CSI estimate does not get the job done.
Remark: Consistency is less a problem for TB sensing measurement (e.g. an AP may trigger a larger number of STAs in each TF sounding phase to reduce the probability of no common STA in any two consecutive CSI measurements).

## Slide 6: Issue 2: Consistent CSI Measurements over Time (III)
An ideal scenario of consistent CSI measurements: the same set of STAs participate in each sensing measurement instance during the SBP procedure.
  In sensing measurement instance #1, CSI of STA1-AP and STA2-AP are estimated and reported.
  In sensing measurement instance #2, CSI of STA1-AP and STA2-AP are estimated and reported.
  …
  In sensing measurement instance #n, CSI of STA1-AP and STA2-AP are estimated and reported.
Question: Should a requirement be defined for the consistency of CSI measurements over time?

## Slide 7: SP 1
Which of the following do you prefer?
  TGbf should start to develop solution(s) to address the issue of frequency of sensing measurements for SBP (described on Slide 3).
  It is too early for TGbf to address the issue.
  The issue does not need to be addressed.
  Abstain.

## Slide 8: SP 2
Which of the following do you prefer?
  TGbf should start to develop solution(s) to address the issue of consistency of sensing measurements for SBP (described on Slides 4 - 6).
  It is too early for TGbf to address the issue.
  The issue does not need to be addressed.
  Abstain.