## Slide 1: Tx Power Control and Reporting
Date: 2022-02-21
Authors:

## Slide 2: Tx Power in CSI Sensing
Effects of Tx Power on Sensing
Scales CSI (together with Rx Gain)
  Needs to be accounted when comparing consecutive sensing intervals
RF components can introduce non-linear effects
  Change in Tx Power can alter non-linear effects, create artifacts in sensing
  Due to large power imbalance between direct path and reflections, even small artifacts appear as targets

## Slide 3: Reasons for Tx Power Changes
In regular WiFi data packets, Tx Power is jointly selected with MCS
  Typically based on packet loss statistics
  Decided by transmitter based on ACK/Block ACK feedback
Sensing may have different way to set Tx Power
  Tx Power will affect Tx EVM
  TB NDP needs to avoid near/far effect of multiple sensing transmitters
Open loop Tx Power control is the worst
  Always noisy
  Small pathloss estimate fluctuations will lead to constant Tx Power adjustments

## Slide 4: Proposed Solution
Basic solution
Transmitter needs to indicate Tx Power level and/or Tx Power change
Keep Tx Power changes to a minimum
Ideal solution
Receiver indicates desired Tx Power level to transmitter (regularly)
Receiver will know Tx Power changes ahead of time
Receiver can optimize EVM relative to Rx Noise figure

## Slide 5: Implementation in Non-TB Ranging I
Initiator indicates in NDP-A
I2R NDP Tx Power
R2I NDP Target RSSI

## Slide 6: Non-TB Ranging Overview

## Slide 7: Definitions of Subfields
The I2R NDP Tx Power subfield indicates the combined average power per 20 MHz bandwidth referenced to the antenna connector, of all antennas used to transmit the following I2R NDP. The transmit power is reported with a resolution of 1 dB, with values in the range 0 to 60 representing –20 dBm to 40 dBm, respectively. Values above 60 are reserved.
The R2I NDP Target RSSI subfield indicates the preferred receive signal power, averaged over the ISTA's antenna connectors, for future R2I NDPs to be transmitted by the RSTA. The preferred receive signal power in units of dBm is TargetRSSI = –110 + FVal, where FVal is the value of the R2I NDP Target RSSI subfield, except that values above 90 indicate that the ISTA has no receive signal power preference for the R2I NDPs.

## Slide 8: Implementation in Non-TB Ranging II
Responder indicates in LMR
R2I NDP Tx Power
I2R Target RSSI

## Slide 9: Definitions of Fields
The R2I NDP Tx Power field indicates the combined average power per 20 MHz bandwidth referenced to the antenna connector, of all antennas used to transmit the preceding R2I NDP. The transmit power is reported with a resolution of 1 dB, with values in the range 0 to 60 representing –20 dBm to 40 dBm, respectively. Values above 60 are reserved.
The I2R NDP Target RSSI field indicates the preferred receive signal power, averaged over the RSTA's antenna connectors, for future I2R NDPs transmitted by the ISTA. The preferred receive signal power in units of dBm is TargetRSSI = –110 + FVal, where FVal is the value of the Target RSSI field, except that values above 90 indicate that the RSTA has no preferred receive signal power for the I2R NPDs.

## Slide 10: Possible Additions
Target RSSI does not specify a particular Tx Power
Is based on measured pathloss
Will be noisy when trying to achieve exactly
Indicate if Tx Power change/update is allowed/desired
Current field/subfields have 8 bits, 0-255
Only 0-90 are used
Suggestions
Use a reserved value to indicate “No Tx Power Change”
Use MSB or LSB to convey RSSI value + “No Tx Power Change” indication

## Slide 11: TB Ranging Overview

## Slide 12: TB Ranging
TF Sounding specifies UL Target Receive Power
Tx power depends on measured pathloss
Without I2R LMR, no way to report Tx Power fluctuations
Suggestions (drawback)
Make I2R LMR mandatory to report I2R Tx Power (overhead)
Change TF Sounding to indicate Tx Power directly (big change)
Change TF Sounding to indicate no Tx Power change